## Slide 1: Chapter 2: Review of Important Networking Concepts
Magda El Zarki
Dept. of CS
UC Irvine
elzarki@uci.edu
http://www.ics.uci.edu/~magda

## Slide 2: Networking Fundamentals
Basic Internet technologies
Basic networking strategies

## Slide 3: The Internet: A Collection of Networks

## Slide 4: The Internet: A Mesh of Links

## Slide 5: What’s the Internet: “nuts and bolts”view
millions of connected computing devices:
  hosts = end systems
  running network apps
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers:
  forward packets (chunks of data)
Home network
Institutional network
Mobile network
Global ISP
Regional ISP

## Slide 6: What’s the Internet: a service view
communication infrastructure
  enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery

## Slide 7: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: e.g., telephone network
  packet-switching: data sent thru network in discrete “chunks”

## Slide 8: Network Core: Circuit Switching
End-end resources reserved for “call”
  Resources: link bandwidth, switch capacity
  Reserved/dedicated resources: no sharing
  Guaranteed performance: your lane, fixed size
  Call setup (reservation) required
Each call gets a dedicated
lane on large highway
Call 1
Call 2

## Slide 9: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “parts”-> e.g. lanes on a highway
  dividing link bandwidth into “parts”
    frequency division - FDM
    time division - TDM
parts allocated to calls
allocated part idle if not used by owning call (no sharing)

## Slide 10: Network Core: Packet Switching
each end-to-end data stream divided into parts called packets
user A, B packets share network resources
each packet uses full link bandwidth for a short duration of time
resources used as needed – no reservations or ownership

## Slide 11: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, bandwidth shared on demand  statistical multiplexing.
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
at switch waiting
for output Link
One large highway
with only one lane

## Slide 12: Networking Concepts
Protocol Architecture
Protocol Layers
Encapsulation
IP Addressing

## Slide 13: A Data Transfer Example: Argon -> Neon
Argon
Neon
The actual path
followed by data

## Slide 14: Sending a packet from Argon to Neon
DNS: The IP address of “neon.tcpip-lab.edu” is 128.143.71.21
ARP: What is the MAC address of 128.143.137.1?
DNS: What is the IP address of “neon.tcpip-lab.edu”?
128.143.71.21 is not on my local network.
Therefore, I need to send the packet to my
default gateway with address 128.143.137.1
frame
128.143.71.21 is on my local network.
Therefore, I can send the packet directly.
ARP: The MAC address of 128.143.137.1 is 00:20:af:03:98:28
ARP: What is the MAC address of 128.143.71.21?
frame
ARP: The MAC address of 128.143.137.1 is 00:e0:f9:23:a8:20

## Slide 15: Sequence of events:
1.Web client at Argon starts an HTTP Request.
2.Argon contacts its DNS server to translate the domain name “neon.cerf.edu” into IP address “128.143.71.21” and looks up the well-known port number of the web server (port 80).
3.The HTTP client at Argon requests a TCP connection to port 80 at IP address 128.143.71.21.
4.The TCP client at Argon requests its Internet Protocol (IP) to deliver an IP datagram with the connection request to destination 128.143.71.21.
5.The IP process at Argon decides that it cannot deliver the IP datagram directly, and decides to send the IP datagram to its default gateway 128.143.137.1.
6.The Address Resolution Protocol (ARP) at Argon sends an ARP request for the MAC address of IP address 128.143.137.1.
7.The ARP request is broadcast by the Ethernet device driver at Argon to all devices on the Ethernet network.
8.The router with IP address 128.143.137.1 responds with an ARP Response to Argon which includes MAC address 00:e0:f9:23:a8:20.
9.The IP process at Argon asks its Ethernet device driver to send the IP datagram in an Ethernet frame to MAC address 00:e0:f9:23:a8:20.
10.Ethernet device driver at router with MAC address 00:e0:f9:23:a8:20 unpacks the IP datagram, and passes it to its IP process.
11.The IP process at the router decides that it can deliver the IP datagram with destination 128.143.137.21 directly (without the need of additional routers).
12.The Address Resolution Protocol (ARP) at the router sends an ARP request for the MAC address of IP address 128.143.137.21.
13.The ARP request is broadcast by the Ethernet device driver at the router to all devices on the Ethernet network.
14.Neon (which has IP address 128.143.137.21) responds with an ARP Response to the router which includes MAC address 00:20:af:03:98:28.
15.The IP process at the router asks its Ethernet device driver to send the IP datagram in an Ethernet frame to MAC address 00:20:af:03:98:28.
16.The Ethernet device driver at Neon unpacks the IP datagram contained in the Ethernet frame, and passes it to its IP process.
17.The IP process unpacks the TCP connection request contained in the IP datagram and passes it to the TCP server at port 80.
18.The TCP server at port 80 processes the TCP connection request.

## Slide 16: Communications Architecture
The complexity of the communication task is reduced by using multiple protocol layers:
    Each protocol is implemented independently
    Each protocol is responsible for a specific subtask
    Protocols are grouped in a hierarchy
A structured set of protocols is called a communications architecture or protocol suite

## Slide 17: Protocol Stack
Application
Transport
Network
Link
Physical
DHCP, DIS, DNS, FTP, HTTP, IMAP, RTP, SMTP, SSH, Telnet
TCP, UDP, RSVP
IP, ICMP, IGMP
Ethernet, 802.11, ADSL
copper wires, fibre-optic cable, radio waves

## Slide 18: Protocol Layers at work
Router

## Slide 19: Functions of the Layers
Data Link Layer:
  Service: Reliable transfer of frames over a link
  Functions: Framing (timing and synchronization)
      Media access control
      Error checking
Network Layer:
  Service: Direct packets hop by hop from source host to destination host
  Functions: Forwarding
Transport Layer:
  Service: Delivery of data between hosts end to end
  Functions: Connection establishment/termination
  error control
  flow control
Application Layer:
  Service: Application specific (delivery of email, retrieval of HTML documents, transfer of file)
  Functions: Application specific

## Slide 20: Layers in action in the Example
Send HTTP Request to neon
Establish a connection to 128.143.71.21 at port 80
Open TCP connection to 128.143.71.21 port 80
Send a datagram (which contains a connection request) to 128.143.71.21
Send IP datagram to 128.143.71.21
Send the datagram to 128.143.137.1
Send Ethernet frame to 00:e0:f9:23:a8:20
Send Ethernet frame to 00:20:af:03:98:28
Send IP data-gram to 128.143.71.21
Send the datagram to 128.143.7.21
Frame is an IP datagram
Frame is an IP datagram
IP datagram is a TCP segment for port 80

## Slide 21: Layers and Services
Service provided by TCP to HTTP:
  reliable transmission of data over a logical connection
Service provided by IP to TCP:
  unreliable transmission of IP datagrams across an IP network
Service provided by Ethernet to IP:
  transmission of a frame across an Ethernet segment
Other services:
  DNS: a network service - translation between domain names and IP addresses
    Maps fully qualified domain names (narok.cs.ucl.ac.uk) to their IP addresses (128.16.5.123)
  ARP: Translation between IP addresses and MAC addresses
    Used by IP to find the physical address of a device on a link

## Slide 22: Assignment of Protocols to Layers

## Slide 23: Encapsulation
As data is moving down the protocol stack, each protocol is adding layer-specific control information

## Slide 24: Encapsulation in our Example
Let us look in detail at the Ethernet frame between Argon and the Router, which contains the HTTP web page request to Neon, the resultant TCP segment to Neon and the IP datagram carrying the network informatio.

## Slide 25: Encapsulation: Ethernet Header

## Slide 26: Encapsulation: Ethernet Header in Hex Format

## Slide 27: Encapsulation: IP Header

## Slide 28: Encapsulation: TCP Header
Option: maximum segment size

## Slide 29: Different Protocol Views of Networking
Application (e.g. HTTP) and Transport Layer (e.g. TCP) view of the network
End to End Transmission

## Slide 30: IP View of the Network
Concatenation of Networks via Routers

## Slide 31: Ethernet view of the network
Single Link

## Slide 32: APPLICATION LAYER

## Slide 33: Application Layer Protocols
Determine what messages are sent between applications
  Messages defined by syntax and semantics
Various standards for messages, typically set by RFCs (Requests for Comments) hosted by the IETF (Internet Engineering Task Force)

## Slide 34: E.G. HTTP Request
If you connect to Host www.cs.ucl.ac.uk at Port 80
And then type in ASCII the following message:
      GET /staff/A.Steed/ HTTP/1.1
      Host: www.cs.ucl.ac.uk
And type two carriage returns
You get …

## Slide 35
HTTP/1.0 200 Document follows
MIME-Version: 1.0
Server: CERN/3.0
Date: Sun, 08 Feb 2009 15:25:18 GMT
Content-Type: text/html
Content-Length: 16150
Last-Modified: Wed, 21 Jan 2009 17:42:00 GMT
<?xml version="1.0" encoding="iso-8859-1"?>
<!DOCTYPE html PUBLIC "-//W3C//DTD XHTML 1.0 Transitional//EN" "http://www.w3.org/TR/xhtml1/DTD/xhtml1-transitional.dtd">
<html xmlns="http://www.w3.org/1999/xhtml" lang="en" dir="ltr">
<head>
<meta http-equiv="Content-Type" content="text/html; charset=iso-8859-1" />
<meta name="keywords" content="A. Steed, Anthony Steed, Department of Computer Science, University College London, virtual environments, virtual reality, computer graphics" />

## Slide 36: Application Protocol Descriptions
Often ASCII preamble, with binary assets inserted at known or marked positions
Some messages are designed to be carried over a reliable stream and are of unknown length (likely to be over TCP)
Some messages are small and it is not important if they get lost (likely to be over UDP)

## Slide 37: Common Application Protocols

## Slide 38: E.G. Domain Name Service (DNS)
Maps fully qualified domain names (narok.cs.ucl.ac.uk) to their IP addresses (128.16.5.123)
Is a network service, thus takes time
Time is variable because it’s a hierarchical search
Local DNS servers cache query responses for a fixed time (e.g. 24 hours)
If not in the cache, needs to send query up the hierarchy

## Slide 39: TRANSPORT LAYER

## Slide 40: Transport Layer Protocols
User Datagram Protocol (UDP)
  Send a message (datagram) and forget about it
  No guaranteed delivery
  No guaranteed ordering
Transmission Control Protocol (TCP)
  Guaranteed, in-order stream of data from one host to another

## Slide 41: End to End Principle
  Only the sender and receiver understand TCP or UDP (or other higher-level protocols). The routers in the Internet do not.
Port Number
IP Address
Physical Address

## Slide 42: Application Protocols and Port Numbers

## Slide 43
Destination Port = Portyyy
Transport
Network
Link
Transport
Network
Link
Application
Application
Application
Source Port = Portxxx
Destination Port = Portzzz
Multiplexing of Users and Sessions
Host IP 128.116.22.5
Host IP 128.116.48.10
Notes: Figure 3.5

## Slide 44: UDP
All hosts on the Internet have an IP address
How does the network know which application program (i.e. process) it needs to reach on a host?
And if it is a shared application, how to distinguish between different users using that same application!
Solution: add a port number to the IP address for use by end-to-end transmission only
  Port numbers are 16 bits numbers, so must lie in the range 0-65535
  Some are reserved, see later
Processes listen for incoming UDP packets
Checksum can be used to check the packet for consistency.

## Slide 45: UDP Segment Layout – Header 8bytes
Bits | 0 15 | 16 31
0-31 | Source Port | Destination Port
32-63 | Length | Checksum
64+ | Data | 
Notes: Figure 3.4

## Slide 46: UDP Checksum
The UDP header field checksum is used to check the integrity of the packet.
It provides a means of detecting errors in the UDP datagram.
The UDP checksum is calculated using a UDP-pseudo header, UDP header and the UDP data.
The UDP pseudo header contains the source IP-address, the destination IP-address, the protocol identifier (UDP in this case), and UDP datagram length taken from UDP header.
The header field checksum is optional. UDP packets with wrong checksums are discarded.
The action taken is that the packet is dropped [RFC 768]

## Slide 47: UDP Checksum Calculation
UDP Protocol

## Slide 48: TCP
In comparison to UDP, TCP offers:
  A connection-oriented services with bi-directional (full-duplex) communication
  Reliable transmission of messages in each direction
  Congestion avoidance, using variable rate transmission
  In order, and non-duplicate delivery of information
Applications place the data bytes into an outgoing buffer
The buffer is streamed in the form of segments to the receiver
At the receiver, the segments are dismantled and the data is stored in a buffer byte by byte, and pushed to the application.

## Slide 49
Transport
Network
Link
Application
Msg i – Y bytes
Msg i-2
Msg i-1
…
Data
Header
Data
Buffer
Segment: “x” data bytes
from buffer + header
Notes: Figure 3.9

## Slide 50: Layout of a TCP Segment – Header 20-40bytes
Bits | 0 15 |  |  | 16 31
0-31 | Source Port |  |  | Destination Port
32-63 | Sequence Number (SN) |  |  | 
64-95 | Acknowledgement Number (ACK) |  |  | 
96-127 | Data Offset | Not Used | Flags | Receive Window
128-159 | Checksum |  |  | Urgent Pointer
160-191 | Options (Optional) |  |  | 
160+ 192+, 224+, etc. | Data |  |  | 
Notes: Figure 3.10

## Slide 51: TCP Checksum
The TCP header field checksum is used to check the integrity of the segment.
It provides a means of detecting errors in the TCP segment.
The TCP checksum is calculated the same way as the UDP-checksum is calculated and therefore also considers a TCP-pseudo header.
The TCP pseudo header contains the source IP-address, the destination IP-address, the protocol identifier (TCP here), and TCP length (calculated from header field and data field. [RFC 793]

## Slide 52: TCP Checksum Calculation

## Slide 53: TCP is Bi-Directional
Even if, logically, data only flows one way, in order to ensure reliability, we need to send an empty “data” segment back which, by means of fields in the header, tells the transmitter which data has been successfully received (ACK)
The sender must maintain the buffered data until it receives an ACK

## Slide 54
Transport
Data
Header
Send Buffer
Receive Buffer
Next Byte Expected from other side
Received Data
Sent Data
Start Byte No.
Start Byte No. = Start Byte No. of last MSS + Last MSS (message segment size)
Sequence Number = Start Byte
Acknowledgement Number = Byte Expected
Unsent
Expected in opposite direction
MSS
Notes: Figure 3.11

## Slide 55
Header
Sequence Number = M
Transport
Send Buffer
Acknow-ledged
Last Acknowledged
= M
Next Sequence Number
= N
Unsent
To Send
Data
Transport
Receive Buffer
Received
Expected
= N
Just Received
Transport
Send Buffer
Acknowledged
Last Acknowledged
= N
Unsent
Header
Acknowledgement Number = N
An empty data packet, solely
used for ACKs in opp. direction
if no data at receiving end.
Notes: Figure 3.12

## Slide 56: TCP Reliability
How to detect if something has gone missing
  A timeout
  Returning an ACK repeatedly which indicates the buffer hasn’t grown (packets discarded because errors occurred or packets lost in network)

## Slide 57: Packet Resent on Duplicate ACK Out of order reception
Seq # = 100
Data
Host A
Host B
Seq # = 200
Data
Seq # = 300
Data
Ack # = 200
Data
Ack # = 200
Data
Seq # = 200
Data
Ack # = 400
Data
Scenario for “out of” order
data packet reception
Packet 1
Packet 1 & 3
Packet 1,3,2
Buffer
Cumulative ACK (400)
Notes: Figure 3.15

## Slide 58: Packet Resent on Duplicate ACK In order reception
Seq # = 100
Data
Host A
Host B
Seq # = 200
Data
Seq # = 300
Data
Ack # = 200
Data
Ack # = 200
Data
Seq # = 200
Data
Ack # = 300
Data
Scenario for “in” order
data packet reception
Packet 1
Packet 1
Packet 1,2
Buffer
Discard out of
order packet
Request next “in”
order packet
Notes: Figure 3.15

## Slide 59: Packet Resent on Timeout
Seq # = 100
Data
Seq # = 200
Data
Ack # = 200
Data
Seq # = 200
Data
Timeout
Host A
Host B
No new data arrival to
Trigger repeat ACK
Notes: Figure 3.16

## Slide 60: A Lost ACK Doesn’t Matter if Cumulative ACKs are used
Seq # = 100
Data
Seq # = 200
Data
Seq # = 300
Data
Ack # = 200
Data
Ack # = 400
Data
Ack # = 300
Data
Host A
Host B
Cumulative
ACK, 400 ACKs
All previous
receptions
Cumulative ACK
Notes: Figure 3.17

## Slide 61: TCP Fairness
How does TCP decide when to send packets (with UDP you call “send”)?
It sends packets with increasing frequency but when theythey are delayed or lost (detected via timeouts or repeated ACKs), it halves its rate
There are LOTS of variants of TCP
Protocols are often tested to see if they are TCP-fair, i.e. if N streams share a network link they get 1/Nth of the bandwidth
UDP is NOT fair, sends data whenever available in application buffer

## Slide 62
Time
Rate (bytes/s)
10K
20K
30K
Notes: Figure 3.22

## Slide 63: Observations
There are potentially lots of ACK packets in TCP
TCP is slow to start (connection set-up, 3way handshake), UDP is rapid start
UDP protocols need to play fair when there is congestion

## Slide 64: NETWORK LAYER

## Slide 65: Network Layer
The Internet is a collection of machines that understand IP packets
A network routes packets from one host to another through routers
Router
Route
Table
IP Packet
IP Packet

## Slide 66: IPv4
In IPv4 addresses are 32 bits in the form 128.16.13.118
They are running out of addresses.
IPv6 has larger address space, is deployed but not widely.

## Slide 67: IP: The waist of the hourglass
IP is the waist of the hourglass of the Internet protocol architecture
Multiple higher-layer protocols
Multiple lower-layer protocols
Only one protocol at the network layer.

## Slide 68: The Internet protocol
IP is the highest layer protocol which is implemented at BOTH routers and hosts

## Slide 69: IP Service
Delivery service of IP is minimal
IP provide provides an unreliable connectionless best effort service (also called:“datagram service”).
  Unreliable: IP does not make an attempt to recover lost packets
  Connectionless: Each packet (“datagram”) is handled independently. IP is not aware that packets between hosts may be sent in a logical sequence
  Best effort: IP does not make guarantees on the service (no throughput guarantee, no delay guarantee,…)
Consequences:
  Higher layer protocols have to deal with losses or with duplicate packets
  Packets may be delivered out-of-sequence

## Slide 70: IP Service
IP supports the following services:
    one-to-one (unicast)
    one-to-all (broadcast)
    one-to-several (multicast)
    one-to-anyone (anycast)
IP multicast also supports a many-to-many service.
IP multicast requires support of other protocols (IGMP, multicast routing)
unicast
broadcast
multicast
anycast

## Slide 71: IP Packet Format
Bits | 0 15 |  |  |  |  | 16 31 | 
0-31 | Version |  | Header Length |  | Type of Service | Total Length | 
32-63 | Identification |  |  |  |  | Flags | Fragment Offset
64-95 | Time to Live |  |  |  | Protocol | Header Checksum | 
96-127 | Data Offset | Not Used |  | Flags |  | Receive Window | 
128-159 | Source Address |  |  |  |  |  | 
 | Destination Address |  |  |  |  |  | 
160-191 | Options (Optional) |  |  |  |  |  | 
Bits | 0 15 |  |  | 16 31 | 
0-31 | Version | Header Length | Type of Service | Total Length | 
32-63 | Identification |  |  | Flags | Fragment Offset
64-95 | Time to Live |  | Protocol | Header Checksum | 
96-127 | Source Address |  |  |  | 
128-159 | Destination Address |  |  |  | 
160-191 | Options (Optional) |  |  |  | 
160+ 192+, 224+, etc. | Data |  |  |  | 
Notes: Figure 3.24

## Slide 72: Protocol Types
This is necessary to tell the receiver what the IP packet contains. E.G.:
  1: Internet Control Message Protocol (ICMP)
  2: Internet Group Management Protocol (IGMP)
  6: Transmission Control Protocol (TCP)
  17: User Datagram Protocol (UDP)
  89: Open Shortest Path First (OSPF)

## Slide 73: IP Addresses
Structure of an IP address
Subnetting
Classless Inter Domain Routing (CIDR)

## Slide 74: IP Addresses

## Slide 75: What is an IP Address?
An IP address is a unique global address for a network interface.
  Each device on the Internet has a network interface. Some devices may have more than one! Example: ???
  Each device belongs to a domain. A
An IP address:
  is a 32 bit long identifier
  encodes a network number (network prefix) and a host number

## Slide 76: Dotted Decimal Notation
IP addresses are written in a so-called dotted decimal notation
Each byte is identified by a decimal number in the range [0..255]:
10001111
10000000
10001001
10010000
1st Byte
= 128
2nd Byte
= 143
3rd Byte
= 137
4th Byte
= 144
128.143.137.144

## Slide 77: Network prefix and Host number
The network prefix identifies a network and the host number identifies a specific host (actually, interface on the network).
How do we know how long the network prefix is?
  The network prefix is implicitly defined (class-based addressing)
  The network prefix is indicated by a netmask/prefix.
network prefix
host number

## Slide 78: Example
Example: ellington.cs.virginia.edu
Network id is: 128.143.0.0
Host number is: 137.144
Network mask is: 255.255.0.0 or ffff0000
Prefix notation: 128.143.137.144/16
Network prefix is 16 bits long
128.143
137.144

## Slide 79: Example
Example: ellington.cs.virginia.edu
IP address is 128.143.137.144
  Is that enough??? -> No, need netmask or prefix
Using Prefix notation IP address is: 128.143.137.144/16
  Network prefix is 16 bits long
Network mask is: 255.255.0.0 or hex format: ffff0000
  -----> Network id (IP address AND Netmask) is: 128.143.0.0
  -----> Host number (IP address AND inverse Netmask) is: 137.144
128.143
137.144

## Slide 80: Subnetting
University Network
Medical
School
Library
Engineering
School
Subnetting
Problem: Organizations have multiple groups/entities within their organization which are independently managed. Each would prefer to manage their own IT facilities, i.e., own network
  Solution 1: Allocate to each entity their own IP network/domain
    Organization must own multiple IP address domains
    Expensive (each IP domain costs money) and cumbersome to manage
  Solution 2: Add another level of hierarchy to the existing IP addressing structure

## Slide 81: Basic Idea of Subnetting
Split the host number portion of an IP address into a subnet number and a (smaller) host number.
Result is a 3-layer hierarchy
Then:
    Subnets can be freely assigned within the organization
    Internally, subnets are treated as separate networks
    Subnet structure is not visible outside the organization
network prefix
host number
subnet number
network prefix
host number
extended network prefix

## Slide 82: Typical Addressing Plan for an Organization that uses subnetting
128.143.0.0/16
In this IP domain, each Ethernet segment is allocated a subnet address.
Extended Prefix
Network Prefix

## Slide 83: Subnetting Example: Argon

## Slide 84: Network without subnets

## Slide 85: Same Network with Subnets

## Slide 86: Same network with different subnetmasks

## Slide 87: Subnetting Example
An organization with 4 departments has the following IP address space: 10.2.22.0/23. As the systems manager, you are required to create subnets to accommodate the IT needs of 4 departments. The subnets have to support to 200, 61, 55, and 41 hosts respectively. What are the 4 subnet network numbers?
Solution:
  10.2.22.0/24 (256 addresses > 200)
  10.2.23.0/26 (64 addresses >61)
  10.2.23.64/26 (64 addresses > 55)
  10.2.23.128/26 (64 addresses > 41)

## Slide 88: CIDR - Classless Inter Domain Routing
Key Concept: The length of the network id (prefix) in the IP addresses is kept arbitrary: 32 - 1
Routers advertise not only reachable IP addresses, but ALSO the length of the prefix for each IP address

## Slide 89: CIDR Example
CIDR notation of a network address:
192.0.2.0/18
    "18" says that the first 18 bits are the network part of the address
    32-18 = 14 bits are available for host/device addresses
The network part is called the prefix

## Slide 90: CIDR: Prefix Size vs. Host Space
CIDR Block Prefix # of Host Addresses
/27 32 hosts
/26 64 hosts
/25 128 hosts
/24 256 hosts
/23 512 hosts
/22 1,024 hosts
/21 2,048 hosts
/20 4,096 hosts
/19 8,192 hosts
/18 16,384 hosts
/17 32,768 hosts
/16 65,536 hosts
/15 131,072 hosts
/14 262,144 hosts
/13 524,288 hosts

## Slide 91: CIDR and Address assignments
Backbone ISPs obtain large blocks of IP address space and then reallocate portions of their address blocks to their customers.
Example:
Assume that an ISP owns the address block 206.0.64.0/18, which represents 16,384 (232-18=214) IP host addresses
Suppose a client requires 800 host addresses
  512=29<800<1024=210 -> 32-10 = 22,
  Assigning a /22 block, i.e., 206.0.68.0/22 -> gives a block of 1,024 (210) IP addresses to client.

## Slide 92: Subnetting and Classless Inter Domain Routing (CIDR)
Subnetting is done by allocating some of the leading bits of the host number to indicate a subnet number.
  With subnetting, the network prefix and the subnet number make up an extended network prefix.
  The extended prefix can be expressed in terms of a subnetmask or, using CIDR notation, by adding the length of the extended subnetmask after the IP address.
For example, for Argon, the first byte of the host number (the third byte of the IP address) is used to denote the subnet number.
  128.143.0.0/16 is the IP address of the network (network prefix /16),
  128.143.137.0/24 is the IP address of the subnet,
  128.143.137.144/32 is the IP address of the host, and
  255.255.255.0 is the subnetmask of the host (or subnet prefix /24))

## Slide 93: CIDR and Routing Information
206.0.64.0/18
204.188.0.0/15
209.88.232.0/21
Internet Backbone
ISP K owns:
Company X :
206.0.68.0/22
ISP Y :
209.88.237.0/24
Organization Z1 :
209.88.237.192/26
Organization Z2 :
209.88.237.0/26

## Slide 94: CIDR and Routing Information
206.0.64.0/18
204.188.0.0/15
209.88.232.0/21
Internet Backbone
ISP K owns:
Company X :
206.0.68.0/22
ISP Y :
209.88.237.0/24
Organization Z1 :
209.88.237.192/26
Organization Z2 :
209.88.237.0/26
Backbone sends everything which matches the prefixes 206.0.64.0/18, 204.188.0.0/15, 209.88.232.0/21 to ISP K.
ISP K sends everything which matches the prefix: 206.0.68.0/22 to Company X,
209.88.237.0/24 to ISP Y
Backbone routers do not know anything about Company X, ISP Y, or Organizations Z1, Z2.
ISP K does not know about Organizations Z1, Z2.
ISP Y sends everything which matches the prefix: 209.88.237.192/26 to Organizations Z1 209.88.237.0/26 to Organizations Z2

## Slide 95: CIDR and Routing
Aggregation of routing table entries:
  128.143.0.0/16 and 128.142.0.0/16 can be represented as 128.142.0.0/15 at a router.
    ????
Longest prefix match: Routing table lookup finds the routing entry that matches the longest prefix
  Why????
E.g., What is the outgoing interface
For destination IP address:
128.143.137.0?
Prefix | Interface/outgoing link
128.143.128.0/17 | interface #1
128.128.0.0/9 | interface #2
128.0.0.0/4 | interface #5
Routing table

## Slide 96: IP Address Allocation
For a specific device interface, we either need to:
  Set IP address manually
  Get an IP address automatically using Dynamic Host Control Protocol (DHCP)
DHCP is a network service protocol, it passes out IP addresses on a subnet, based on a pool of available addresses assigned by network administrator.
Host sends a request to local DHCP for an available IP address,
Each IP address has a lease that needs to be renewed, done automatically so long as device is active

## Slide 97
Notes: Figure 3.31

## Slide 98: LINK AND PHYSICAL LAYER

## Slide 99: Link and Physical Layer
The one we all have experience with is Ethernet, either wired or wireless
Link Layer deals with communication over a single network segment which could be a point to point link, a radio channel a coax cable, or ……..
To deliver packets we need to have a mapping between the MAC address of the Ethernet adapter (physical device address) and the IP address (network address)
Use Address Resolution Protocol (ARP)

## Slide 100: Protocol Layers at work
Router

## Slide 101: Address Translation with ARP
ARP Request: Argon broadcasts an ARP request to all stations on the network: “What is the hardware address of Router with IP address 128.143.137.1?”
Arp Request:
What is MAC address
of 128.143.137.1

## Slide 102: Address Translation with ARP
ARP Reply: Router 137 responds with an ARP Reply which contains the hardware address
Arp Reply:
MAC address of 128.143.137.1
Is 00:e0:f9:23:a8:20

## Slide 103: Link Layer Frame Format
Bits | 0 15 |  |  |  |  | 16 31 | 
0-31 | Version |  | Header Length |  | Type of Service | Total Length | 
32-63 | Identification |  |  |  |  | Flags | Fragment Offset
64-95 | Time to Live |  |  |  | Protocol | Header Checksum | 
96-127 | Data Offset | Not Used |  | Flags |  | Receive Window | 
Bits | 0 15 | 16 31
0-31 | Destination MAC Address (6bytes) … | 
32-63 | … Destination MAC Address | Source MAC Address (6bytes)…
64-95 | …Source MAC Address | 
96-127 | Protocol Type | Data
… | Data | 
… | CRC Checksum | 
Notes: Figure 3.33

## Slide 104: Basic Networking Strategies

## Slide 105: Architectures
Peer to Peer
Client/Server
Hybrid

## Slide 106: Consider Just Two Machines
What is the relationship between them?
  Peers?
  Master/slave? Client/server?
  Does one have data the other one does not?

## Slide 107: Peer to Peer with Two Clients
Need to decide separation of responsibilities
  E.G. Each client simulates one player’s actions
Need to communicate sufficient information to the other that they can get both get the same state
Assumes that they have the same information other than real-time input
Can be achieved simply with sending input to each other

## Slide 108: For Example DOOM - P2P
Doom ClientA
Read
Input
Rendering
Receive
Input
Simulate
Doom ClientC
Read
Input
Rendering
Receive
Input
Simulate
Notes: Figure 11.6

## Slide 109: Master/Slave with Two Clients
One process calculates results of input
Other just waits for rendering information

## Slide 110: For Example – Thin Client/Server
Slave
Read
Input
Rendering
Master
Read
Input
Rendering
Receive
Input
Simulate
Notes: Figure 11.6

## Slide 111: More Than two Clients
The same issues exist:
  Who is responsible?
  Who has the necessary data to evolve the state?
  Who can be trusted to evolve the state?

## Slide 112: Peer to Peer Architecture
Client
Client
Client
Client
Client

## Slide 113: Client-Server Architecture
Server
Client
Client
Client
Client

## Slide 114: Implications
Peer to Peer
  Data needs to be sent multiple times on the network, links might vary in bandwidth & latency
  Clients need to manage multiple connections
Client Server
  The Server is a bottleneck
  Clients manage one connection
  Server can have privileged data, and can probably be trusted
  Latency is higher
  Synchronization is easy

## Slide 115: Hybrid Architectures
Multiple servers serving different regions
Multiple service types & service layers
Server pool

## Slide 116: Summary

## Slide 117: Which Protocol to Use?
If there is an application layer protocol that is appropriate use that!
UDP
  Good for fast changing data, and initial start update
  Good for position information
TCP
  Good for reliable data, and bulk data transfer
  Good for data assets and critical information such as score

## Slide 118: Which Protocol to Use?
Some people implement “reliability-lite” on top of UDP
Other platforms mix UDP & TCP
  There are many catches with this
Many platforms support application layer protocols such as HTTP or FTP for bulk asset transfer

## Slide 119: Conclusions
NVEs & NGs have a long history, but it is in the last 10 years that they have really taken off
The Internet is a best effort network where applications need to deal with latency & loss
There are various architectures that support NVEs & NGs