## Slide 1
Chapter 1 Introduction
Computer Networking: A Top Down Approach
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016

## Slide 2: Chapter 1: introduction
goal:
get familiar with terminology
the Internet - a brief peek/tour
overview:
what is the Internet?
What is a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
protocol layers, service models

## Slide 3: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models

## Slide 4: What is the Internet: “nuts and bolts” view
billions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
switches: forward chunks of data (packets)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
components
configurations
Notes: 4

## Slide 5: “Fun” Internet-connected devices
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress

## Slide 6
Internet “network of networks”
  interconnected networks transport data
protocols control sending, receiving of information – data exchange between end devices
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  IETF: Internet Engineering Task Force
    RFC: Request for comments
  IEEE: Inst. of Electrical & Electronic Eng.
  ITU: Intl Telecomm. Union (UN)
What is the Internet: “nuts and bolts” view
mobile network
global ISP
regional ISP
home
network
institutional
network
tying it all together and making it work

## Slide 7: What is the Internet: a service view
provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving application programs to “connect” to Internet
  service options necessary for the functionality of applications, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network
an infrastructure that:

## Slide 8: Postal Service Analogy
From address
To address
Stamp
Letter  Data
Delivery  Transmission
Postal Service Rules  Internet Rules
Envelope  Packet
Delivery Options  Trans. Options
Notes: Service Options: first class, registered, 2-day delivery….. Trans options: priority, guaranteed error free, high speed….

## Slide 9: What is a protocol?
human protocols:
asking a question
in a classroom
introductions
a courtroom
dinner conversation
network protocols:
machines rather than humans
diverse devices
type of application:
  queries
  reports/files
protocols define format, order of messages sent and received and actions taken on message transmission, receipt

## Slide 10
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What is a protocol?
Bye
Bye
Disconnect
Disconnect
Notes: Courtroom, dinner table……

## Slide 11: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
Notes: 11

## Slide 12: A closer look at network structure:
network edge:
  hosts/end devices: clients, servers, sensors, appliances….
    servers often in data centers
  end devices generate data
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home/residential
network
institutional
network

## Slide 13: Access networks and physical media
end devices connect to an edge router via
  mobile access networks
  residential access nets
  institutional access networks (school, company)
access network C/Cs
  bandwidth (capacity - bits per second)
  shared or dedicated

## Slide 14: Residential access network: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
use dedicated existing telephone line to connect to central office
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
asymmetric:
    < 2.5 Mbps upstream transmission rate
    < 24 Mbps downstream transmission rate (typically
DSL
modem
splitter
DSL access
multiplexer

## Slide 15
Residential access network: cable network
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
data, TV transmitted at different
frequencies over shared cable
distribution network
cable modem
termination system
ISP
CMTS
asymmetric:
  > 70Mbps downstream transmission rate,
  > 10 Mbps upstream transmission rate
homes share access network to cable headend
TV/ Broadcast

## Slide 16: Enterprise access network
typically used in companies, universities, etc.
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 17: Mobile access networks
shared wireless access network connects end systems to internet router via a cell tower – wide area cellular network
wireless wide area access
  provided by telco (cellular) operator
  range 10’s km
  3G, 4G: LTE
  between 1 and 10 Mbps
to Internet

## Slide 18
Home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
wireless access point:
range 100ft
802.11b/g/n (WiFi)
11, 54, 450 Mbps transmission
wireless
devices
often combined
in single box

## Slide 19: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely in space, e.g., radio, cellular

## Slide 20: Physical media: coax, fiber, twisted pair
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-1000’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps

## Slide 21: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types (range/distance, frequency spectrum, bandwidth):
terrestrial microwave
  e.g. up to 45 Mbps channels
local area (e.g., WiFi)
  54 Mbps
wide area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  long end-end delays
  geosynchronous versus low orbit

## Slide 22: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
Notes: 22

## Slide 23: The network core
mesh of interconnected switches referred to as routers
packet-switching: hosts break application-layer data into chunks and put into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
  many end devices share network links

## Slide 24: End devices: generate data
every device, e.g. host, has a “network” address
address is used to find a receiving (aka destination) device
device sending function:
  takes application data
  breaks into smaller chunks, known as packets, of length L bits
  transmits packet into access network at transmission rate R
    link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet over link
L (bits)
R (bits/sec)
=
=

## Slide 25: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet over link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link – hop by hop
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = # of hops x L/R (assuming zero propagation delay)

## Slide 26: Packet Switching: shared network resources - queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 27: Two key network-core functions
forwarding: move packets from router’s input (port) to appropriate router output (port) based on forwarding table created by routing algorithm
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
Network addr
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 28: Alternative core: circuit switching
end-end resources allocated to/reserved for “connection” between source & dest:
in diagram, each link has four circuits.
  connection gets 2nd circuit in top link and 1st circuit in right link.
no sharing:
  dedicated resources to connection
  guaranteed performance
  circuit segment idle if not used by connection
commonly used in traditional telephone networks

## Slide 29: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Circuits can be a dedicated physical link or a shared physical link with:
a dedicated frequency channel per connection
a dedicated time slot per connection
Notes: Two simple multiple access control techniques.
FDM more constrained as freq channels are set. TDM allows a provider to allocate a number of slots to a user for hiher bandwidth.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 30: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time (not continuous)
circuit-switching:
  1 Mbs/100 kbs = 10 users
packet switching:
  with 10% activity  35 users
  why? probability that more than 10 users are active at same time is less than .0004 *
packet switching allows more users to use network if user data is not a continuous stream!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Notes: Queueing theory
Data will start to pile up and you will incur delays (queueing delays)

## Slide 31
great for bursty data
  resource sharing
  simpler, no circuit setup
excessive congestion possible
  packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: how to provide circuit-like behavior for non bursty apps?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (see chapter 7)
is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching
Notes: One on one tutor
Teacher in front of a class

## Slide 32: Internet structure: network of networks
end systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
access ISPs in turn must be interconnected via provider ISPs
  so that any two hosts can send packets to each other
  referred to as regional ISPs
  they in turn need to be interconnected…. by eventually backbone ISPs referred to as Tier 1 ISPs
hierarchy of interconnections  a global Internet
resulting “network of networks” is very complex
  evolution was driven by economics and national policies
let us take a stepwise approach to describe current Internet structure

## Slide 33: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 34: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…

## Slide 35: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option1: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP

## Slide 36: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net

## Slide 37: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP

## Slide 38: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
access
net
access
net
access
net
regional net

## Slide 39: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users – overlay networks

## Slide 40: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” backbone ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g., Google): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP

## Slide 41: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 42: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
Notes: 42

## Slide 43: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (trans delay)
packets queueing (queue delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 44: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 45
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Four sources of packet delay
* Check out the Java applet for an interactive animation on trans vs. prop delay
dtrans and dprop
very different
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 45

## Slide 46: Caravan analogy
Cars (bits) “drive” at 100 km/hr –> propagation time
toll booth (transmission link) takes 12 sec to service car (transmission time per bit - bandwidth)
car ~ bit; caravan ~ packet
Q: How long until caravan (packet) is lined up before (reaches) 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec = 2mins
time for last car to travel from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 47: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr –> 100/1000=6mins
and suppose toll booth now takes one min to service a car -> 10mins for 10cars
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 6+1=7mins, first car arrives at second booth; 10-7=3 cars still at first booth  i.e., 7 cars in transit between two toll booths when first arrives.
This shows that if propagation time is low and bandwidth is low, a packet can occupy the full link for awhile.
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 48: Queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R --> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
* Check online interactive animation on queuing and loss
Need congestion control to stem flow – much like the highways

## Slide 49: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply
3 probes
3 probes
3 probes

## Slide 50: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org
Notes: The source host will send out another ICMP request with higher TTL, it tries that several times till it gets a response or a destination unreachable error. If TTL exceeds max, it stops and ends the quest.

## Slide 51: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 52: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 53: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 54: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput (for Z connections): min(Rc,Rs,R/Z)
in practice: Rc or Rs is often bottleneck link (<R) but if there are many connections sharing R, then R will be bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 55: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
Notes: 55

## Slide 56: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 57: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain or not)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Source
Destination

## Slide 58: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain?)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 59: Why layering?
dealing with complex systems:
layered structure allows breakdown of a complex system into smaller, well identified modules with explicit responsibilities/relationships to each other
  layered reference model – up/down relationships only - well defined
modularization eases maintenance/updating of system
  change of implementation of a layer’s service transparent to rest of system – internals are hidden
    e.g., change in gate procedure doesn’t affect rest of system operation, a flight is still a flight, passenger still gets to destination
    but a change in a layer’s service could impact performance of end system -> passengers may not be happy with a new gate procedure – unless reflected in their ticket purchase
layering considered harmful?
  Overlap in functionality (e.g., error control), dependency wrt specific requirements (e.g., timestamps) – not fully independent
Notes: Change runway, change airplane, change baggage carrousel….. It could impact “quality” of service, but you will still be serviced, changing implementation of layer is different than changing a service.

## Slide 60: Internet protocol stack - layers
application: supporting networked applications, process to process transfer – data stream  managed as messages
  FTP, SMTP, HTTP,…. – process id
transport: process to process message transfer  managed as segments/datagrams – port ids (216bits)
  TCP, UDP
network: routing of data segments from source to destination hop by hop  managed as datagrams – network address (4bytes x.y.z.a)
  IP
link: data transfer between neighboring network elements  managed as frames – hardware address (6octets)
  Ethernet, 802.11 (WiFi), PPP
physical: data “on the wire” managed as bits
  optical, electrical, electromagnetic…..
application
transport
network
link
physical

## Slide 61: Layers: Functionality & Services
Data Link Layer: Transmission of frames
  Functions: Framing, link/hardware addressing, media access control, error checking, flow control
Network Layer: Forwarding of packets (datagrams)
  Functions: Network addressing, hop by hop routing, header checking, loop prevention
Transport Layer: Transfer of “chunks of application data”
  Functions: Connection establishment/termination, port id, error control, flow control, congestion control
Application Layer: Application specific – display/presentation
  Functions: Synchronization/timing, error recovery

## Slide 62: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 63: IEFT Protocol Stack Example
00:20:af:03:98:28
0a:e8:b7:46:19:50
Port 80
Port 2531
128.143.137.144
128.143.71.21
00:e0:f9:23:a8:20
00:10:25:ae:a3:40

## Slide 64: Protocols in Action
64
Send HTTP Request to neon
Establish a connection to 128.143.71.21 at port 80
Open TCP connection to 128.143.71.21 port 80
Send a datagram (which contains a connection request) to 128.143.71.21
Send IP datagram to 128.143.71.21
Send the datagram to 128.143.137.1
Send IP data-gram to 128.143.71.21
Send Ethernet frame to 00:20:af:03:98:28
Send Ethernet frame to 00:e0:f9:23:a8:20
Send the datagram to 128.143.7.21
Frame is an IP datagram
Frame is an IP datagram
IP datagram is a TCP segment for port 80
IP Router
Port 2531
Port 80
0a:e8:b7:46:19:50
00:20:af:03:98:28
128.143.137.144
128.143.137.1
128.143.71.21
00:e0:f9:23:a8:20
00:10:25:ae:a3:40

## Slide 65: Encapsulation
with layering comes encapsulation
each layer adds control bits used to process the information:
  bits for addressing
  bits to provide the desired type of service to the layer above it and ultimately to the application
the packet grows in size as it drops from application to datalink at the source
the packet is stripped of bits as it travels back up the stack to the application layer

## Slide 66: IETF Encapsulation
transport layer segment
network layer datagram
link layer frame
linkh
networkh
transporth
linkt

## Slide 67: Example
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
M
Ht
Hn
M
router
switch
message
M
Ht
M
Hn
Ht
Hn
Hl
M
frame 1
Tl
Ht
Hn
Hl
M
frame 1
Tl
Ht
Hn
Hl
M
frame 2
Tl
Ht
Hn
Hl
M
frame 1
Tl
Ht
Hn
Hl
M
frame 1
Tl
X
Hx: header
Tx: trailer
M: message
X: t - transport, n - network, l - link

## Slide 68: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 68

## Slide 69: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 70: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 71
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure

## Slide 72: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 73: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
… lots more on security (throughout, Chapter 8)

## Slide 74: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 74

## Slide 75: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 76
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 77
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 78
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Internet history

## Slide 79
2005-present
~5B devices attached to Internet (2016)
  smartphones and tablets
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access
emergence of online social networks:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own networks
  bypass Internet, providing “instantaneous” access to search, video content, email, etc.
e-commerce, universities, enterprises running their services in “cloud” (e.g., Amazon EC2)
Internet history

## Slide 80: Introduction: summary
covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
you now have:
context, overview, “feel” of networking
more depth, detail to follow!

## Slide 81
Chapter 1 Additional Slides

## Slide 82
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received