## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 3 Transport Layer

## Slide 2: Chapter 3 Outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 3: Introduction –Why a Transport Layer?
provide logical communication channel between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 4: Transport vs. Network Layer
network layer: logical communication between end devices (hosts)
transport layer: logical communication between processes
  relies on network layer services
  (can) enhance network layer services
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who sort the letters from and to the kids
network-layer protocol = postal service
human analogy:

## Slide 5: Orientation
more than one transport protocol available to apps on the Internet
  TCP and UDP
not all apps use the transport layer
  directly over IP, e.g., OSPF
  interactions with ICMP

## Slide 6: Transport-layer Services
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 7: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 8: Port Numbers
UDP and TCP use port numbers to identify logical connections between processes
a globally unique address for a logical connection on a host is the tuple <IP address, port number>
the tuple identifies one end of the logical end-to-end connection to a process on a host
Multiplex on Protocol
Field in IP Header
Multiplex on to IP
Datagram

## Slide 9: Restricted Port Numbers (0 – 1023)
16 bits are reserved for port numbers in the transport layer header --> 216 = 65,535 ports per host.
well known Internet applications have reserved port numbers – know as “well known” port numbers
when connecting to one of these applications, a specific port number (taken from a list) is used.
some of the well known port numbers are listed in the table below
port #s port #s

## Slide 10: Multiplexing/demultiplexing
process
socket
use header info - port #s - to
deliver received segments
(from P3, P4) to correct process
demultiplexing at receiver:
handles data from multiple processes (P1,P2)
adds transport header (includes port #s for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 11: How demultiplexing works
host receives IP datagrams
  each datagram has:
    source IP address, destination IP address
    protocol type
  each datagram carries one transport-layer segment
    each segment has source and destination port number
host uses IP addresses, protocol field & port numbers to direct segment to appropriate process in transport layer (TCP or UDP)
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 12: Connectionless demux: example
Destination port =
6428
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
Source port = 5775
Source port = 9157
source: port: 9157, IP: A
dest: port: 6428, IP: S
source: port: 6428, IP: S
dest: port: 9157, IP A:
source: port: 6428, IP: S
dest: port: 5775, IP: B
source: port: 5775, IP: B
dest: port: 6428, IP: S
PC A
PC B
Server S

## Slide 13: Connectionless (UDP) demultiplexing
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
when creating datagram to send via UDP, an application must specify
  destination IP address
  destination port #
this is done via a socket – a small program that is used to pass information between the application and the transport layer.
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at destination

## Slide 14: Connection-oriented TCP demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
e.g., web servers have different sockets for each connecting client

## Slide 15: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP, port: A, 9157
dest IP, port: B, 80
source IP, port: B, 80
dest IP, port: A, 9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP, port: C, 5775
dest IP, port: B, 80
source IP, port: C, 9157
dest IP,port: B, 80
3 segments from 3 different connections, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B

## Slide 16: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 17: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
need reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!

## Slide 18: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
demuxing
why not use TCP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why use UDP?

## Slide 19: UDP checksum
sender:
calculate checksum over header and payload and parts of IP header (IP addresses)
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
computed checksum equals checksum field value??
  NO - error detected, drop segment
  YES - no error detected But maybe errors nonetheless? Yes!
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 20: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 21: Channel with errors and losses
Errors:
error detection - underlying channel may flip bits in a packet – packet is corrupted – extra bits (checksum) used to detect error
to recover from errors when detected
  acknowledgements (ACKs): receiver explicitly tells sender that packet received OK. No further action at sender
  negative acknowledgements (NAKs): receiver explicitly tells sender that packet had errors
    sender retransmits packet
Losses:
packets (data and ACKs and NAKs) may get lost
  header corrupted (error detection) – packet dropped
  buffer overflow in network devices – packet dropped
recovery from losses:
  how do we know a packet is lost?

## Slide 22: Recovery has a flaw!
assumption:
underlying channel can corrupt and also lose packets (data, ACKs, etc)
checksum, ACKs, retransmissions, etc., can help recover from errors and losses …
but they are not enough on their own!! -> need a recovery scheme to handle complex scenarios
receiver and sender not always aware of what is going on at other end, e.g.:
  no packets arriving at receiver – lost packets or sender done?
  sender gets no ACKs – packet lost or ACK lost?
recovery approach:
use a timer to recover from lack of “visibility”
  sender waits a reasonable amount of time (timeout) for an ACK to a transmitted packet
  retransmits if no ACK received in this time
but if a packet or an ACK) just delayed (i.e., not lost)?
  sequence numbers come into play to recover from discrepancies/duplicates at receiver

## Slide 23: Recovery to avoid flaw!
sender doesn’t know what happened at receiver!
receiver can’t tell sender what happened if nothing received
sender adds sequence number to each packet
receiver uses seq no. to ACK
sender sets a timer for a packet to detect a loss
receiver can also detect if a gap in seq no.
delays and timers can cause duplicate reception
receiver uses Seq # to detect duplicates

## Slide 24: Error Control Schemes - ARQ

## Slide 25: Simple Scheme: Stop and Wait
stop and wait
seq # 0, 1, alternate
sender sends packet with seq # 0
waits for receiver response
  Response (ACK) must have received packet seq #
sender then sends next packet with seq # 1, etc.
process repeats
Handles Recovery FLAW
does not use NAKs

## Slide 26: Stop and Wait with Seq. Nos
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 27: Stop and Wait with Seq. Nos
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)

## Slide 28: Stop-and-wait performance
first packet bit transmitted, t = 0
last packet bit transmitted, t = L / R
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
- if RTT=30 msec, one 8kbit packet every 30 msec
 ~270kbits/sec throughput over 1 Gbps link
- network protocol limits use of physical resources!

## Slide 29: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 30: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!

## Slide 31: “Sliding” Window Concept
Packet 3 ACK received
Now packet 2 (waiting in buffer)
can be sent
Window slides right when a sent packet is ACKed
Window of sent
packets – Max 7
None yet ACKed
Packets in buffer waiting
to be sent
Packets sent and
ACKS received
Seq Nos of
packets

## Slide 32: Pipelined protocols: overview
Go-back-N:
sender can have up to N unack’ed packets in pipeline (window)
receiver only sends cumulative ack
  doesn’t ack packet if there’s a gap
sender has timer for oldest unack’ed packet
  when timer expires, retransmit all unack’ed packets
Selective Repeat:
sender can have up to N unack’ed packets in pipeline
rcvr sends individual ack for each packet (each ack has a specific seq #)
sender maintains timer for each unack’ed packet
  when timer expires, retransmit only that unack’ed packet
ACKs: how to manage with losses, delays, duplicates when many pkts
Q: how do we ACK the “multiple” pkts that are in flight?
A: each pkt has a seq#.... limit # pkts in flight (window)….

## Slide 33: Go-Back-N: sender
k-bit seq # in pkt header
“window” of up to N consecutive unack’ed pkts allowed between sender and receiver
ACK(n+1): ACKs all pkts up to and including seq # n “cumulative ACK”  waiting for next packet with seq # n+1
  may receive duplicate ACKs
timer for oldest in-flight un ACK’ed pkt
timeout(n): retransmit packet n and all unACK’ed pkts in window (note window is all “unack’ed” pkts and unsent pkts)
all ACK’ed packets delivered to upper layer

## Slide 34: GBN in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait – window full)
sender
receiver
receive pkt0, send ack1
receive pkt1, send ack2
receive pkt3, discard,
(re)send ack2
rcv ack1, send pkt4
rcv ack2, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack2
receive pkt5, discard,
(re)send ack2
rcv pkt2, send ack3
rcv pkt3, send ack4
rcv pkt4, send ack5
rcv pkt5, send ack6
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
Timer reset after every received ACK for oldest
unACKed pkt.
GBN - resend all pkts
in window (here n=2 onwards)
GBN – discard all pkts that are
out of order
-GBN - only one timer
-tracks oldest pkt in queue
-updated every ACK
Timer reset
for pkt(2)
n+1=1
0+1=1
n=0

## Slide 35: Selective repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt (actually, oldest unACKed pkt, timer reset everytime a pkt is ACKed for oldest unACKed packet, all ACKed packets marked as received, and no timer reset if packets are not oldest)
sender window
  N consecutive seq #’s
  Limit on seq #s of sent, unACKed pkts (max window size is set for transmission)

## Slide 36: Selective repeat: sender, receiver windows
?
ACKs sent
Not yet received
at sender

## Slide 37: Selective repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
X
loss
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; send ack2
deliver pkt2,
pkt3, pkt4, pkt5
record ack3 arrived
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
record ack4 arrived
record ack5 arrived
Q: what happens when ack2 arrives?
SR: every pkt has a timer or oldest unACKed
window moves forward to cover all now ACKed pkts
that are in seq. Here it will be 6 as 3,4,5 all previously ACKed
Q: window at receiver?
deliver pkt0, pkt1
moves forward to 6 once
pkt 2 arrives

## Slide 38: Selective repeat: dilemma
example:
seq #’s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
Unaware it is a DUPLICATE
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can’t see sender side.
receiver behavior identical in both cases!
something’s (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
A: window size must be << than
seq # space
Q: what relationship between seq # size and window size to avoid problem in (b)?
 half or less

## Slide 39: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 40: TCP: Overview RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size

## Slide 41: Segments? Packets? Frames?
transport layer segment with header Ht
network layer datagram with header Hn
link layer frame with header and trailer
linkh
networkh
transporth
linkt
message
MSS
MTU
MSS=Max. Segment Size – Data field of Transport
MTU=Max. Trans. Unit – Data field/Payload of Link

## Slide 42: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length – Max 40)
U-URG: urgent data
A-ACK: ACK #
field valid
P-PSH: push data
R-RST, S-SYN, F-FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
cwr
ECN
this points to
control info
embedded in
data when U=1
cwr, ecn: network
congestion
bits
TCP uses a default segment size called the Maximum Segment Size – MSS --> “< MTU”
Exchanges that information with receiving side. MSS consists of data portion of TCP segment.

## Slide 43: Sequence Nos
sequence number is 32 bits long
  the range of SeqNo is
      0 <= SeqNo <= 232 -1  4.3 Gbyte
  a sequence number identifies a specific byte in the byte stream. Each byte has a sequence number
  an Initial Sequence Number (ISN) for a new connection is picked randomly at each end of the connection and is exchanged during connection establishment
0
1
1499
5500
1500
2590
2591
//
//
//
//
//
//
Segment 1 – 0 to1499 bytes
Segment 2 – 1500 to 2590 bytes
Segment 3 – 2591 to 5500 bytes

## Slide 44: Acknowledgement Nos
ACKs can be piggybacked
  a segment from A -> B can contain an acknowledgement for data sent in the B -> A direction
a hosts uses the acknowledgment field to ACK a pkt
  if a host sends an ACK# in a segment it sets the “ACK flag”
the ACK# contains the next Seq# that a receiving host is expecting to receive from the sender.
  the ACK# for a segment with Seq# 0 and data length of 1500 bytes (0-1499) is = 1500
  next byte TCP receiver is expecting is byte # 1500 (received 0-1499)
  next segment sent from sender should have Seq# = 1500 (1st byte in that segment is # 1500 in the original data byte stream)
0
1
1499
5500
1500
2590
2591
//
//
//
//
//
//
Segment 1 – 0 to 1499 bytes, Seq#0
Segment 2 – 1500 to 2590 bytes, Seq#1500
Segment 3 – 2591 to 5500 bytes, Seq#2591

## Slide 45: TCP seq. numbers, ACKs
sequence numbers:
  byte stream “number” of first byte in segment’s data
acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments?
A: TCP spec doesn’t say, - up to implementor – GBN, SACK – discard? rearrange?
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender

## Slide 46: TCP seq. numbers, ACKs
User
types
‘C’
host ACKs receipt of
byte #79 - ‘D’
host ACKs receipt of ’C’ by sending #43
and responds with character ‘D’that is Seq#79
simple scenario
Host B
Host A
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘D’
Seq=43, ACK=80
Host ACKs a previous pkt
Expecting byte #79
Sends character ‘C’ =1 byte with
Seq#42
Piggybacked ACK
Just an ACK
Why?

## Slide 47: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average over several recent measurements, not just current SampleRTT

## Slide 48: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 49: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 50: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 51: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
  pipelined segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
let’s initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 52: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments

## Slide 53: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
premature timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
ACK=120
timeout
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92
timeout

## Slide 54: TCP: retransmission scenarios
X
timeout better estimate, cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120

## Slide 55: TCP ACK generation [RFC 1122, RFC 2581]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap

## Slide 56: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs (every out of order segment will generate an ACK).
if sender receives 1+3 ACKs for same data (i.e., original + “triple or 3” duplicate ACKs),
resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
Note: “triple” duplicate ACKs, means one ACK
and 2 duplicates of that ACK

## Slide 57: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 58: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 59: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may
remove data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
-> this may cause buffer overflow
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 60: TCP flow control (FC)
receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems auto adjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value (changes value of sending window  FC window = rwnd)
guarantees receive buffer will not overflow
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver-side buffering
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
segment sent to sender from receiver
original sending window
rwnd window
if rwnd > unACKed,
then sender can send
more packets up to rwnd

## Slide 61: Example
receiver ACKs data
closes window
receiver opens window again
Delay
Persist Timer
If Delay > Persist Timer
Sender sends a small packet to feel out
receiver incase an ACK with window >0 was lost
.1K|SeqNo = 4096

## Slide 62: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 63: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters

## Slide 64: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
A: No
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 65: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 66: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 67: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB

## Slide 68: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 69: Principles of congestion control
congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
    results in retransmissions which will increase network load
  long delays (queueing in router buffers)

## Slide 70: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 71: TCP Congestion Control: Principle
Avoid losses from occurring
Q: How to do that? A: Control traffic flow!
A connection knows nothing about the network when it starts up.
  TCP has to learn what is going on: probe – RTT (delays) and losses (timeouts)
  TCP has to adapt once it gets feedback: adjust the flow

## Slide 72: TCP Basic Operation
TCP congestion control consists of two phases of traffic transmission
  Slow Start Phase – Network Probing
  Congestion Avoidance Phase – limit transmissions to avoid congestion and thus losses
TCP uses a congestion window “cwnd” at the sender side that controls the number of segments it will transmit
  cwnd is dynamic, a function of perceived network congestion
TCP reacts to network status based on events (timeouts, DUP ACKs) and adapt its behavior

## Slide 73: TCP Congestion Control Window
sender limits transmission so that:
cwnd changes with network condition – increases and decreases according to perceived congestion
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
cwnd
LastByteSent-
LastByteAcked
<
cwnd
sender sequence number space
rate
~
~
cwnd
RTT
bytes/sec
Sender uses a window called the congestion window - cwnd

## Slide 74: TCP Slow Start Phase (SS)
Slow start: probe network, grow fast
when connection begins, start with one packet.
  cwnd = 1 MSS
increase rate exponentially until first loss event or threshold (ssthresh) is reached
  increment cwnd by “one” for every ACK received (even if cumulative ACK)
initial rate is slow but ramps up exponentially fast – 1, 2, 4, 8….
Host A
one segment
RTT
Host B
time
two segments
four segments
5
6
7
8
3
4

## Slide 75: TCP Congestion Avoidance (CA)
Congestion Avoidance – linear growth
when cwnd >= ssthresh, grow more slowly
for every received ACK (including cumulative ACK)
  cwnd = cwnd + MSS*(MSS/cwnd)
  i.e., cwnd increases by 1 MSS only when ACKs received = cwnd
  e.g., if cwnd=8, sender has to receive 8 ACKs before cwnd -> 9

## Slide 76: TCP Congestion Avoidance Phase (CA)
linear growth after cwnd >= ssthresh
cwnd increments by one when all pkts in cnwd window are ACKed
e.g. cwnd = 8
cwnd +1 = 9 only when 8 ACKs received
note cwnd limits sender window, but sender window <= cwnd
Host A
Host B
time
cwnd=8
cwnd=?
How many ACKs received?
cwnd increases?
How many ACKs received?
cwnd increases?
cwnd=?
sender window = 4
sender window = 5
sender window = 6
ACK
ACK
ACK
ACK
ACK
ACK
ACK
ACK
sender window = 8
sender window = 5

## Slide 77: TCP and Network Congestion
TCP reacts to perceived congestion by switching between the two phases - SS and CA – and thus the value of “cwnd”
How does TCP perceive congestion:
  timeout – when a sent packet timer expires TCP assumes the packet is lost dues to congestion and will react accordingly
  receiving duplicate ACKs – when 3 DUPs ACKs have been received for a packet, it assumes the packet is lost
    loss due to congestion?
    loss due to error?
  reaction to these event sets TCP schemes apart

## Slide 78: TCP: Detecting & Reacting to a Loss
loss indicated by timeout: TCP goes back to slow start phase
  ssthresh = cwnd/2, cwnd set to 1 MSS again;
  back to slow start: window grows exponentially to ssthresh, then grows linearly

## Slide 79: TCP: Detecting & Reacting to DUPs
Receiving 3 duplicate ACKs (1+3 in total):
Classic TCP - TCP TAHOE:
Assumes a loss occurred due to congestion:
  fast retransmit - resends “lost” packet -> does not wait for TIMEOUT
  back to slow start: ssthresh = cwnd/2, cwnd set to 1 MSS
Popular TCP - TCP RENO:
Assumes loss may not be due to congestion as other packets are being received (triggering the DUPs)
  dup ACKs indicate network capable of delivering segments
  treats event as a loss due to error till a timeout occurs
  goes into Fast recovery Phase

## Slide 80: Fast Recovery Phase
sets:
  ssthresh=cwnd/2,
  cwnd=ssthresh+3 (for 3 dups received)
resends “lost” packet
if it receives ACK (new ACK) for resent pkt before timeout, it stays goes back to congestion avoidance (CA) phase, and sets cwnd = ssthresh
if timeout occurs for resent pkt before it receives new ACK, it goes into slow start SS, sets:
  ssthresh = cwnd
  cwnd = 1
if it receives a dup ACK again, it sets:
  cwnd = cwnd+1 and continues to send “lost” packet
  wait for new ACK of resent pkt or timeout

## Slide 81: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!
Classic TCP Tahoe

## Slide 82: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd = ssthresh
Ssthresh starts with default value
cwnd = 12
cwnd = 1
SS
CA
CA
SS
Reno in Fast Recov:
cwnd = sshthresh/2 +3 = 9
cwnd = cwnd+MSS for every DUP ACK received
retransmit lost packet, start
cwnd= 9
time x
If at time x (< Timeout) a new ACK received:
transition to CA with cwnd = sstresh
If time x = and no new ACK
Reno goes back to SS
on Timeout:
ssthresh is set to 1/2 of cwnd
cwnd = 1
both Tahoe and Reno go to SS
on 3 DUP ACKs:
Tahoe goes into SS mode
Reno goes into Fast Recovery mode

## Slide 83: TCP congestion control principle
based on the Fast Recovery mechanism:
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  Additive Increase: increase cwnd by 1 MSS every RTT (i.e., received ACK) until loss detected (3DUPs)
  Multiplicative Decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time
AIMD

## Slide 84: Which TCP???
…many TCP flavors.
TCP is implemented at edge, not in Internet so not critical to Internet operations.
Impacts edge devices/apps and their transport across the Internet.
Most popular implementation is Reno. Fast Recovery made a considerable impact on TCP performance. SACK is also enabled by default at session setup time.

## Slide 85: TCP Sender Window Size
Which window control packet transmission at the sender?
transit or inflight or (re)transmit window
flow control window
congestion window
Which one??????
TCP selects the smallest of the 3 as its “sending window”
holds back on any “new” transmissions if sender window size is reached

## Slide 86: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 87: Why is TCP fair?
two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 88: Fairness (more)
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2

## Slide 89: Explicit Congestion Notification (ECN)
network-assisted congestion control:
two end points negotiate ECN capability in setup phase with options in SYN, SYN ACK packets)
two bits in IP header (ToS field) marked by network router to indicate congestion capability (01 or 10) and congestion (11)
congestion indication carried to receiving host (packet not dropped)
receiver (seeing 11 in IP datagram) sets ECN bit on receiver-to-sender ACK segment to notify sender of congestion (unused flag fields in TCP)
sender reduces cwnd (linearly by one MSS, sometimes 1/2) and sets CRW bit (second unused flag bit) on next segment transmission
if congestion continues, this process is repeated till router buffer clears
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
ECN=01
ECN=11
IP datagram
TCP ACK segment
ECN=1
CRW=1
TCP response segment