## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 4 Network Layer:
The Data Plane

## Slide 2
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
  NAT
Chapter 4: outline

## Slide 3: Chapter 4: network layer
chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 4: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Two key network-layer functions
network-layer functions:
forwarding: move packets from router’s input to appropriate router output
routing: determine route (router by router) taken by packets from source to destination
  routing algorithms
1
2
3

## Slide 6: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 7
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact/exchange information in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 8
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 9: Router architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operttes in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 10: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forward
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
forward based on destination IP address
  goal: complete input port processing at ‘line speed’
queueing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
e.g. optical pulses
data link layer:
frame level reception
e.g., Ethernet
switch
fabric

## Slide 11: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking, as it should have been switched now but blocked red switched instead – was ahead
switch
fabric
X

## Slide 12: Output ports
buffering required if switching fabric faster than transmission rate of link
scheduling discipline chooses which, among queued datagrams, should be transmitted
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 13: Output port queueing
buffering when arrival rate via switch exceeds output line speed and/or switch fabric speed
queueing (delay) and loss due to output port buffer overflow!
at t, red and blue packets move
from input to output in a slot time
one slot time later 1st red packet starting transmission and 2nd packet arrives, 3rd will arrive next slot time - queue will fill up and overflow
switch
fabric
switch
fabric
Link BW < N link switch fabric capacity

## Slide 14: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example? – join a queue at a bus stop
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 15: Scheduling policies: priority
priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example? – airline boarding
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service
2 and 3 arrive while 1 in service
3 jumps ahead of 2 for service

## Slide 16: Scheduling policies: still more
Round Robin (RR) scheduling:
multiple classes
cyclically scan class queues, sending one complete packet from each class (if available) – fair queueing
1
2
3
4
5
5
5
2
3
1
1
3
3
4
4
arrivals
departures
packet in service
2 and 3 arrive while 1 in service
3 gets serviced ahead of 2 as each class gets one serviced each cycle
queue
(waiting area)
queue
(waiting area)
arrivals
classify
departures
link
(server)

## Slide 17: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
weighted Round Robin
each class gets weighted amount of service in each cycle, e.g., each sweep of the queues, red gets 2, green gets 1 and blue gets 3

## Slide 18
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 19: The Internet network layer
IP (Internet Protocol) is a Network Layer Protocol.
IP’s current version is Version 4 (IPv4). It is specified in RFC 891.
ICMP, IGMP are
Service/helper protocols
related to IP

## Slide 20: IP: The waist of the hourglass
IP is the waist of the hourglass of the Internet protocol architecture
multiple higher-layer protocols
multiple lower-layer protocols
pnly one protocol at the network layer.
Network Layer: Data Plane 4-20

## Slide 21
IP is the highest layer protocol which is implemented at both routers and hosts
The Internet network layer
Network Layer: Data Plane 4-21

## Slide 22: IP Service
delivery service of IP is minimal
IP provides an unreliable connectionless best effort service (also called: “datagram service”).
  unreliable: IP does not make an attempt to recover lost packets
  connectionless: Each packet (“datagram”) is handled independently. IP is not aware that packets between hosts may be sent in a logical sequence
  best effort: IP does not make guarantees on the service (no throughput guarantee, no delay guarantee,…)
consequences:
  higher layer protocols have to deal with losses or with duplicate packets
  packets may be delivered out-of-sequence
Network Layer: Data Plane 4-22

## Slide 23: IP Functions
forwarding
table
Host and router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”

## Slide 24: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version number (4bits)
header length (4bits)
(# of rows (32bits))
upper layer protocol
to deliver payload to,
e.g., TCP (6), UDP(17)
total datagram
length 216 (bytes)
ToS:“type” of service
data needs (8bits)
for
fragmentation/
reassembly
max number
remaining hops (8bits)
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit (max 40
bytes)
CRC check for
header only

## Slide 25: Maximum Transmission Unit (MTU)
maximum size of IP datagram is 65535 bytes, but the data link layer protocol generally imposes a limit that is much smaller
for example:
  Ethernet frames have a maximum payload of 1500 bytes
  IP datagrams encapsulated in Ethernet frame cannot be longer than 1500 bytes
the limit on the maximum IP datagram size, imposed by the data link protocol is called maximum transmission unit (MTU)
examples of MTU sizes:
  Ethernet: 1500 FDDI: 4352
  802.3: 1492 PPP: 296
Network Layer: Data Plane 4-25

## Slide 26: IP fragmentation, reassembly
network links have different MTU sizes -
  different link types  different MTUs
large IP datagram divided (“fragmented”) within net to fit the MTU
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 27: Where is fragmentation done?
fragmentation can be done at the sender or at intermediate routers
the same datagram can be fragmented several times.
reassembly of original datagram is only done at destination host.
Network Layer: Data Plane 4-27

## Slide 28: What’s involved in fragmentation?
the following fields in the IP header are affected:
Identification when a datagram is fragmented, the identification is the same in all fragments
Flags DF bit is set: “=1” datagram cannot be fragmented and must be discarded if MTU is too small
MF bit set: “more” bit - this datagram is part of a fragment and an additional fragment follows this one
Fragment offset 13 bits - offset of the payload of the current fragment in the original datagram/8. why?
Total length total length of the fragment
Network Layer: Data Plane 4-28

## Slide 29: IP fragmentation – multiple segments
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram = 20 + 3980
MTU = 1500 bytes
data = 1500-20 (IP header) = 1480bytes
3 fragments: 1480+1480+1020 = 3980
1480 +20 bytes in data field
offset =1480/8=185
offset =2x1480/8=370

## Slide 30: Example of fragmentation
A datagram with size 2400 bytes must be fragmented to fit in an MTU of size 1000 bytes (IP header is 20bytes)
First Fragment:
MTU = 1000
Datagram = 2400 = 20 header + 2380 payload
MTU can carry 1000 – 20 (Header) = 980 data bytes
Fragments have to be multiple of 8 in size (213).
So 980/8=122R4
Therefore carried payload will be 980-4=976 bytes
The first fragment will be 20 (Header) + 976 data = 996 in length.
Fragment offset will be 0 bytes.
Data remaining to be transmitted = 2380 – 976.
Offset of next datagram will be 976/8 = 122
Second Fragment:
Data remaining to be carried: 2380 – 976 = 1404 > 980 --> 976
The second fragment will be 20 (Header) + 976 data = 996 in length.
Fragment offset will be 122 bytes (size of 1st fragment payload).
Offset of next datagram will be 122 + 976/8 = 244
Network Layer: Data Plane 4-30
Third Fragment:
Data remaining to be transmitted = 2380 – 976 – 976 = 428
The 3rd fragment will be 20 (Header) + 428 data = 448 in length.
Fragment offset will be 244 bytes (size of 1st + 2nd fragment payloads).

## Slide 31
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 32: Internet Addressing: Introduction
Internet address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
    each interface creates a distinct/separate network
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
    interfaces may or may not be on a same network
Internet address associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 33: What is an Internet address?
an Internet address is usually referred to as the IP (Internet Procotol) address - henceforth we will refer to it as an IP address
an IP address is a unique global address for a network device interface card
an IP address uniquely identifies a network that a device/host is attached to via an interface card
a device can have multiple network interface cards, each will have an IP address identifying the network it is connected to
if the interface cards are attached to the same network (for redundancy) they will all identify the same network but will differ in some (least important) bits in the address (called “host bits”)

## Slide 34: Network number and host number
an IP address:
  is a 32 bit long identifier – 4bytes
  encodes a network part referred to as network number and a device part referred to as host number
  the network number is assigned by a global organization
  the host number is assigned locally in each network
human analogy:
  network number  ``street name, city, state, country’’
  host number  house number
if the interfaces are connected to the same network (i.,e., on the same street), they will only have a different host number (i.e., house number)
if they are connected to different networks, the network number (i.e., street name) (and possibly host number) will be different.
the size (i.e., no. of bits) of the network number is flexible
the size is indicated by a “network mask” and is called, or referred to as, the network prefix (more on that later)
network number
host number

## Slide 35: IP Dotted Decimal Notation
IP addresses are written in a dotted decimal format
each byte is identified by a decimal number in the range [0….255] – 28
Example:
10001111
10000000
10001001
10010000
1st Byte
= 128
2nd Byte
= 143
3rd Byte
= 137
4th Byte
= 144
128.143.137.144

## Slide 36: Network prefixes and network masks
the network number is identified by a network mask
a network mask consists of contiguous “1’s” for the network number part and contiguous “0’s” for the host number
e.g., an IP address 143.12.10.1 has the network mask:
11111111.11111111.00000000.00000000 -> 255.255.0.0
  Q: what is the network number for IP address 143.12.10.1?
  A: if you AND the IP address and the network mask you get the network number.
Here 143.12.10.1 AND 255.255.0.0 -> 143.12.0.0
to simplify IP address notation we use the prefix notation:
  143.12.10.1/x
  /x denotes the number of contiguous “1’s” in the network mask
for our example 255.255.0.0 -> x=16
And the IP address is represented as: 143.12.10.1/16 (instead of using mask notation)

## Slide 37: Networks, Devices and IP Addresses
IP address – 32 bits:
  network number - high order bits – assigned globally
  host number - low order bits – assigned locally
what comprises a network ?
  device addresses with same network number
what does it mean?
  devices on same network can physically reach each other without help of a router (they can directly ARP each other)
a router is required to send data from one network to another
3 interconnected networks
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
Net 223.1.3
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
Net 223.1.1
Net 223.2.1
Router

## Slide 38: How many distinct networks?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.2
223.1.7.1
223.1.8.2
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 39: Addressing in a large organization
Subnetting
usually an organization applies for one network number
organizations have multiple departments
and departments want to manage their own networks (floor/bldg/function)
  allocate a network number for each department? costly!
solution: introduce a hierarchy to the IP addressing structure only visible within the organization
Institutional Network
128.143.0.0
Medical
School
Library
Engineering
School

## Slide 40: Basic Idea of Subnetting
  subnets can be freely assigned within the organization
  internally, subnets are treated as separate networks
  subnet structure is not visible outside the organization
cannot touch the network number – assigned globally
host number assigned locally
split the host number portion of an IP address into a
  subnet number and a (smaller) host number
result is a 3-layer hierarchy
network number
host number
subnet number
network number
host number
extended network number

## Slide 41: Subnetting & extended mask/prefix
subnetting is done by allocating some of the leading bits of the host number to indicate a subnet number
  with subnetting, the network number and the subnet number make up an extended network number
  the extended number can be expressed in terms of a subnet mask (subnet prefix)
in our example 143.12.10.1/16, we will use the first byte of the host number (the third byte of the IP address) to denote the subnet number
  so subnet mask = 16+8=24
  255.255.255.0 is the subnet mask of the subnet
  143.12.10.1/24 is the IP address of the host with new prefix = 24
  143.12.10.0/24 is the subnet address the host is attached to
  note that: 143.12.0.0/16 is the still the network address (or ID) (network prefix /16) of the organization and used to by Internet to route traffic to it
  that network now has a subnet layer that is identified by 3rd byte NOT visible to outside world, only used internally.

## Slide 42: Subnets
one large network:
  223.1.0.0/16
  comprised of 3 subnets interconnected via a router
each isolated network is called a subnet
  223.1.1.0/24
  223.1.2.0/24
  223.1.3.0/24
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.2.2
223.1.3.27
223.1.2.1
223.1.0.0

## Slide 43: Advantages of Subnetting
with subnetting, IP addresses use a 3-layer hierarchy:
        network
        subnet
        host
improves efficiency of IP addresses by not consuming an entire address space for each physical network
reduces router complexity.
  since external routers do not know about subnetting, the complexity of routing tables at external routers is reduced
note: length of the subnet mask need not be identical for all subnetworks within a campus network

## Slide 44: Examples of Addressing
148.187.97.156/x = 10010100.10111011.01100001.10011100/x
X = 8 -> subnet mask? 11111111.0.0.0 -> 255.0.0.0
Netword ID? Subnet mask AND IP Address
  11111111.00000000.00000000.00000000
  AND
  10010100.10111011.01100001.10011100
  Network ID: 148.0.0.0
X = 12 -> subnet mask? 11111111.11110000.0.0 -> 255.192.0.0
Netword ID? Subnet mask AND IP Address
  11111111.11110000.00000000.00000000
  AND
  10010100.10111011.01100001.10011100
  Network ID: 148.176.0.0
X = 22 -> subnet mask? 11111111.11111111.11111100.0 -> 255.255.252.0
Netword ID? Subnet mask AND IP Address
  11111111.11111111.11111100.00000000
  AND
  10010100.10111011.01100001.10011100
  Network ID: 148.187.96.0

## Slide 45: An example of subnetting
Given: a campus network prefix of 125.36.0.0/16
create subnets that can accommodate maximum of 500 hosts each
Network ID: 125.36  cannot be touched - assigned
0.0  (subnet + host bits) –> 8 + 8 = 16 bits
500 hosts require “x” bits for host addressing
  2x > 500, what is x? 28 = 255, 29 = 512  x=9
rightmost 16 bits for this campus IP address are ‘subnet + host’ bits
  subnet address space = 16 – bits required for hosts = 16 - x
  x = 9, therefore no. of bits available for subnets = 16 – 9 = 7
7 bits left for subnetting --> 27=128 subnets
  subnet addresses: {0,1, 2, 3, 4….127}

## Slide 46: An example of subnetting
Given: a campus network prefix of 125.36.0.0/16
create 5 subnets to accommodate a minimum of 250 hosts each
Network ID:125.36  cannot be touched - assigned
0.0  (subnet + host bits) –> 8 + 8 = 16 bits
need only 5 subnets: 22=4 < 5 –> not enough, 23=8 > 5  3 bits
  subnet addresses: {0,1, 2, 3, 4, 5, 6, 7}
host address space = 16 – 3 subnet bits =13bits
  213 >250
125.36.0.0 campus network, possible subnets
  125.36.xxxxxxxx.xxxxxxxx  xxx – {0,1,2,3,4,5,6,7}
5 possible subnet prefixes:
    125.36.00100000.00000000  125.36.32.0/19
    125.36.01000000.00000000  125.36.64.0/19
    125.36.01100000.00000000  125.36.96.0/19
    125.36.10000000.00000000  125.36.128.0/19
    125.36.10100000.00000000  125.36.160.0/19

## Slide 47: Another example
Given: a campus network ID of 125.36.0.0/18
create 10 subnets for this campus network
125.36.00 (=18)  cannot be touched - assigned
000000.0  (subnet + host bits) –> 6 + 8 = 14 bits
rightmost 14 bits of this campus IP address are “subnet + host” bits
need 10 subnets  23 = 8 < 10, 24 = 16  4 bits
  subnet addresses: {0,1, 2, ……, 15}
leaves 14 - 4 = 10bits for host addresses -> 210 = 1024 addresses
125.36.0.0/18 campus network, possible subnets:
  xxxxxxxx.xxxxxxxx  xxxx – {0,1,2,3,...15}
example subnet IDs with prefix 18 + 4 = 22:
  125.36.00000000.00000000  125.36.0.0/22
  125.36.00000100.00000000  125.36.4.0/22
  125.36.00001000.00000000  125.36.8.0/22
  125.36.00001100.00000000  125.36.12.0/22
  125.36.00100100.00000000  125.36.36.0/22
  125.36.00101000.00000000 -> 125.36.40.0/22

## Slide 48: Another example
Given previous example, 2 subnets are subnetted further into 2 subnets, each to accommodate max. of 500 hosts each.
assume we used subnet IDs {0,1,…9}  {0000, 0001, 0010,…. 1001}
use subnets 0000 and 0001 to further subnet in two subnets
  125.36.00000000.00000000  125.36.0.0/22
  125.36.00000100.00000000  125.36.4.0/22
500 hosts --> 29 = 512, we need to allocate 9 bits for host address
  125.36.0000000x.xxxxxxxx
  125.36.0000010x.xxxxxxxx
two subnets need: 20 = 1 < 2, 21 = 2 -> need 1 bit
  125.36.000000Xx.xxxxxxxx
  125.36.000001Xx.xxxxxxxx
subnet ID prefixes for these new subnets will be: 22 + 1 = 23
Subnet IDs will be: subnet numbers now are: 0000xx, 0001xx
  00000, 00001  0, 2 -> 125.36.00000000.00000000/23, 125.36.00000010.00000000/23
  00010, 00011  4, 6 -> 125.36.00000100.00000000/23, 125.36.00000110.00000000/23

## Slide 49: Network without subnets
128.143.0.0/16

## Slide 50: Same network with subnets

## Slide 51: Same network with more subnetmasks
128.143.137.0/24
Subnet

## Slide 52: Final subnetting example
an organization with 4 departments has the following IP address space: 10.2.22.0/23. As the systems manager, you are required to create subnets to accommodate the IT needs of 4 departments. The subnets have to support up to 200, 71, 55, and 41 hosts respectively. What are the 4 subnet network numbers?
solution:
  10.2.22.0/24 (256 addresses > 200)
  10.2.23.0/25 (128 addresses >71)
  10.2.23.128/26 (64 addresses > 55)
  10.2.23.192/26 (64 addresses > 41)

## Slide 53: Example of a subnetting plan
Internet
Router
Subnet 2
Subnet 3
R
Subnet 4
Subnet 5
IP Network: 128.49.0.0/16
Subnet 128.49.2.0/24
Subnet 128.49.1.0/25
Subnet 128.49.1.128/25
Subnet 128.49.3.0/24
Subnet 1: 128.49.1.0/24
2 bytes available for subnetting
0=00000000
128=10000000

## Slide 54: CIDR - Classless InterDomain Routing
builds on the flexible netmask concept
restructure IP address assignments to increase efficiency
hierarchical routing aggregation to minimize route table entries
Key Concept: the length of the network id (prefix) in IP addresses is arbitrary/flexible and is defined by the network hierarchy.
  consequence:
    routers use the IP address and the length of the prefix for forwarding.
    all advertised IP addresses must include a prefix

## Slide 55: IP addressing and CIDR
subnet portion of address of arbitrary length
address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 56: CIDR Example
assume that a site requires an IP network domain that can support 1000 IP host addresses
with CIDR, the network is assigned a continuous block of:
  1024 = 210 (>1000) addresses
  with a 32-10 = 22-bit long prefix

## Slide 57: CIDR: prefix value vs. host space
CIDR Block Prefix # of Host Addresses
/27 32 hosts
/26 64 hosts
/25 128 hosts
/24 256 hosts
/23 512 hosts
/22 1,024 hosts
/21 2,048 hosts
/20 4,096 hosts
/19 8,192 hosts
/18 16,384 hosts
/17 32,768 hosts
/16 65,536 hosts
/15 131,072 hosts
/14 262,144 hosts
/13 524,288 hosts

## Slide 58: CIDR and Address assignments
Backbone ISPs obtain large blocks of IP address space and then reallocate portions of their address blocks to their customers.
example:
assume that an ISP owns the address block 206.0.64.0/18
  206.0.01000000.0/18
  32-18 = 14 represents 232-18=214 IP host addresses
suppose a client requires 800 host addresses
  512=29<800<1024=210 -> 32-10 = 22
  assign a /22 block – 206.0.01????xx.xxxxxxxx/22
  e.g., 206.0.010001xx.xxxxxxxx -> 206.0.68.0/22 allocates a block of 1,024 (210) IP addresses to client

## Slide 59: Example CIDR Address Assignment
206.0.64.0/18
204.188.0.0/15
209.88.232.0/21
Internet Backbone
ISP X owns:
Company X :
206.0.68.0/22
ISP y :
209.88.237.0/24
Organization z1 :
209.88.237.192/26
Organization z2 :
209.88.237.0/26

## Slide 60
206.0.64.0/18
204.188.0.0/15
209.88.232.0/21
Internet Backbone
ISP K owns:
Company X :
206.0.68.0/22
ISP Y :
209.88.237.0/24
Organization Z1 :
209.88.237.192/26
Organization Z2 :
209.88.237.0/26
Backbone sends everything which matches the prefixes 206.0.64.0/18, 204.188.0.0/15, 209.88.232.0/21 to ISP K.
ISP K sends everything which matches the prefix: 206.0.68.0/22 to Company X,
209.88.237.0/24 to ISP Y
Backbone routers do not know anything about Company X, ISP Y, or Organizations Z1, Z2.
ISP K does not know about Organizations Z1, Z2.
ISP Y sends everything which matches the prefix: 209.88.237.192/26 to Organizations Z1 209.88.237.0/26 to Organizations Z2
Example CIDR Address Assignment

## Slide 61: IP address: how to get one?
Q: How does a router get IP address?
hard coded by system admin
  every interface/port is assigned a unique IP address reflecting network assignment
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.0
223.1.1.0
223.1.2.0

## Slide 62
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 63: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 64: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.3.2
223.1.3.1
223.1.1.2
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network
DHCP
Server sees request and responds with an IP address

## Slide 65: DHCP: more than IP addresses
a network can have a dedicated DHCP server or you can configure the local network router to act as a DHCP server
DCHP server may not be on same subnet, in that case, the local router will forward the request to the DHCP server on behalf of the client, i.e., acting as a relay agent/proxy ( has to be enabled)
there maybe more than one DHCP server on the network.
  all, or some, will respond to a client request
  client picks one of those that responded, usually first response that comes in

## Slide 66: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
Client sends broadcast message over UDP to port 67 (reserved for DHCP) on the server, from port 68, asking for IP address
DHCP server responds offering an IP address that the client can use from pool of addresses it has available.
Note: there could be several DHCP servers that might respond to client.
Client chooses one to bind with and responds to that server accepting its IP address
Server sends final ACK binding that IP address and blocking for x secs

## Slide 67: DHCP client-server summary
DHCP server: 223.1.2.5
arriving
client
DHCP discover
DHCP offer
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
DHCPRequest
yiaddrr: 223.1.2.4
transaction ID: 655
DHCP serverID: 223.1.2.5
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
DHCPAck
yiaddrr: 223.1.2.4
transaction ID: 655
DHCP serverID: 223.1.2.5
lifetime: 3600 secs
src: 0.0.0.0, 68
dest: 255.255.255.255, 67
DHCPDiscover
yiaddr: 0.0.0.0
transaction ID: 654
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
DHCPOffer
yiaddr: 223.1.2.4
transaction ID: 654
DHCP serverID: 223.1.2.5
lifetime: 3600 secs

## Slide 68: DHCP: more than IP address
DHCP returns more than just an IP address on subnet:
  network mask (indicating network versus host portion of address)
  its address (i.e., DHCP server)
  address of first-hop (default) router for client
  name and IP address of DNS server

## Slide 69: DHCP in operation
connecting laptop needs an IP address, address of first-hop router, address of DNS server
configured to use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP (255.255.255.255), encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: ff:ff:ff:ff:ff:ff) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 70: DHCP in operation
DCP server formulates DHCP OFFER containing client’s IP address/prefix, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP OFFER, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router
A great “plug and play” service

## Slide 71: IP addressing: the last word...
Q: how does an ISP get a block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 72
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 73: IP Forwarding
IP delivery is process of getting from source to destination – moving forward hop-by-hop
translates to moving packets from a router’s input port to appropriate router output based on a table

## Slide 74: Hop-by-Hop Delivery of a datagram
IP
view at the IP layer:
  an IP network is a logical entity with a network (subnet) number
  we represent an IP network as a “cloud”
  IP delivery service is hop-by-hop across clouds of networks/subnets

## Slide 75: Under the Hood
IP
view at the data link layer layer:
  the clouds consist of collection of LANs, switched LANs, point-to-point links, that are connected by routers

## Slide 76: Input Port to Output Port delivery
destination-based forwarding: forward based only on destination IP address
using header field values
lookup output port using forwarding table in input port memory

## Slide 77: Tenets of end-to-end delivery of datagrams
The following conditions must hold so that an IP datagram can be successfully delivered
The network prefix of an IP destination address must correspond to a unique network interface – i.e., a data link layer network (LAN or point-to-point link or switched network).
Routers and hosts that have a common network prefix must be able to exchange IP datagrams using a data link protocol (e.g., Ethernet, PPP).
An IP network is formed when a data link layer network is connected to at least one other data link layer network via a router. Each router interface is an IP network.

## Slide 78: Processing of an IP datagram in IP
processing of IP datagrams is very similar on an IP router and a host
main difference: “IP forwarding” is enabled on router and disabled on host
IP forwarding enabled  if a datagram is received, but it is not for the local system, the datagram will be sent to a different system
IP forwarding disabled  if a datagram is received, but it is not for the local system, the datagram will be discarded

## Slide 79: Processing of IP datagram at a router
IP header validation
Process options in IP header
Forwarding table lookup
Decrement TTL
Perform fragmentation (if necessary)
Calculate checksum
Transmit to next hop
Send ICMP packet (if necessary)
Receive an IP datagram

## Slide 80: Forwarding tables
Each router and each host maintains a forwarding table which tells the router how to process an outgoing packet
Main columns:
    Destination address: where is the IP datagram going to?
    Next hop or interface: how to send the IP datagram?
Forwarding tables are setup so that a datagram gets closer to its destination with every hop
Destination | Next Hop
20.2.1.0/28 10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.1.0.0/16 | direct R2 R4 direct direct R1
Forwarding table of a host or router
IP datagrams can be directly delivered (“direct” via an interface) or are sent to a next hop router (R1,R2,R4).
Entry in table will give interface number (e.g., eth0) or IP address of next hop router (e.g., R2=10.2.1.5)

## Slide 81: Example of Next Hops
10.0.96.0/19
10.0.192.0/18
12.0.160.0/19
eth0
eth1
ser1
ser1
Destination | Next Hop
10.0.96.0/19 10.0.160.0/19 10.0.192.0/18 20.160.0.0/14 Default (0.0.0.0) | (direct) eth0 (direct) eth1 (direct) ser1 (R2) IPaddr (R2) IPaddr
R2
10.0.96.1/19
10.0.192.1/18
12.0.160.1/19
10.0.192.11/18
eth1
20.160.0.1/14
20.160.0.0/14

## Slide 82: Types of forwarding table entries
Network route (prefix 1-31)
  Destination addresses is a network address (e.g., 10.0.2.0/24)
  Most entries are network routes
Host route (prefix 32)
  Destination address is an interface address (e.g., 10.0.1.2/32)
  Used to specify a separate route for certain hosts
Default route (prefix 0)
  Used when no network or host route matches
  The router that is listed as the next hop of the default route is the default gateway (for Cisco: “gateway of last resort)
Loopback address (prefix 8)
  Routing table for the loopback address (127.0.0.1)
  The next hop lists the loopback (lo0) interface as outgoing interface

## Slide 83: Forwarding table lookup
When a router or host needs to transmit an IP datagram, it performs a routing table lookup
Routing table lookup: Use the IP destination address as a key to search the routing table.
Result of the lookup is the IP address of a next hop router, or the name of a network interface
Destination address | Next hop
network prefix (/1-31) or host IP address (/32) or loopback address (/8) or default route (/0) | IP address of next hop router* or Name of a network interface
* Note: A router has many IP addresses. The IP address in the routing table refers to the address of the network interface of next hop router on the same directly connected network.

## Slide 84: Typical Forwarding Table at:
Host
Destination Gateway Genmask Flags Iface
10.0.96.100 10.0.160.1 255.255.255.255 UGH eth0
10.0.32.0 10.0.192.2 255.255.224.0 UG eth1
10.0.96.0 10.0.160.1 255.255.224.0 UG eth0
10.0.64.0 10.0.192.1 255.255.224.0 UG eth1
10.0.160.0 *(direct) 255.255.224.0 U eth0
10.0.192.0 *(direct) 255.255.224.0 U eth1
127.0.0.1 * 255.0.0.0 U lo
0.0.0.0(default) 10.0.160.2 0.0.0.0 UG eth0
Router
Prefix
/32
/19
/19
/19
/19
/19
/8
/0

## Slide 85: Longest Prefix Match
Longest Prefix Match: Search for the routing table entry that has the longest prefix match with the destination IP address. WHY?
  The longer the prefix the closer you are to destination….
128.143.71.21
The longest prefix match for 128.143.71.21 is for 20 bits with entry 128.143.64.0/20
Datagram will be sent to R4
Matches but prefix 16 < 20
Search for a match on all 32 bits
Search for a match for 31 bits
…..
32. Search for a match on 0 bits
Host route  32-bit prefix match
Default route is represented as 0.0.0.0/0  0-bit prefix match

## Slide 86: Forwarding to an interface
10.2.1.0
?
?
?
Destination | Next Hop
20.2.1.0/28 10.4.2.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.1.0.0/16 | eth0 ser0 R4 eth1 eth2 R4
IP Dest:
10.2.1.55
?
20.2.1.0
10.3.1.0
10.4.2.0
10.2.1.55/28 = 20.2.1.0
10.2.1.55/24 = 10.4.2.0
10.2.1.55/24 = 10.1.2.0
10.2.1.55/24=10.2.1.0
128.5.2.1
10.4.2.2
136.4.33.2
R4
eth1
eth0
eth2
ser0
Datagram

## Slide 87: Forwarding to a Router as next hop
87
?
?
?
Destination | Next Hop
20.2.1.0/28 10.4.2.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.1.0.0/16 | eth0 ser0 R4(10.4.2.2) eth1 eth2 R4
IP Dest:
10.1.2.65
?
20.2.1.0
10.3.1.0
10.2.1.0
10.4.2.0
10.1.2.65/28 = 20.2.1.0
10.1.2.65/24 = 10.4.2.0
10.1.2.65/24 = 10.1.2.0
128.5.2.1
10.4.2.2
136.4.33.2
R4
10.1.2.0
ser0
10.4.2.2/28 = 20.2.1.0
10.4.2.2/24 = 10.4.2.0
Route to R4 – IP address 10.4.2.2
10.1.2.1
eth0
eth2
eth1
Datagram

## Slide 88: Constructing a Network Topology from a Host’s Forwarding Table
Destination | Router/ Interface
10.0.96.100/32 | 10.0.160.1 (R1)
10.0.32.0/19 | 10.0.192.2 (R2)
10.0.96.0/19 | 10.0.160.1 (R1)
10.0.64.0/19 | 10.0.192.1 (R3)
10.0.160.0/19 | eth0
10.0.192.0/19 | eth1
127.0.0.0/8 | lo
0.0.0.0 | 10.0.160.2 (R4)
10.0.160.0/19
10.0.96.0/24
10.0.192.0/19
10.32.0.0/19
10.0.64.0/24
All other destinations
R1
R2
R3
eth1
eth0
R4
10.0.96.100/24

## Slide 89: GNS3 Example

## Slide 90: Forwarding Table and Routing Cache
every router has a routing table
from routing table a forwarding table is created
once a destination has been looked up in the forwarding table, it is placed in a route cache

## Slide 91: Forwarding Table & Cache on R1

## Slide 92: Path Aggregation
20.2.0.0/16 -> 20.00000010.0.0
20.3.1.0/28 -> 20.00000011.00000001.00000000
Longest prefix match algorithm permits the aggregation of prefixes with identical next hop address to a single entry
This contributes significantly to reducing the size of routing tables of Internet routers
Destination | Next Hop
10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.0.2.0/15 | R3 direct direct R3 R2
Destination | Next Hop
10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.2.0.0/16 20.3.1.0/28 | R3 direct direct R3 R2 R2
8+7=15

## Slide 93: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (routing table)
  assume A knows R’s MAC address (ARP)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 94: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 95: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram extracted, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 96: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 97: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 98: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy

## Slide 99: Local/Adjacent and Remote devices
71-65-f7-2b-08-53
1a-2f-bb-76-09-ad
58-23-d7-fa-20-b0
0c-c4-11-6f-e3-98
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
All devices are on same “network” (137.196.7) can find and reach each other via MAC address
LAN
137.196.49.3
137.196.49.51
18-a4-d7-fa-20-c0
137.196.7.1
bd-c4-11-af-55-03
137.196.49.1
Devices on different “network” (137.196.49) can only be reached via a router using network address
f4-18-13-df-57-93

## Slide 100: Remote devices
71-65-f7-2b-08-53
1a-2f-bb-76-09-ad
58-23-d7-fa-20-b0
0c-c4-11-6f-e3-98
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
LAN
137.196.49.3
137.196.49.51
18-a4-d7-fa-20-c0
137.196.7.1
bd-c4-11-af-55-03
137.196.49.1
Devices on different “networks” (137.196.49) can only be reached via a router.
That means that the host cannot ARP for the remote host, uses a next hop router.
f4-18-13-df-57-93
ROUTER
Host 137.196.7.88 will ARP for ROUTER 137.196.7.1 interface MAC address
Then ROUTER will ARP for Host 137.196.49.3 interface MAC address

## Slide 101: What happens when a host has a larger view of network?
larger view -> means shorter prefix, i.e., does not see the local subnets
Host 223.1.1.1/16 thinks that all PCs with 223.1.0.0 prefix are in its local subnet and it will not ask the local (default router) to forward the datagram to any of the PCs
  Network view of Host:223.1.1.1/16 = 223.1.0.0
  Network view of Host for PC2:223.1.3.1/16 = 223.1.0.0
Host will directly ARP for PC2
Can PC2 respond?
NO. It is not on the same network, no one will respond to the ARP
Solution: Proxy ARP!
Host: 223.1.1.1/16
223.1.1.2/24
223.1.1.3/24
223.1.1.4/24
223.1.2.9/24
223.1.2.2/24
223.1.2.1/24
223.1.3.2/24
PC2: 223.1.3.1/24
223.1.3.27/24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Router
223.1.0.0/16

## Slide 102: Proxy ARP
Host will directly ARP for PC2
Proxy ARP - router intervenes:
  will notice that Host is looking for a remote host PC2 not on the local network
  it will respond with its own hardware address, pretending to be PC2, then forward packet
we call this Proxy ARP, the router masquerades as the remote PC (PC2) for Host
only applied when the router has a viable/routable path to both local PC (Host) and remote PC, PC2 in this case
not as popular anymore with use of DHCP (security problems)
used in smaller networks that did not use dynamic routing (i.e., system admin had to setup routing tables in hosts)
Cisco routers have it set by default
Host: 223.1.1.1/16
223.1.1.2/24
223.1.1.3/24
223.1.1.4/24
223.1.2.9/24
223.1.2.2/24
223.1.2.1/24
223.1.3.2/24
PC2: 223.1.3.1/24
223.1.3.27/24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Router
223.1.0.0/16

## Slide 103: Example: Host to PC2
Host: 223.1.1.1/16
223.1.1.2/24
223.1.1.3/24
223.1.1.4/24
223.1.2.9/24
223.1.2.2/24
223.1.2.1/24
223.1.3.2/24
PC2: 223.1.3.1/24
223.1.3.27/24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Router
Host: ARP Request for PC2
PC2
X
R: ARP Reply to Host
Host: Datagram for PC2
R: Datagram from Host for PC2
R: ARP Request for PC2
PC2: ARP Reply to R
Router R
PC2
223.1.0.0/16

## Slide 104
Non Proxy ARP – Host /24:
  Host will ARP for Router – normal operation
  Host’s ARP cache – has IP address of Router
  (223.1.1.4/24) at 00:e0:f9:23:a8:20 [ether] on eth0
Proxy ARP – Host /16:
  Host will ARP for PC2 – proxy ARP used by Router
  Host’s ARP cache – has IP address of PC2
  (223.1.3.1/16) at 00:e0:f9:23:a8:20 [ether] on eth0
ARP Cache in ARP vs Proxy ARP Example

## Slide 105: Summary: Proxy Arp
allows devices on two different IP subnetworks to share a single IP network prefix
  Source believes destination is on same IP network
must configure router to respond to ARP broadcast requests for destinations on different connected subnet
  router masquerades as destination for ARP request sent by source on a subnet
  the two devices are unaware that they are on different subnets, subnet mask indicates that they have the same network prefix.
masquerades: router responds to broadcast ARP Request from source host that arrives on one of its connected networks for a destination host that is on one of its other connected networks.

## Slide 106
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 107: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol – original (errored) datagram discarded after ICMP error message created with error info that is sent back to source
  queries: echo request/reply (used by ping), timestamps, router advertisements
network-layer “above” IP:
  ICMP msgs carried/transported in IP datagrams
ICMP Message – min 8 bytes

## Slide 108: ICMP Query message
ICMP query:
Request sent by host to a router or host
Reply sent back to querying host

## Slide 109: Example of ICMP Queries
Type/Code: Description
8/0 Echo Request
0/0 Echo Reply
13/0 Timestamp Request
14/0 Timestamp Reply
10/0 Router Solicitation
9/0 Router Advertisement
The ping command uses Echo Request/ Echo Reply

## Slide 110: Ping and ICMP
PC% ping IPAddress
PC calculates the RTT and displays on screen
PC also keeps statistics on number of transmitted requests and received replies
ICMP Echo Request
ICMP Echo Reply

## Slide 111: ICMP Router Solicitation ICMP Router Advertisement
after starting up, a router broadcasts an ICMP router solicitation.
in response, routers send an ICMP router advertisement message
also, routers periodically broadcast ICMP router advertisement
has nothing to do with routing protocols
-> this is sometimes called the Router Discovery Protocol

## Slide 112: ICMP Error message
ICMP error messages report error conditions
Typically sent when a datagram is discarded
Error message is often passed from ICMP to the application program

## Slide 113: ICMP Error message
ICMP error messages include the complete IP header and the first 8 bytes of the payload (typically: UDP, TCP)

## Slide 114: Common ICMP Error messages
Type | Code | Description | 
3 | 0–15 | Destination unreachable | Notification that an IP datagram could not be forwarded and was dropped. The code field contains an explanation.
5 | 0–3 | Redirect | Informs about an alternative route for the datagram and should result in a routing table update. The code field explains the reason for the route change.
11 | 0, 1 | Time exceeded | Sent when the TTL field has reached zero (Code 0) or when there is a timeout for the reassembly of segments (Code 1)
12 | 0, 1 | Parameter problem | Sent when the IP header is invalid (Code 0) or when an IP header option is missing (Code 1)

## Slide 115: Some subtypes of the “Destination Unreachable”
Code | Description | Reason for Sending
0 | Network Unreachable | No routing table entry is available for the destination network.
1 | Host Unreachable | Destination host should be directly reachable, but does not respond to ARP Requests.
2 | Protocol Unreachable | The protocol in the protocol field of the IP header is not supported at the destination.
3 | Port Unreachable | The transport protocol at the destination host cannot pass the datagram to an application.
4 | Fragmentation Needed and DF Bit Set | IP datagram must be fragmented, but the DF bit in the IP header is set.

## Slide 116: Example: ICMP Port Unreachable
RFC 792: If, in the destination host, the IP module cannot deliver the datagram because the indicated protocol module or process port is not active, the destination host may send a destination unreachable message to the source host.
Scenario:
Client
Request a service at a port 80
Server
No process is waiting at port 80
Port Unreachable

## Slide 117: Traceroute and ICMP
source sends series of UDP segments (56bytes) to destination
  first set (3) has TTL =1
  second set has TTL=2, etc.
  … and finally unlikely (i.e., nonexistent) port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends to source ICMP message (type 11, code 0 -> TTL = 0)
  ICMP message includes name of router & IP address (of incoming port)
when ICMP message arrives at source, it records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 118: Example of Traceroute output
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org
Notes: The source host will send out another ICMP request with higher TTL, it tries that several times till it gets a response or a destination unreachable error. If TTL exceeds max, it stops and ends the quest.

## Slide 119: Routing Error: table manipulations with ICMP
when a router detects that an IP datagram should have gone to a different router, the router (here R2)
    forwards the IP datagram to the correct router
    sends an ICMP redirect message to the host
host uses ICMP message to update its forwarding cache not its forwarding table!!!
R1
Routing Cache

## Slide 120
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
Chapter 4: outline

## Slide 121: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 122: IPv6 datagram format
priority: identify priority among datagrams in flow
flow label: identify datagrams in same “flow” (concept of“flow” not well defined)
next header: identify upper layer protocol for data
checksum, fragmentation: removed to reduce processing time at routers
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 123: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 124: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 125: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 126: IPv6: adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why?

## Slide 127
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  DHCP
  IPv4 forwarding
  ICMP
  IPv6
  NAT
Chapter 4: outline

## Slide 128: Network Address Translation - NAT
Translation from internal, hidden, IP addresses to valid external Internet addresses.
Saves costs
Increases the number of available addresses
Secure – devices behind a firewall

## Slide 129: Private Network
Private IP network is an IP network that is not accessible to the Internet. It is closed and self contained.
IP addresses in a private network can be assigned arbitrarily.
  Not registered and not guaranteed to be globally unique
Generally, private networks use addresses from the following experimental address ranges (non-routable addresses):
  10.0.0.0 – 10.255.255.255
  172.16.0.0 – 172.31.255.255
  192.168.0.0 – 192.168.255.255
Private networks can be connected to the Internet via a router but the devices are not directly accessible from the outside.

## Slide 130: Private Networks and Addresses

## Slide 131: Network Address Translation (NAT)
NAT is a method that enables hosts on private networks to communicate with hosts on the Internet
NAT is run on routers that connect private networks to the public Internet, to replace the IP address and (possibly) port# of an IP packet with another IP address-port pair at the boundary of a private network

## Slide 132: Basic operation of NAT
NAT device has address translation table
one to one address translation
Router IP address: 128.143.71.1

## Slide 133: Pooling of IP addresses
Scenario: Corporate network has many hosts but only a small number of public IP addresses
NAT solution:
  Corporate network is managed with a private address space
  NAT device, located at the boundary between the corporate network and the public Internet, manages a pool of public IP addresses
  When a host from the corporate network sends an IP datagram to a host in the public Internet, the NAT device picks a public IP address from the address pool, and binds this address to the private address of the host

## Slide 134: Pooling of IP addresses
128.143.71.21
Router accepts all addresses in pool:
128.143.71.0 – 128.143.71.30

## Slide 135: Supporting migration between network service providers
Scenario: In CIDR, the IP addresses in a corporate network are obtained from the service provider. Changing the service provider requires changing all IP addresses in the network.
NAT solution:
  Assign private addresses to the hosts of the corporate network
  NAT device has static address translation entries which bind the private address of a host to the public address.
  Migration to a new network service provider merely requires an update of the NAT device. The migration is not noticeable to the hosts on the network.
  Note:
  The difference to the use of NAT with IP address pooling is that the mapping of public and private IP addresses is static.

## Slide 136: Supporting migration between network service providers

## Slide 137: IP Masquerading – Most Common NAT
Also called: Network address and port translation (NAPT), port address translation (PAT).
Scenario: Single public IP address is mapped to multiple hosts in a private network.
NAT solution:
  Assign private addresses to the hosts of the corporate network
  NAT device modifies the port numbers for outgoing traffic

## Slide 138: IP Masquerading

## Slide 139: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 140: Load balancing of servers
Scenario: Balance the load on a set of identical servers, which are accessible from a single IP address
NAT solution:
  Here, the servers are assigned private addresses
  NAT device acts as a proxy for requests to the server from the public network
  The NAT device changes the destination IP address of arriving packets to one of the private addresses of a server
  A sensible strategy for balancing the load of the servers is to assign the addresses of the servers in a round-robin fashion.

## Slide 141: Load balancing of servers
Source: 213.168.12.3
Destination: 10.0.1.4
Public Source
Address
This is a situation where one public address is shared by several machines
inside a private network for the sole purpose of load balancing.
Here we see that IP address 128.143.71.21 is shared by several machines.
The NAT device uses a round robin technique to distribute the incoming requests to the servers.
The source addresses of incoming requests are used to distinguish between the traffic streams connected to the internal servers.

## Slide 142: NAT: Public Services and P2P
NAT does not allow outside (public) access to any machine behind the NAT device if there is NO unique public IP address associated (directly mapped) with a specific internal IP address.
In other words, it can route traffic that is addressed to a device behind a NAT device ONLY if it has a public IP address allocated to it (i.e., mapped to its internal address).
  Services such as Web hosting, FTP, can be addressed by the one to one mapping of a specific IP address.
  P2P services (Skype, Spotify, etc.) cannot be hosted unless a specific server called a moderator/tracker/relay is used to serve as a go between.

## Slide 143: Possible NAT Scenarios
Three possible scenarios:
  Two clients reside behind the same NAT, on one private network
  The clients reside behind different NATs, different private networks
  The clients each reside behind two levels of NAT: a common “first-level”NAT deployed by an ISP for example, and distinct “second-level” NATs such as consumer NAT routers for home networks

## Slide 144: Hole Punching: UDP and TCP
one of the most effective methods of establishing peer-to-peer communication between hosts on different private networks is known as “hole punching.”
hole punching enables applications to function within the default security policy of most NATs, effectively signaling to NATs on the path that peer-to-peer communication sessions are “solicited” and thus should be accepted.
unfortunately, no traversal technique works with all existing NATs, because NAT behavior is not standardized.
we will focus on the simplest hole punching technique that works cleanly and robustly in the presence of “well-behaved” NATs in any reasonable network topology.

## Slide 145: NAT Terminology
The notion of session:
  “A session endpoint for TCP or UDP is an (IP address, port number) pair, and a particular session is uniquely identified by its two session endpoints.”
From the perspective of a host, a session is effectively identified by the 4-tuple (local IP, local port, remote IP, remote port).
The direction of a session is normally direction of the first packet that initiates the session: i.e., the initial SYN packet for TCP, or the first user datagram for UDP.
The most common type of NAT is traditional or outbound NAT, which provides an asymmetric bridge between a private network and a public network.
Outbound NAT has two sub-varieties: Basic NAT, which only translates IP addresses, and Network Address/Port Translation (NAPT), which translates entire session endpoints.
Hole punching uses NAPT.

## Slide 146: Understanding the Problem
The key to the NAT puzzle lies in making machines behind a NAT gateway reachable from the outside, (i.e., the public Internet).
To do that, an application has to force a host behind the NAT to initiate a connection to a host outside, that is seeking to connect to the internal host.
NAT devices allow inbound traffic, i.e., replies to requests originating from behind the NAT device.
So instead of connecting directly to the host behind NAT (impossible), we need to mimic a scenario in which the target host originates a connection to the outside host by responding to the request. In other words, the connection request to the target host should seem like a reply to the NAT device. “Connection Reversal”

## Slide 147: Approach
First is the issue of how to get the private host to send a request so we can send a “connection request” to it that is masquerading as a reply.
But, NAT devices (routers) also have an idle timer, typically of around 60 seconds, they stop waiting for replies once a request originates and no reply comes within 60 seconds. So, it is not enough that the private host originate traffic, but also we have to act fast—we have to send the “reply” before the NAT device (router) removes the “association” with the private host, which will frustrate the connection attempt.

## Slide 148: Traversal By Connection Reversal Using a Server – Public to Private
Going from a host/peer on the public IP internet to a host/peer on a private network with no dedicated public IP address.
Use a “rendezvous” server, listening on a global IP address through a persistent TCP or UDP connection.
If A on a private network wants to initiate a connection to B on a public network, then a direct connection attempt works automatically, because B is not behind a NAT and A’s NAT interprets the connection as an outgoing session.
If B wants to initiate a connection to A, however, any direct connection attempt to A is will not be routed by the Internet as A does not have a valid IP address.
B can instead relay a connection request to A through a well-known server S, asking A to attempt a “reverse” connection back to B.

## Slide 149: Connection Reversal
Public to Private

## Slide 150: Relaying Using an Intermediate Server – P2P both behind NAT
Relaying - A reliable, but least efficient method for P2P communication across NAT is simply to make the communication look to the network like standard client/server communication, through relaying.
Two client hosts, A and B, each initiate TCP or UDP connections to a well-known “rendezvous” server S, at S’s public IP address YY and a predetermined port number XX.
The two clients simply use the server S to relay messages between them along along their already-established client/server connections, and server S forwards the messages.
Connections (TCP and UDP) have to be persistent. NAT times out UDP NAPT connections, so it has to happen fast or host has to continue sending “keep alive” UDP packets to the server to maintain the connection. TCP session has to be kept alive too.

## Slide 151: Relaying with a Server

## Slide 152: UDP Hole Punching - Basic Idea
UDP hole punching enables two clients to set up a direct P2P UDP session with the help of a well-known “rendezvous” server, even if the clients are both behind NATs.
Rendezvous - eliminates the “Server” function after connection setup.
Hole punching assumes that the two clients, A and B, already have active UDP sessions with a “rendezvous” server S.
When a client registers with S, the server records two endpoints for that client: the (IP address, UDP port) pair that the client is using to talk with S, and the (IP address, UDP port) pair that the server observes the client to be using to talk with it. (private pair and public pair)
We refer to the first pair as the client’s private endpoint and the second as the client’s public endpoint.
HOW???

## Slide 153: Relaying
Public
End Point
Private
End Point

## Slide 154: Obtaining the Clients’ Private and Public Addresses
The server will obtain:
  the client’s private endpoint from the client itself in a field in the body of the client’s registration message, and
  obtain the client’s public endpoint from the source IP address and source UDP port from the in the IP and UDP headers of the registration message.

## Slide 155: Establishing P2P Sessions
A initially does not know how to reach B, so A asks S for help establishing a UDP session with B.
S replies to A with a message containing B’s public and private endpoints. At the same time, S uses its UDP session with B to send B a connection request message containing A’s public and private endpoints. Once these messages are received, A and B know each other’s public and private endpoints.
When A receives B’s public and private endpoints from S, A starts sending UDP packets to both of these endpoints, and subsequently “locks in” whichever endpoint first elicits a valid response from B. ?????
Similarly, when B receives A’s public and private endpoints in the forwarded connection request, B starts sending UDP packets to A at each of A’s known endpoints, locking in the first endpoint that works. ?????
The order and timing of these messages are not critical as long as they are asynchronous.
If both A and B are on the same NAT device the private endpoints will work. If they are not, then only the public endpoints will work to connect.

## Slide 156: Hole Punching: Same NAT

## Slide 157: Hole Punching Process

## Slide 158: After Hole Punching

## Slide 159: Hole Punching: Different NATs
Public
Private
Session A-B
155.99.25.11:6200
138.76.29.7:31000

## Slide 160: Hole Punching Scenarios
Three possible scenarios:
  Two clients reside behind the same NAT, on one private network
  The clients reside behind different NATs, different private networks
  The clients each reside behind two levels of NAT: a common “first-level”NAT deployed by an ISP for example, and distinct “second-level” NATs such as consumer NAT routers for home networks
It is in general difficult or impossible for the application itself to determine the exact physical layout of the network, and thus which of these scenarios (or the many other possible ones) actually applies at a given time.
Nevertheless, hole punching works automatically in all of these scenarios without the application having to know the specific network organization, as long as the NAT routers involved behave in a “reasonable” fashion, i.e., don’t overwrite IP addresses and port numbers in bodies of messages (i.e., registration messages).
Why? Because some apps embed IP addresses in the data, and to work properly the NAT needs to change the private address to the public one in the body of the message. In that case it wont work. So it depends on how the NAT is setup.

## Slide 161: NAT:Pros
local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 162: NAT: Cons
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved: -> IPv6
  violates end-to-end argument
    NAT existence and usage must be taken into account by app designers, e.g., P2P applications
    NAT traversal: what if client wants to connect to server behind NAT?