## Slide 1: Embedded Systems
Computer-based systems which do not appear to be computers
  Complexity is hidden from the user
Embedded systems are much more common than desktop/laptop systems
Interact with users via simple interface:
  Digital camera, TV, cellphone, …
Interact with another device, invisible to user:
  Disk drive, memory stick, anti-lock braking system, …

## Slide 2: Tight Constraints
Embedded design methodology: Be Efficient!
  Majority of embedded products are in cost critical markets (i.e. consumer electronics)
  Other applications are in performance/power critical markets (i.e. military, medical)
Constraints include:
  Maufacturing cost, Design cost, Performance, Power, Time-to-Market
Very different from traditional software engineering
  Moore’s law will save you eventually
Embedded system designers should be control freaks
  Need to have explicit control over timing, memory
  Why trust a compiler/interpreter/OS?

## Slide 3: Application Specificity
Embedded systems are generally application-specific
  Perform one task or set of related tasks
  Some devices blur the line (i.e. cell phones)
Allows design to be focused on one application
  Unlike general-purpose systems (i.e. laptop)
Higher design efficiency is possible
  Special-purpose vs. general purpose (i.e. video games)

## Slide 4: Hardware/Software Codesign
Hardware and software are often designed together
  General-purpose systems use HW and SW developed by different companies
Greatly improved optimization is possible
  Include only HW/SW needed for your application
More work for the designers
  Must understand both HW and SW

## Slide 5: Generic ES Structure
microcontroller
sensors
ADC
DAC
actuators
IP
FPGA
Sensors receive data from the world
Actuators cause events in the world
Application-Specific Integrated Circuit (ASIC)- special-purpose hardware
Field Programmable Gate Array (FPGA) - reconfigurable hardware

## Slide 6: Sensors
Receive data from the environment
  Motion - IR/ultrasonic detectors, potentiometers, encoders
  Light - Photoresistors, cameras
  Touch - Capacitive touch, pressure sensors
Variety of physical principles used
Many sensors are analog

## Slide 7: Actuators
Cause external events
  Mechanical - motors
  Audio – speakers, buzzers
  Visual – LED, LCD, laser
May consider external communication to be actuation
Many actuators are analog

## Slide 8: Analog/Digital Conversion
Analog-to-Digital Converter (ADC)
  Converts analog data to digital data
  Used to interface with analog sensors
Digital-to-Analog Converters (DAC)
  Converts digital signals to analog signals
  Used to interface with analog actuators

## Slide 9: Intellectual Property (IP) Core
An integrated circuit which performs one function
Cheap in high volume
Very useful for common tasks
  Network controllers (ethernet, CAN)
  Audio/Video (audio codec, VGA controller)
Must interact with the microcontroller
  Consider communication protocol

## Slide 10: Field Programmable Gate Array (FPGA)
Hardware which can be reconfigured via RAM
Faster than SW, slower than ASIC
No fabrication needed
Logic Block
Interconnect

## Slide 11: Microcontrollers
Microcontrollers are the center of the system
Accept input data, process it, make decisions, cause output events
Hardware/Software Interface
  Write code, execute it on a microcontroller
  Microcontroller interacts with hardware components

## Slide 12: General-Purpose vs. DSP
General-Purpose
  Used in for any application
  Many features included
Digital Signal Processors (DSP)
  Made to support DSP functions
  Vector instructions
  Cheaper but more limited

## Slide 13: Software Translation
Machine language: CPU instructions represented in binary
Assembly language: CPU instructions with mnemonics
  Easier to read
  Equivalent to machine language
High-level language: Commonly used languages (C, C++, Java, etc.)
  Much easier to use
All software must be translated into the machine language of the microcontroller

## Slide 14: Compilation/Interpretation
Compilation: Translate instructions once before running the code
  C, C++, Java (partially)
  Translation occurs only once, saves time
Interpretation: Translate instructions while code is executed
  Basic, Java (partially)
  Translation occurs every execution
  Translation can adapt to runtime situation

## Slide 15: Why C for Embedded Systems?
Easier to use than Assembly language
Allows more control than higher-level languages (Java, Python, etc.
C example Python example
int a, b, c; a = b + c
a = b + c;
How much memory is used in each example?

## Slide 16: Compilation Example
a = b + c;
lw $r1, ($s1)
lw $r2, ($s2)
add $r3, $r2, $r1
sw $r3, ($s3)
Load b from memory
Load c from memory
Add b and c
Store result a in memory
10010001000000110000001000000001
add
$r3
$r2
$r1
Compiler
Assembler

## Slide 17: Microcontroller Components
Register: Stores a single value
- Like a single memory location
- Extremely fast
- Extremely expensive
Storage Elements
- Data is stored in different components
- Speed/Cost (area) tradeoff
Several special-purpose registers, used internally
General-purpose registers, used by the program

## Slide 18: Storage Elements
Register File: Stores many values
- A set of registers, each has an address
- Acts just like a memory
- Extremely fast, expensive
Instruction operands are here
  add $r3, $r2, $r1
Can only read one or two registers at a time
May contain ~32 registers

## Slide 19: Memories
Cache: Stores many values
- Slower than a register file
- Cheaper than a register file
- Still fairly fast and expensive
Data cache holds data that the program operates on
Instruction cache holds program instructions

## Slide 20: Main Memory
Very big, Gigabytes (Gb)
Not in the CPU
Connected to the CPU via a system bus
Memory access is slow
Von Neumann Bottleneck
Memory is much slower then the CPU
Memory access time greatly slows program execution

## Slide 21: Arithmetic Logic Unit (ALU)
Performs arithmetic and logical functions on data
Many instructions use the ALU
  Arithmetic operations: add, subtract, etc.
  Logical Operations: AND, OR, XOR, etc.

## Slide 22: Special-Purpose Registers
Program Counter (PC)
Stores the address of the next instruction
Drives the instruction cache
Incremented after most instructions
Updated after jump/branch instructions
Program Status Word
Contains various bits indicating operation status
  Negative, zero, etc.
Contains privileged mode bit
  Indicates higher security permission

## Slide 23: Basic Processor Core
PC
Instruction
Cache
Register
File
Data
Cache
ALU
PC is updated after each instruction
Control logic needed to coordinate activity

## Slide 24: Executing an Instruction
Instruction Fetch – Get instruction from memory
  Update Program Counter afterward
Instruction Decode, Register Fetch – Identify instructions, get input operands
Execute – Perform operation
Register Write – Put result operands in register file
  add $r3, $r2, $r1

## Slide 25: Microcontroller Characteristics
Datapath Bitwidth
  Number of bits in each register
  Determines accuracy and data throughput
Input/Output Pins
  Need enough pins to support your application
Performance
  Clock rates are slower than desktop

## Slide 26: Other mproc Features
Timers
  Needed for real-time applications
Analog-to-Digital Converters
  Used to read input from analog sensors
Low-power modes
  Power saving is important
Communication protocol support
  Interface with other Ics
  UART, I2C, SPI, etc.

## Slide 27: AVR ATmega2560
8-bit microcontroller
Up to 16MHz
256KB of flash memory
4KB EEPROM, 8KB SRAM
Peripherals
  Timers, PWM, comparators, ADC, …

## Slide 28: AVR STK600 Board
Allows many different Atmel AVR microcontrollers to be programmed and interfaced with
Comes with a Routing Card containing the ATmega2560
Allows direct access via board pins
Other interfaces: USB, CAN, RS-232

## Slide 29: Facts about STK600
Has LEDs and buttons for experimentation
Headers are available to connect to microcontroller pins
Microcontroller I/O pin headers must be connected to board components manually using cables
Programming I/O must also be connected manually to board programming HW

## Slide 30: Atmel Studio 6.1
Integrated Development Environment (IDE) provided by Atmel
  Replaces Eclipse
Free download from www.atmel.com
Install everything that it tries to install
  .NET, Visual Studio Shell, USB driver, etc.
GNU toolchain is automatically installed too

## Slide 31: Atmel Studio 6.1 Example
Project – A single application
  Can contain many files (.c, .h, etc.)
Solution – Contains all code on a single microcontroller
  Can contain many projects
Solution Explorer – Contents of solution
Output – Results of operations

## Slide 32: Make a New Project
File->New->Project
Select GCC C Executable Project
Name and Solution Name are the same
Note the location – a directory will be created
Click OK when done

## Slide 33: Select Device
Window appears after new project is created
Select device ATmega2560

## Slide 34: C Code Template
Text editor in upper left corner with program template
Solution Explorer lists all projects/files
Write the C code
Compile: Build->Build Solution
Build Succeeded message at bottom
Should create .elf file in Debug subdirectory of the project

## Slide 35: Programming the Board
Plug in the board via USB
Turn on the board
  May download drivers if it is the first time
  May update firmware
Bring up programming window
  Tools->Device Programming

## Slide 36: Interface Settings
Select Tool STK600
Select Device ATmega2560
Select Interface ISP
Click Apply
  May upgrade firmware
Set ISP clock
  100kHz is safe
Read Device ID and Target Voltage
  Verifies communication

## Slide 37: Programming Memory
Must program the .elf file into the Flash memory
Select Memories in left column
Browse to select the .elf file under Flash
  In Debug directory
Click Program

## Slide 38: Communication Problem
After board is connected, may get an error about “Cannot establish connection to debugging agent” or something like that
May be caused by a firewall
I had this problem with McAfee, not with Avast
Might occur with other anti-virus/firewall tools