## Slide 1: Therac-25
Slides created by:
Professor Ian G. Harris
Computer-controlled radiation therapy machine
Massively overdosed 6 people, June 1985–January 1987
Medical linear accelerator
Radiation beam bent and spread using magnets
Controlled by a PDP-11
Dual-mode – electron setting (low energy) or X-ray photon (high energy)

## Slide 2: History of the Device
Slides created by:
Professor Ian G. Harris
Therac-6
  Photon mode only
  Manual device, PDP-11 for convenience
  Hardware safety features
Therac-20
  Dual mode device
  Manual device, PDP-11 for convenience
  Hardware safety features
Therac-25
  Dual mode device
  Automatic device PDP-11 required
  Some hardware safety features replaced by software

## Slide 3: Turntable
Slides created by:
Professor Ian G. Harris
Rotates equipment into the beam path
3 modes, 3 sets of equipment
Electron mode – scan magnets to spread beam
X-ray photon mode – flattener needed to focus and weaken beam
  Very high energy beam
Field light position – mirror needed to pass light
Mirror
Turntable in the wrong position = Death

## Slide 4: Basic Operation
Slides created by:
Professor Ian G. Harris
Operator enters desired parameters
Each parameter is verified by sensors
After all parameters are verified, operator can type ‘p’ for ‘proceed’
Treatment Pause shutdown
  Small parameter variation
  Wait 5 secs, press ‘p’
Treatment Suspend shutdown
  Major problem
  Must reset system

## Slide 5: Therac-25 Software
Slides created by:
Professor Ian G. Harris
Borrowed code from Therac-20
  Assumed that the code was good
  Ignored the fact that hardware safety had been removed
Written in PDP 11 assembly code
Real-time OS developed for this device
  Preemptive, priority scheduling algorithm
  0.1 second time quantum

## Slide 6: Software Tasks
Slides created by:
Professor Ian G. Harris
Critical Tasks
  Treatment Monitor – manages all stages of the setup and treatment process
  Servo Task – controls gun emission, dose rate, beam steering, and machine motions
  Housekeeper Task – performs checks of system status, limits, displays messages to CRT
Non-Critical Tasks
  Keyboard processor
  Screen processor
  Hand task – set turntable to proper position for selected mode/power

## Slide 7: Data Entry Process
Slides created by:
Professor Ian G. Harris
Treat task accepts data in the Datent state
Keyboard handler writes data to the MEOS structure
Hand task uses low byte of MEOS to rotate turntable
Keyboard handler assumes that: data entry is complete when the cursor is at the bottom of the page
  Does not consider parameter corrections

## Slide 8: Data Entry Complete
Slides created by:
Professor Ian G. Harris
When data entry is complete, Datent does the following
  Calls MAGNET subroutine to adjust bending magnets
  Move to Set Up Test state (apply radiation)
MAGNET subroutine takes time (8sec), calls Ptime for each magnet
Ptime exits if MEOS is changed, but only on the first call to Ptime
If MEOS changes during calls to Ptime (other than the first), the change is not registered by Hand
Possible Error
  Operator sets field light mode by mistake
  Turntable rotates to mirror
  Operator quickly changes mode to photon mode
  X-ray photons are emitted with no attenuation

## Slide 9: Software Problems
Slides created by:
Professor Ian G. Harris
Bytes of MEOS can be non-correlated
  Offset parameters byte can be updated while mode/energy byte changes are ignored
Access to MEOS should be mutually exclusive
  No read access while data entry is not complete
  Proper detection of Data Entry Complete
Solution
  “the key for moving the back through the prescription sequence must not be used for editing or any other purpose.”

## Slide 10: Second Bug
Slides created by:
Professor Ian G. Harris
Occurred during the Set Up Test phase, after Datent
Each pass through Set Up Test increments the turntable position check variable Class3
  If Class3 is non-zero then the turntable position must be checked to match the parameters
Set Up Test is executed hundreds of times
  Rescheduled waiting for other events
Class3 is 1 byte long
Every 256th pass through Set Up Test, checking is not performed
If the operator presses “set” on pass 256, turntable position can be in field light position

## Slide 11: Hardware Abstraction
Slides created by:
Professor Ian G. Harris
A processor may use many types of I/O devices
Each device has a different interface
  Look at the datasheets
Applications cannot handle variations in hardware
  There are far too many
Operating systems abstract hardware details from user processes
  Disk vs. USB flash – no difference

## Slide 12: Device Drivers
Slides created by:
Professor Ian G. Harris
A uniform interface (mostly) for the interaction between SW and HW devices
User Application
Library Function
System Call
Device Driver
HW
User
Space
Kernel
Space
“Hello, world.”
printf
vfprintf
HDMI or UART driver
HDMI or UART port

## Slide 13: Functions of Device Drivers
Slides created by:
Professor Ian G. Harris
Initialize the device
Accept read/write requests from the layer above
Check validity of input parameters
Add device-specific detail to requests
  Disk write – track, sector, cylinder number
Check if device is in use
Control the device
  Conform to device input protocol (SATA, I2C, …)
Respond to device
  i.e. accept incoming network message

## Slide 14: Device Driver Implementation
Slides created by:
Professor Ian G. Harris
Interface to system calls is defined as a standard set of functions
Driver code must convert system requests into I/O signaling in the protocol of the device
Must respond to interrupts from the device
  Driver may include interrupt service routines
Device Driver
System Call
HW Device
void vfprintf (…) {
open(device);
…
write(device,data);
VGA Controller
IC
I/O protocol
Interrupts

## Slide 15: Device Driver Protocol
Slides created by:
Professor Ian G. Harris
Each interface function in the driver should write appropriate data into the device registers
  Most devices have registers to accept commands
  Typically write to them using standard bus protocol (I2C, etc.)
After writing a command, verify that command is accepted
  Check error conditions (ACK or NACK, etc.)
Synchronize with the device I/O
  Block or not, wait for interrupt or not
  Several options on this
Structure for the behavior of a device driver

## Slide 16: File System Interface
Slides created by:
Professor Ian G. Harris
All devices look like files on a linux system
Special files are created, usually in the /dev directory
Device interaction is the same (mostly) as file interaction
User programs
Virtual File System Switch
Hardware
fd=open(“/dev/abc”)
read(fd)
write(fd,dat)
close(fd)
abc_open()
abc_read()
abc_write()
abc_close()
System calls
Device driver routines

## Slide 17: Driver Routine Execution
Slides created by:
Professor Ian G. Harris
Execute as part of the operating system
  Need highest access to interact with HW
Can be compiled into the kernel
  Common on embedded systems
  Drivers are fixed
Can be loaded dynamically
  Loadable Kernel Modules (LKM) in linux
Bugs in drivers can be damaging
  Same access as OS
  Security vulnerabilities are an issue

## Slide 18: Types of Devices
Slides created by:
Professor Ian G. Harris
Three types depending on how data is transferred
Character Device
  Can read and write individual characters efficiently to this device
Block Device
  More efficient to read/write blocks of data (i.e. disk drives)
  I/O buffering is commonly used
Network Device
  Device needs to be services periodically
  Interrupts are needed

## Slide 19: Major and Minor Numbers
Slides created by:
Professor Ian G. Harris
Each device is assigned a major number which indicates the device type and its driver
Minor number is the specific device within the major number
Name | Create/Owner | Permissions | Major | Minor
/dev/usbmon0 | root, root | crw------- | 252 | 0
/dev/usbmon1 | root, root | crw------- | 252 | 1

## Slide 20: Device Driver Interface
Slides created by:
Professor Ian G. Harris
Each device must implement an interface according to its type
Character drivers implement the file_operations interface
struct file_operations {
ssize_t (*read) (struct file *, char *, size_t, loff_t *);
ssize_t (*write) (struct file *, const char *, size_t, loff_t *);
int (*ioctl) (struct inode *, struct file *, unsigned int, unsigned long);
int (*open) (struct inode *, struct file *);
int (*release) (struct inode *, struct file *);
…
};
open, release, read, write are the basics

## Slide 21: Driver Routine Example
Slides created by:
Professor Ian G. Harris
Need a driver for an SRAM chip connected via I2C
  We did this before
  Philips PCF8570, 256 locations, 8-bit
Decide how to map device access to file access operations
Device is random access but files are sequential access
Solution: Make device sequential access
  Maintain readPtr and writePtr for next read/write access address
  Read operation reads from readPtr++
  Write operation writes to writePtr++

## Slide 22: open and release
Slides created by:
Professor Ian G. Harris
Note: This is a simplified version
  Driver-specific data structure in the inode, mem_dev
int mem_open(struct inode *inode, struct file *file){
mem_dev->readPtr = 0;
mem_dev->writePtr = 0;
return 0;
}
int mem_release(struct inode *inode, struct file *fd){
return 0;
}

## Slide 23: write considerations
Slides created by:
Professor Ian G. Harris
Write takes 4 arguments
  struct file *fp: file pointer (not needed)
  char *buf: buffer to write to device
  size_t count: number of bytes to write to device
  loff_t *ppos: Position in device to write to
    Should be mem_dev->writePtr
Copying data requires special functions
  User space and kernel space may have different memory mappings
  May not trust pointers provided by user app
copy_to_user(), copy_from_user()

## Slide 24: write implementation
Slides created by:
Professor Ian G. Harris
int mem_write(struct file *fp, char *buff, size_t cnt,
loft_t *ppos){
char data;
for (int i=0; i<cnt; i++) {
copy_from_user(&data, buff+cnt, 1);
WriteMTSR(MEM_I2C_ADDR, (*ppos)++, data);
}
return 0;
}
WriteMTSR writes a char to an I2C slave at the given address
MEM_I2C_ADDR is the I2C address of the memory
Must update *ppos

## Slide 25: init Function
Slides created by:
Professor Ian G. Harris
init is called when the driver is loaded
  Or during boot for a static driver
Responsibilities:
Associating a device major number with the driver
Allocating memory for the per-device structure
Connecting the entry points (open(), read(), etc.) with the driver
Initializing hardware
  Check if it exists

## Slide 26: register_chrdev Function
Slides created by:
Professor Ian G. Harris
Registers the driver with the virtual file system switch (VFS)
struct file_operations mem_fops = {
NULL, /* lseek() */
mem_read, /* read() */
mem_write, /* write() */
…
};
long mem_init(long kmem_start) {
printk("Sample Device Driver Initialization\n");
if (register_chrdev(22, “mem", &mem_fops))
printk("error--cannot register!\n");
TurnOnI2C();
return 0;
}

## Slide 27: Buffered I/O
Modified version of slide by Paul Krzyzanowski
Kernel copies the write data to a block of memory (buffer):
  Allow the process to write bytes to the buffer and continue processing
  Buffer does not need to be written to the disk … yet
Read operation:
  When the device is ready, the kernel places the data in the buffer
Why is buffering important?
  Deals with device burstiness
    Rate mismatch between host and device
  Caching (for block devices)
  Alignment (for block devices)

## Slide 28: Buffer Cache
Modified version of slide by Paul Krzyzanowski
Pool of kernel memory to hold frequently used blocks from block devices
Minimizes the number of I/O requests that require device I/O
Allows applications to read/write from/to the device as a stream of bytes or arbitrary-sized blocks
User I/O Requests
Buffer Cache
Device Block I/O Requests
fast
slow