## Slide 1: ATmega 2560 Datasheet
Main features are listed
Multiple similar parts described in one datasheet

## Slide 2: ATmega 2560 Pins
Fixed-Use pins
  VCC, GND, RESET
  XTAL1, XTAL2 - input/output for crystal oscillator
  AVCC - power for ADC, connect to VCC
  AREF - analog reference pin for ADC
General-Purpose ports
  Ports A-E, G, H, J, L
  Ports F and K are for analog inputs
  All ports are 8-bits, except G (6 bits)

## Slide 3: ATmega 2560 Pin Positions
Pin positions are always in the datasheet
Many pins have multiple functions/names

## Slide 4: IC Packages
Package determines IC dimensions, pin size/spacing
Surface mount packages are very small
ICs are often available in multiple packages
Thin quad flat pack (TQFP)
Ceramic ball grid array (CBGA)

## Slide 5: ATmega 2560 Architecture
Shows connectivity between peripherals, memory, I/O, bus
CPU core is in the center, executes instructions

## Slide 6: Pin Descriptions
Function of each pin is described
Descriptions are brief, assuming an understanding of the part
Almost all pins can be accessed on the STK 600

## Slide 7: AVR CPU Core
Common CPU for all AVR parts
Ex. add $r1, $r2, $r3
Read instruction from program memory
Load instr. into instr. Register
Get source register numbers from instruction
Fetch source data from register file
Pass sources to ALU, add
Pass result to register file

## Slide 8: AVR Status Register
Records “interesting events” which must be handled
Sign bit, carry flag, overflow flag, negative flag, zero flag, etc.
May be used as branch conditions or to trigger interrupts

## Slide 9: General Purpose Registers
32 8-bit registers
Used by the compiler
X, Y, and Z registers are 16-bits long
  XH, XL, etc.
Used to address memory (64K)

## Slide 10: Instruction Execution Timing
Two-stage pipeline, fetch, and execute
Register fetch, execute, and write back, all in one clock cycle

## Slide 11: SRAM Organization
64K addressable memory
Registers mapped to beginning addresses
Internal SRAM mapped in the middle
External SRAM mapped at the end

## Slide 12: I/O Pins, Output Path
DDRx
PORTx

## Slide 13: I/O Pins, Input Path
PINx

## Slide 14: I/O Control Registers
DDRx – Controls the output tristate for port x
  DDRx bit = 1 makes the port x an output pin
  DDRx bit = 0 makes the port x an input pin
  Ex. DDRA = 0b11001100, outputs are bits 7, 6, 3, and 2
PORTx – Control the value driven on port x
  Only meaningful if port x is an output
  Ex. PORTA = 0b00110011 assigns pin values as shown
PINx – Contains value on port x
  Ex. Q = PINC;

## Slide 15: Typical Embedded C Program
#include <stdio.h>
main() {
// initialization code
while (1) {
// main code
}
}
#include is a compiler directive to include (concatenate) another file
main is the function where execution starts

## Slide 16: C Syntax Basics
Comments: single line //, multiline /* … */
Semicolon used to terminate all statements
# indicates a compiler directive (include, define, etc.)
Brackets { … } group lines of code for execution
Blankspace between lines is not important in C
  Still need to separate tokens
int a, b, c;
a = b + c;
int a,b,c;a=b+c;
inta,b,c;a=b+c;
correct
incorrect (inta)
correct

## Slide 17: Variables
All variables’ types must be declared
  Memory space requirements known statically
  Type checking can be performed at compile-time
Numerical Types: int, float, double
Other types: char, void
Type qualifiers: short, long, unsigned, signed, const
  Specify alternate sizes, constrain use modes

## Slide 18: Variable Declaration
Static allocation vs. Dynamic allocation
Static dedicates fixed space on the stack
  int i;
Dynamic (malloc) allocates from the heap at runtime
  ptr = malloc(32);
Type sizes depend on the architecture
  On x86, int is 32 bits
  On ATmega2560, int is 16 bits
  char is always 8 bits

## Slide 19: Volatile Variables
The value of a volatile variable may change at any time, not just at an explicit assignment
Also, may be read at any time
Compiler optimizations are not applied to volatile variables
for (i=0; i<10000; i++);
An optimizing compiler would delete this loop
  i is not used anywhere in the code
i = 1; … i = 1;
If i is not modified in between, the second assignment is removed

## Slide 20: Volatile Variables
When can variables be used without an explicit assignment?
1. Memory-mapped peripheral registers
2. Global variables modified by an interrupt service routine
3. Global variables accessed by other processors

## Slide 21: Volatile Example
.
.
while (*periph != 1); // wait until data transfer
. // is complete
.
periph is the mapped address of the peripheral status info
*periph is assigned by peripheral directly
Compiled code will move memory contents to a register
Memory will only be moved once because *periph does not change

## Slide 22: Base Representation
Base 10 is default
Base can be specified with a prefix before the number
Binary is 0b, Hexadecimal is 0x
  Ex. char x = 0b00110011;
  char x = 0x33;
Binary is useful to show each bit value
Hex is compact and easy to convert to binary
  1 hex digit = 4 binary digits

## Slide 23: Types of Statements
Assignment – =
Relational - <, >, ==, !=
Control Flow – if, for, while, do, switch
Arithmetic Operations - +, -, *, /, %
Logical Operations - &&, ||, !
Bitwise Logical Operations - &, |, ^

## Slide 24: Logical Operators
These operators accept binary input and produce binary output
&&, ||, !
Non-binary inputs are cast to binary values
int a=1, b=0; c=56; d=-1, res;
res = a && b; // res = 0
res = a || b; // res = 1
res = c && d; // res = 1

## Slide 25: Bitwise Operations
Treat the value as an array of bits
Bitwise operations are performed on pairs of corresponding bits
X = 0b0011, Y = 0b0110
Z = X | Y = 0b0111
Z = X & Y = 0b0001
Z = X ^ Y = 0b0101
Z = ~X = 0b1100
Z = X << 1 = 0b0110
Z = x >> 1 = 0b0001

## Slide 26: Bit Masks
Need to access a subset of the bits in a variable
  Write or read
Masks are bit sequences which identify the important bits with a ‘1’ value
Ex. Set bits 2 and 4 in X, don’t change other bits
  X = 01010101, mask = 0010100
  X = X | mask
Ex. Clear bits 2 and 4
  mask = 11101011
  X = X & mask

## Slide 27: Bit Assignment Macros
1 << (n) and ~(1) << (n) create the mask
  Single 1 (0) shifted n times
Macro doesn’t require memory access (on stack)
#define SET_BIT(p,n) ((p) |= (1 << (n)))
#define CLR_BIT(p,n) ((p) &= (~(1) << (n)))

## Slide 28: Header Files
Files included at the top of a code file
Traditionally named with .h suffix
Include information to be shared between files
  Function prototypes
  externs of global variables
  Global #defines
Needed to refer to libraries

## Slide 29: Function Calls
Functions enable simple code reuse
Control moves to function, returns on completion
Functions return only 1 value
main() {
int x;
x = foo( 3, 4);
printf(“%i\n”, x);
}
int foo(int x, int y) {
return (x+y*3);
}

## Slide 30: Function Call Overhead
main() {
int x;
x = foo(2);
printf(“%i\n”, x);
}
int foo(int x) {
int y=3;
return (x+y*3);
}
Program counter value needs to be restored after call
Local variables are stored on the stack
Function calls place arguments and return address on
the stack
20:
21:
22:
30:
31:
103: | 3 | local var
102: | 2 | argument
101: | 21 | return addr
100: | 2 | local var

## Slide 31: Embedded Toolchain
A toolchain is the set of software tools which allow a program to run on an embedded system
Host machine is the machine running the toolchain
Target machine is the embedded system where the program will execute
  Host has more computational power then target
We are using the GNU toolchain
  Free, open source, many features

## Slide 32: Cross-Compiler
A compiler which generates code for a platform different from the one it executes on
  Executes on host, generates code for target
Generates an object file (.o)
Contains machine instructions
References are virtual
  Absolute addresses are not yet available
  Labels are used instead

## Slide 33: Cross-Compiler Example
ABBOTT.o
…
MOVE R1, (idunno)
CALL whosonfirst
…
ABBOTT.c
int idunno;
…
whosonfirst(idunno)
…
Cross- compiler
COSTELLO.c
int whosonfirst(int x)
{
…
}
Cross- compiler
COSTELLO.o
…
…
whosonfirst:
…
Idunno, whosonfirst
Unknown addresses

## Slide 34: Linker
Combines multiple object files
References are relative to the start of the executable
Executable is relocatable
Typically need an operating system to handle relocation

## Slide 35: Linker Example
ABBOTT.o
…
MOVE R1, (idunno)
CALL whosonfirst
…
COSTELLO.o
…
whosonfirst:
MOVE R5, R1
…
HAHA.exe
…
MOVE R1, 2388
CALL 1547
…
MOVE R5, R1
…
(value of idunno)
1547
2388
Linker
Functions are merged
Relative addresses used

## Slide 36: Linker/Locator
Links executables and identifies absolute physical addresses on the target
Locating obviates the need for an operating system
Needs memory map information
  Select type of memory to be used (Flash, SRAM, …)
  Select location in memory to avoid important data (stack, etc.)
  Often provided manually

## Slide 37: Segments
Data in an executable is typically divided into segments
Type of memory is determined by the segment
Instruction Segment - non-volatile storage
Constant Strings – non-volatile storage
Uninitialized Data – volatile storage
Initialized Data – non-volatile and volatile
  Need to record initial values and allow for changes

## Slide 38: AVR GNU Toolchain
Cross-Compiler: avr-gcc
Linker/Locator: avr-ld
Cross-Assembler: avr-as
Programmer: avrdude
All can be invoked via Atmel Studio 6

## Slide 39: Controlling Pins
int main (void) {
DDRA = 0xFF; // Set pins to OUTPUT
while (1) {
PORTA = 0xFF;
}
}