## Slide 1
The Arduino Platform
A “development module”
A board with a microcontroller and USB interface to a PC
Large open source community

## Slide 2
Arduino Environment
A development board
- 8-bit microcontroller
- programming hardware
- USB programming interface
- I/O pins
A software environment
- cross-compiler
- debugger
- simulator
- programmer
Special-purpose “shields”
- daughter boards
- unique functionalities
- easy to attach
- good libraries provided

## Slide 3
Arduino Hardware
Microcontroller | ATmega328
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limits) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
Analog Input Pins | 6
DC Current per I/O Pin | 40 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega328) of which 0.5 KB used by bootloader
SRAM | 2 KB (ATmega328)
EEPROM | 1 KB (ATmega328)
Clock Speed | 16 MHz
Typical of an 8-bit processor
- low speed, low memory
- low cost ($1.50 for the microcontroller, $40 for the board)

## Slide 4
Raspberry Pi
32-bit processor
Broadcom BCM2838 SoC, ARM11
700 MHz clock
512 MB RAM
Broadcom VideoCore IV GPU
SD card slot, no flash built-in
Ports: USB (2), HDMI, RCA audio/video, SD, Ethernet, 2x13 pins
MIPI Camera Interface
Size of a credit card
$35

## Slide 5
Raspberry Pi Software
32-bit machine, can support an operating system
  Arch linux, Debian, Fedora, Slackware, etc.
A bit slow for development
  Hard to run GUI, IDE
Cross compile with crosstool-ng toolchain or gcc-linaro-arm-linux
Easy Python programming interface is available

## Slide 6
BeagleBone Black
TI Sitara AM3359 ARM Cortex-A8
32-bit processor
1 GHz clock
512 MB RAM
2GB on-board flash
3D graphics accelerator
Ports: USB, Ethernet, HDMI, 2x46 pins
$45 cost, almost the same as an Arduino

## Slide 7
Beagle Software Environment
Several versions of linux are ported
  Ubuntu, Angstrom, Android …
A bit slow for development
  Hard to run GUI, IDE
Cross compile with gcc-arm toolchain
BoneScript (JavaScript) library is provided for simplicity
  Uses an interpreter

## Slide 8
BeagleBone “Capes”
Application-specific, stackable, daughter boards
  Just like Arduino shields
Come with libraries
VGA Cape
DVI-D Cape
Camera Cape

## Slide 9: UART/USART
Universal Asynchronous Receiver/Transmitter
Used for serial communication between devices
UART is asynchronous, no shared clock
Asynchronous allows longer distance communication
  Clock skew is not a problem
USART is the synchronous version of UART
  Common clock is needed
NVIDIA® Tegra™ 250
NVIDIA® Tegra™ 250

## Slide 10: Serial Protocols
Data is transmitted serially
  Only 1 bit needed (plus common ground)
Parallel data transmitted serially
Original bytes/words regrouped by the receiver
Many protocols are serial to reduce pin usage
  Pins are precious

## Slide 11: UART Applications
Slides created by:
Professor Ian G. Harris
Used by modems to communicate with network
Computers used to have an RS232 port, standard
Not well used anymore, outside of embedded systems
  Replaced by USB, ethernet, I2C, SPI
Simple, low HW overhead
Built into most microcontrollers

## Slide 12: Simple UART Structure
Slides created by:
Professor Ian G. Harris
Tx
Rx
Serial Out
Serial In
Parallel In
Parallel Out
status
status
Data is serialized by Tx, deserialized by Rx
Status indicates the state of the transmit/receive buffers
  Used for flow control

## Slide 13: UART Timing Diagram
Slides created by:
Professor Ian G. Harris
First bit is the Start Bit, initiates the transfer
Next bits are the data
Last are the Stop Bits
1 bit
8 bits

## Slide 14: Bit Duration
Slides created by:
Professor Ian G. Harris
Each bit is transmitted for a fixed duration
The duration must be known to Tx and Rx
Baud Rate (f) determines the duration (T)
Baud Rate is the number of transitions per second
    Typically measured in “bits per second (bps)”
T = 1/f
    Ex. F = 9600 baud, T = ~104 microsec
Transmission rate is less than baud rate
  Need start bit, stop bits, parity bit

## Slide 15: UART Synchronization
Slides created by:
Professor Ian G. Harris
Receiver must know the exact start time
    Imprecise start time corrupts data
0
1
stop
bit 7
bit 8
stop
Expected Bit, correct
Expected Bit, incorrect
bit 7
bit 8
stop

## Slide 16: Start Bit, Synchronization
Slides created by:
Professor Ian G. Harris
Detection of the start bit is used to synchronize
  Synchronization based on falling edge of start bit
Start bit is a falling edge
  Following 0 must be long duration to screen out noise
Receiver samples faster than baud rate (16x typical)
Start bit is indicated by a 0 of at least half period
Just a glitch
Start bit detected

## Slide 17: Parity Bit
Slides created by:
Professor Ian G. Harris
Transmission medium is assumed to be error-prone
  E-M radiation noise, synchronization accuracy
Parity bit may be transmitted to check for errors
  Even Parity: Number of 1’s is even
  Odd Parity: Number of 1’s is odd
Parity bit is added to ensure even/odd parity
  After data, before stop bit(s)
Ex. Assume Odd Parity, Data = 011011010
  Parity bit = 0, total parity is odd

## Slide 18: Stop Bit
Slides created by:
Professor Ian G. Harris
Receiver expects a 1 after all data bits and parity bits
If 1 is not received, error has occurred
1 bit
8 bits
Stop Bit

## Slide 19: Data Throughput vs. Baud
Slides created by:
Professor Ian G. Harris
Every transmission involves sending signaling bits
  Stop, start, parity
Data throughput rate is lower than baud rate
  Signaling bits must be sent
Ex. 8 data bits, 1 parity bit, baud rate = 9600
  Send 11 bits to send 8 data bits
  Transmission efficiency = 8/11 = 73%
  Data throughput rate = 9600 * 0.73 = 6981.8 bps

## Slide 20: USART HW in ATmega
Slides created by:
Professor Ian G. Harris
Transmit Pin
Receive Pin
Clock Pin
For synchronous transfers
Output (input) for master (slave)

## Slide 21: Clock Generation
Slides created by:
Professor Ian G. Harris
Two (or 3) clocks may be needed
Internal Clock – Two internal clocks
  High speed clock used by receiver to sample incoming signal
  Slower baud rate clock used by transmitter to time transmission
External Clock – Only used in synchronous mode
  Baud rate clock used to synchronize master and slave
  Generated by master, read by slave

## Slide 22: Clock Generation Logic
Slides created by:
Professor Ian G. Harris
Rx clk in generated from internal fosc
UBRRn – Prescalar value used to generate Rx clk
UBRRn is two 8-bit registers, UBRRH and UBRRL
Internal Tx Clk
Internal Rx Clk

## Slide 23: Clock Operation Modes
Slides created by:
Professor Ian G. Harris
Normal Asynchronous
  Rx/Tx clk rate is 16x baud rate
  Accurate sampling of signal, good synchronization
Double Speed Asynchronous
  Rx/Tx clk rate is 8x baud rate
  Double speed transmission, less accurate synchronization
Master Synchronous
  Synchronous communication, generate clk
Slave Synchronous
  Synchronous communication, receive clk

## Slide 24: Setting Clocks
Slides created by:
Professor Ian G. Harris
High Speed Internal Clock
  Internal Rate = fosc / (UBRRn + 1)
Baud Rate Clk, Normal Asynchronous
  Baud = fosc / 16 (UBRRn + 1)
Baud Rate Clk, Double Speed Asynchronous
  Baud = fosc / 8 (UBRRn + 1)

## Slide 25: Frame Formats
Slides created by:
Professor Ian G. Harris
USART has several communication options to define how many bits are transmitted
  Start bit: 1
  Data bits: 5 – 9
  Parity bit: none, even, odd
  Stop bits: 1 or 2
Set using bits in the UCSRnB and UCSRnC registers
Format must match on both transmitter and receiver

## Slide 26: USART Register Summary
Slides created by:
Professor Ian G. Harris
UBBR is the prescalar used to determine the clocks
  Determines the BAUD rate
UCSRA indicates the status of communications
  Transmit/Receive complete, errors, etc.
UCSRB enables interrupts and communications
  Interrupt enable, Tx/Rx enable, data size, etc.
UCSRC sets parity bits, stop bits, USART mode, ...
UDR holds transmit data and received data

## Slide 27: UCSRA
Slides created by:
Professor Ian G. Harris
Bit 7 – RXCn: USART Receive Complete
Bit 6 – TXCn: USART Transmit Complete
Bit 5 – UDREn: USART Data Register Empty
Bit 4 – FEn: Frame Error
Bit 3 – DORn: Data OverRun
Bit 2 – UPEn: USART Parity Error

## Slide 28: Typical USART Initialization
Slides created by:
Professor Ian G. Harris
#define FOSC 1843200// Clock Speed
#define BAUD 9600
#define MYUBRR FOSC/(16*BAUD)-1
void main( void )
{ USART_Init ( MYUBRR ); }
void USART_Init( unsigned int ubrr){
/* Set baud rate */
UBRRH = (unsigned char)(ubrr>>8);
UBRRL = (unsigned char)ubrr;
/* Enable receiver and transmitter */
UCSRB = (1<<RXEN)|(1<<TXEN);
/* Set frame format: 8data, 2stop bit */
UCSRC = (1<<USBS)|(3<<UCSZ0);
} // USART_Init

## Slide 29: Transmitting Data
Slides created by:
Professor Ian G. Harris
void USART_Transmit( unsigned char data )
{
// Wait for empty transmit buffer
while ( !( UCSRA & (1<<UDRE)) );
// Put data into buffer, sends the data
UDR = data;
}
Data is transmitted by placing it in the UDR register
Data Register Empty (UDRE) bit of the UCSRA register
  Set to 0 while a transfer is going on
  Need to wait for it before sending new data

## Slide 30: Receiving Data
Slides created by:
Professor Ian G. Harris
void USART_Receive( void )
{
// Wait for data to be received
while ( !( UCSRA & (1<<RXC)) );
// Read data from UDRn buffer
return ( UDR );
}
Data is received by reading it from the UDRn register
  Different from transmit UDRn register
Receive Complete flag (RXC) bit of the UCSRA register
  Set to 1 when new data is received

## Slide 31: Communicating with a PC
Slides created by:
Professor Ian G. Harris
Need a Terminal Emulator program which “speaks” UART (serial)
There are many free terminal emulators
  Hyperterm (used to come with Windows)
  Termite
  Putty (which I use)
Need to select a COM port to find the USB-to-serial adapter
Need to match frame format to the ATmega

## Slide 32: Putty Terminal Emulator
Slides created by:
Professor Ian G. Harris
Can communicate in several protocols
Select “Serial”
Fill in baud rate
Adjust settings by selecting “Serial” in left column

## Slide 33: Putty Serial Settings
Slides created by:
Professor Ian G. Harris
Flow control
  Atmega does not seem to support any

## Slide 34: UART Uses
Slides created by:
Professor Ian G. Harris
UART may be an extra (slow) communication channel
Useful if communication speed is not a problem
Debugging
  Make a “print” statement
  Note: will alter performance, but not much
Simple User Interface
  Humans are slow, interface can be as well

## Slide 35: Synchronous Communication
Slides created by:
Professor Ian G. Harris
Synchronous protocols share a common clock
More accurate, faster than asynchronous protocols
  Sampling time is accurately known
Restricted to short range communication
  Clock edge and data must have identical timing
  Clock edge must arrive at all receivers simultaneously

## Slide 36: Synchronous Protocols
Slides created by:
Professor Ian G. Harris
USART
  Limited to communication between two devices (or broadcast)
Serial Peripheral Interface (SPI)
  Multi-Drop Bus protocol, more than two devices
  Single master, many slaves
Inter-Integrated Circuit (I2C)
  Multi-drop, multi-master

## Slide 37: SPI
Slides created by:
Professor Ian G. Harris
a.k.a Four Wire Interface
MOSI
MISO
SCLK
SS’
MOSI
MISO
SCLK
CS’
Master
Slave
Master Out Slave In (MOSI) –From Master to Slave
Master In Slave Out (MISO) –From Slave to Master
SCLK – Clock generated by Master
Slave Select (SS’) – Indicates communication w/ selected slave
Chip Select (CS’) – Alerts slave to communication

## Slide 38: SPI Data Transmission
Slides created by:
Professor Ian G. Harris
Serial transmission synchronized by the clock
Many bytes may be sent in a single transfer
  8-bits is what we will use
Bi-directional data transmission
  MOSI transmits concurrently with MISO
Internal shift register may be used to hold both transmitted and received data
  Shift in a received bit, shift out a transmitted bit

## Slide 39: Clock Polarity and Phase
Slides created by:
Professor Ian G. Harris
Clock polarity and phase determine when data is made valid wrt the clock
  Polarity = 0 or 1, Phase = 0 or 1
Data is valid on each clk rising edge or each clk falling edge
Data valid edge (V) = PHASE XOR POLARITY
  Polarity = 0, Phase = 0: Rising edge sampling
  Polarity = 1, Phase = 1: Rising edge sampling
  Polarity = 0, Phase = 1: Falling edge sampling
  Polarity = 1, Phase = 0: Falling edge sampling

## Slide 40: SPI Timing Diagrams
Slides created by:
Professor Ian G. Harris
bit1
bit2
bit3
SCLK
MOSI
SS’/CS’
bit1
bit2
bit3
SCLK
MOSI
SS’/CS’
Polarity, Phase = 0, 0 or 1, 1
Polarity, Phase = 0, 1 or 1, 0

## Slide 41: Multiple Independent Slaves
Slides created by:
Professor Ian G. Harris
Need a unique SS’ for each slave
Slave
MOSI
MISO
SCLK
SS1’
SS2’
SS3’
MOSI
MISO
SCLK
CS’
Master
MOSI
MISO
SCLK
CS’
MOSI
MISO
SCLK
CS’

## Slide 42: SPI on the ATmega
Slides created by:
Professor Ian G. Harris
Only one SS’ line
SPDR
  Reading accesses last received transmission
  Writing automatically sends a the data
Do not directly access the SPI pins
  Handled in hardware