## Slide 1: SPI on the ATmega
Slides created by:
Professor Ian G. Harris
SS’ line only used in Slave mode
SPDR
  Reading accesses last received transmission
  Writing automatically sends a the data
Do not directly access SPI pins
  Handled in hardware
  Except CS’, as Master

## Slide 2: SPI Pins on the ATmega
Slides created by:
Professor Ian G. Harris
MISO, MOSI, and SCK are not explicitly accessed
  HW handles pin access when SPDR is read/written
  However, program must set directions on these pins
SS’ enables SPI in Slave mode

## Slide 3: SPI Registers
Slides created by:
Professor Ian G. Harris
SPCR - SPI Control Register
  Bit 7 - SPIE: SPI Interrupt Enable
  Bit 6 - SPE: SPI Enable
  Bit 5 - DORD: Data Order (1 = LSB)
  Bit 4 - MSTR: Master/Slave Select (1 = master)
  Bit 3 - CPOL: Clock Polarity
  Bit 2 - CPHA: Clock Phase
  Bits 1,0 – SPR1,SPR0: SPI Clock Rate Select

## Slide 4: SPI Registers
Slides created by:
Professor Ian G. Harris
SPSR - SPI Status Register
  Bit 7 - SPIF: SPI Interrupt Flag
  Bit 6 - WCOL: Write Collision Flag
  Bit 5:1 - Reserved
  Bit 0: SPI2X: Double SPI Speed Bit

## Slide 5: SPI Clock Speed
Slides created by:
Professor Ian G. Harris
Determines SCLK as a function of fosc
SPSR
Bit 0
SPCR
Bit 1
SPCR
Bit 0

## Slide 6: SPI Master Example
Slides created by:
Professor Ian G. Harris
void SPI_MasterInit(void)
{
// Set MOSI and SCK output, all others input
DDRB = (1<<DDB2)|(1<<DDB1);
// Enable SPI, Master, set clock rate fosc/16
SPCR = (1<<SPE)|(1<<MSTR)|(1<<SPR0);
}
void SPI_MasterTransmit(char cData)
{
/* Start transmission */
SPDR = cData;
/* Wait for transmission complete */
while(!(SPSR & (1<<SPIF)));
}

## Slide 7: SPI Slave Example
Slides created by:
Professor Ian G. Harris
void SPI_SlaveInit(void)
{
// Set MISO output, all others input
DDRB = (1<<DDB3);
// Enable SPI
SPCR = (1<<SPE);
}
char SPI_SlaveReceive(void)
{
// Wait for reception complete
while(!(SPSR & (1<<SPIF)));
// Return Data Register
return SPDR;
}

## Slide 8: I2C Protocol
Slides created by:
Professor Ian G. Harris
Synchronous, serial protocol
Multiple masters, multiple slaves
Bitwidth is fixed, independent of number of slaves
Two wires: SDA (serial data) and SCL (serial clock)
Both lines are open-drain
  Pulled up to high by default
  State of bus is always known

## Slide 9: I2C Terminology
Slides created by:
Professor Ian G. Harris
Master – Initiates and terminates transmission. Generates SCL.
Slave – Addressed by the Master
Transmitter – Placing data on the bus
Receiver – Reading data from the bus

## Slide 10: I2C Network
Slides created by:
Professor Ian G. Harris
SDA and SCL are bidirectional
  Unlike SPI
Master
Slave
Master
Slave
Slave
SCL
SDA
Vcc
Vcc

## Slide 11: I2C Transaction Structure
Slides created by:
Professor Ian G. Harris
Start Condition
  Indicates the beginning of a transaction
Address/Direction Byte
  Specifies slave for communication
  Specifies read vs. write transaction
Data Byte(s)
  Transmitted by either master or slave
Stop Condition
  Indicates the end of a transaction

## Slide 12: Start and Stop Conditions
Slides created by:
Professor Ian G. Harris
Start Condition
  Falling transition on SDA while SCL=1
Stop Condition
  Rising transition on SDA while SCL=1
SDA
SCL
Start Condition
SDA
SCL
Stop Condition

## Slide 13: Sending a Bit
Slides created by:
Professor Ian G. Harris
SDA is sampled by receiver on the rising edge of SCL
SDA must be constant which SCL is high
  Exception is Start/Stop Condition
SDA
SCL

## Slide 14: Acknowledge Bit
Slides created by:
Professor Ian G. Harris
After each byte is sent, the receiver must acknowledge
Transmitter releases SDA, receiver must pull SDA low
  Must be low for one pulse of SCL
If SDA is not pulled low, transmission is aborted
SDA
SCL
1
2
3
8
ACK

## Slide 15: Typical I2C Packet
Slides created by:
Professor Ian G. Harris
Each slave has an unique 7-bit address
Direction Bit: 0 indicates write, 1 indicated read
ACK bit after each byte
Data (8 bits)
Address (7 bits)
Direction
Bit
ACK
ACK
Start
Stop

## Slide 16: I2C on ATmega
Slides created by:
Professor Ian G. Harris
Two Wire Interface (TWI) is their name for it
Supports options which we will not consider
  10 bit addressing
  Multi-master arbitration
Packet format is the same
Data sent MSB first

## Slide 17: TWI Module on ATmega
Slides created by:
Professor Ian G. Harris

## Slide 18: Bit Rate Generator Unit
Slides created by:
Professor Ian G. Harris
Generates the clock on SCL
Used only if acting as a Master
Controlled by two registers:
  TWI Bit Rate Register (TWBR)
  Prescalar bits in the TWI Status Register (TWSR)
fSCL = fosc / [16 + 2 (TWBR) * 4 TWPS]
fosc in slave >= 16 * fSCL

## Slide 19: Bus Interface Unit
Slides created by:
Professor Ian G. Harris
TWI Address/Data Register (TWDR)
  Contains the byte to send, of the byte received
START/STOP Controller
  Not directly accessed by programmer
ACK/NACK Bit Register
  Not directly accessed by programmer
Bus Arbitration Logic
  Not directly accessed by programmer

## Slide 20: Address Match Unit
Slides created by:
Professor Ian G. Harris
TWI Address Register (TWAR)
  Contains the address of this device (in slave mode)
Incoming address (in TWDR) is compared to TWAR
TWI General Call Recognition Enable (TWGCRE)
  Bit in TWAR which indicates that general call address (0000000) should be recognized
General call recognition allows broadcasts

## Slide 21: Control Unit
Slides created by:
Professor Ian G. Harris
TWI Control Register (TWCR)
  Used to set various I2C communication options
TWCR contains TWI Interrupt Flag (TWINT)
TWINT is set when an interesting TWI event occurs
  Transmit START condition
  Transmit address
  Receive data byte
TWI Status Register (TWSR)
  Contains status byte after TWINT is set

## Slide 22: Controlling TWI
Slides created by:
Professor Ian G. Harris
Each transaction is divided into stages (“bus cycles”)
  Cycles for a Write Transaction:
  1. Send START, 2. Send Address, 3. Send Byte, 4. Send STOP
TWINT is automatically set and at the end of each stage
  TWSR is also loaded with status of the cycle
Clearing TWINT is required to trigger the next bus cycle
TWINT is cleared by setting TWCR bit to 1

## Slide 23: Write Transaction Example
Slides created by:
Professor Ian G. Harris
Step 1: Send a START Condition
TWEN bit enables TWI logic
TWSTA bit indicates START condition is next cycle
TWINT = 1 clears flag, initiating bus cycle
void SendStart() {
TWCR = (1<<TWINT)|(1<<TWSTA)|(1<<TWEN);
}
SendStart();

## Slide 24: Write Transaction Example
Slides created by:
Professor Ian G. Harris
Step 1.5: Wait for START to be sent, check result
While statement waits for completion of START
TWSR, high 5 bits, should contain START (0x08) to indicate correct transmission
void VerifyStatus(char code) {
while (!(TWCR & (1<<TWINT)));
if ((TWSR & 0xF8) != code) ERROR();
}
VerifyStatus (START);

## Slide 25: Write Transaction Example
Slides created by:
Professor Ian G. Harris
Step 2: Send Address
SLA_W is the slave address + direction bit
Since TWSTA is not set, TWDR will be transmitted
void SendByte (char data) {
TWDR = data;
TWCR = (1<<TWINT) | (1<<TWEN);
}
SendByte (SLA_W);

## Slide 26: Write Transaction Example
Slides created by:
Professor Ian G. Harris
Step 2.5: Wait for Address to be sent, check result
MT_SLA_ACK indicates that ACK was received
VerifyStatus(MT_SLA_ACK);

## Slide 27: Write Transaction Example
Slides created by:
Professor Ian G. Harris
Step 3: Send Data, Wait for completion, Check result
SendByte(DATA);
VerifyStatus(MT_DATA_ACK);

## Slide 28: Write Transaction Example
Slides created by:
Professor Ian G. Harris
Step 4: Send STOP Condition
void SendStop() {
TWCR = (1<<TWINT)|(1<<TWSTO)|(1<<TWEN);
}
SendStop();

## Slide 29: TWI Interrupts
Slides created by:
Professor Ian G. Harris
Example used while loops to wait for cycle completion
TWINT is set at the end of each cycle
Could have used interrupts to execute each stage
No need to waste processor time waiting

## Slide 30: I2C System Example
Slides created by:
Professor Ian G. Harris
Philips PCF8570
256 x 8-bit static low-voltage RAM with I2C-bus interface
Interface with a RAM IC

## Slide 31: Memory IC Wiring
Slides created by:
Professor Ian G. Harris
Address inputs are low bits of the address
High address bits are fixed
SDA, SCL attached to ATmega 2560 pins
Symbol | Pin | Description
A0 | 1 | Address In 0
A1 | 2 | Address In 1
A2 | 3 | Address In 2
Vss | 4 | Negative supply
SDA | 5 | Serial data
SCL | 6 | Serial clock
TEST | 7 | Tied to Vss
Vdd | 8 | Positive Supply

## Slide 32: Memory Timing Diagrams
Slides created by:
Professor Ian G. Harris
Timing diagrams are provided for transactions
Need to write code to match the timing diagrams
WRITE transaction, Master Transmitter, Slave Receiver

## Slide 33: Write Transaction
Slides created by:
Professor Ian G. Harris
void WriteMTSR (char s_addr, char m_addr, char data) {
SendStart();
VerifyStatus(START);
SendByte(s_addr);
VerifyStatus(MT_SLA_ACK);
SendByte(m_addr);
VerifyStatus(MT_DATA_ACK);
SendByte(data);
VerifyStatus(MT_DATA_ACK);
SendStop();
}
WriteMTSR(SLA_ADDR, MEM_ADDR, DATA);

## Slide 34: Analog to Digital Conversion (ADC)
Slides created by:
Professor Ian G. Harris
Converts an analog voltage to a digital value
Maps input voltage range of digital values
  Ex. 0V – 5V -> 0x00 – 0xFF
Allows the digital mC to use analog data
  Can read analog sensors
Commonly built into mControllers
ATmega 2560 ADC has 10-bit accuracy
  Digital value range 0 – 1023

## Slide 35: Starting a Single Conversion
Slides created by:
Professor Ian G. Harris
Set the AD Start Conversion (ADSC) bit in the AD Control and Status Register A (ADCSRA)
ADSC stays high as long as conversion is being performed
ADSC is cleared by HW when conversion is done
  Use this to check for conversion completion

## Slide 36: Auto Triggering
Slides created by:
Professor Ian G. Harris
May want to trigger conversion based on some event
  Previous conversion completed
  External interrupt
  Timer interrupt
Set AD Auto Trigger Enable (ADATE) bit in ADCSRB register
Set AD Trigger Select (ADTS) bits to select trigger

## Slide 37: Auto Trigger Logic
Slides created by:
Professor Ian G. Harris
AD Interrupt Flag (ADIF) enables “Free Running” mode

## Slide 38: ADC Clock Generation
Slides created by:
Professor Ian G. Harris
AD Prescalar Select (ADPS) bits in ADCSRA
50kHz – 200kHz is needed (up to 1000kHz)
Fast ADC clock – low conversion time, less accuracy
Slow ADC clock – high conversion time, more accuracy

## Slide 39: Channel/Reference Selection
Slides created by:
Professor Ian G. Harris
Analog source can be any pin from PortF or PortK
Source channel selected by MUXn bits in ADMUX register
Reference voltage can be Vcc, 2.56V, 1.1V
Reference selected by REFS bits in ADMUX
Changes during a conversion take effect after the conversion

## Slide 40: ADC Conversion Result
Slides created by:
Professor Ian G. Harris
Result is contained in ADCL and ADCH registers
  10-bits contained in 2 registers, 6 bits ignored
ADLAR bit in ADMUX determines left (right) adjust
  Left adjust – ignore low 6 bits of ADCL
  Right adjust – ignore high 6 bits of ADCH
If 8-bit accuracy is enough, choose left adjust and ignore ADCL