## Slide 1: ATmega System Reset
Slides created by:
Professor Ian G. Harris
All I/O registers are set to initial values
  PORT registers set to 0
  DDR registers set to 0 (inputs)
Program execution set to the Reset Vector
  Reset vector can point to regular program
Internal reset is stretched using a counter
  Allows power to become stable

## Slide 2: Reset Sources
Slides created by:
Professor Ian G. Harris
Power-on Reset - Triggered when voltage is below power-on reset threshold
External Reset - Triggered on the RESET’ pin
Watchdog reset - Triggered when watchdog timer expires
Brown-out Reset - Triggered when voltage is below brown-out threshold
JTAG AVR Reset - Triggered if there is a 1 in the JTAG Reset Register

## Slide 3: MCUSR
Slides created by:
Professor Ian G. Harris
Bit 4 – JTRF: JTAG Reset Flag
Bit 3 – WDRF: Watchdog Reset Flag
Bit 2 – BORF: Brown-out Reset Flag
Bit 1 – EXTRF: External Reset Flag
Bit 0 – PORF: Power-on Reset Flag
Indicates which reset has occurred
Must be cleared in Reset function

## Slide 4: Watchdog Timer
Slides created by:
Professor Ian G. Harris
Special-purpose timer
Has its own, slower clock source
Can set prescalar but not start value
Time out from 16ms to 8s
Interrupt mode
  Can wake device from low power mode
System Reset Mode
  Resets ATmega when it expires

## Slide 5: Watchdog Failsafe
Slides created by:
Professor Ian G. Harris
Embedded software can erroneously enter an infinite loop
  Waiting for an event that never happens
Watchdog expiration pulls the program out of an infinite loop
Watchdog must be reset regularly in correct program
WDR instruction resets timer
Use wdt_reset() macro in avr libc

## Slide 6: Watchdog Reset Logic
Slides created by:
Professor Ian G. Harris
WDE is Watchdog Enable
WDIE is Watchdog Interrupt Enable
WDIF is Watchdog Interrupt Flag
Resets cannot be enabled if interrupts are enabled

## Slide 7: Watchdog Register
Slides created by:
Professor Ian G. Harris
WDIF - Watchdog Interrupt Flag
WDIE - Watchdog Interrupt Enable
WDCE - Watchdog Change Enable
  Allows prescalar and WDE to be changed
WDE - Watchdog Enable
WDP3:0 - Watchdog Timer Prescalar

## Slide 8: ATmega Clock Distribution
Slides created by:
Professor Ian G. Harris
Several clocks and clock sources
System Clock Prescalar slows clocks
Several options set by fuses, not regs

## Slide 9: ATmega Clock Generation
Slides created by:
Professor Ian G. Harris
Several different clock are generated on chip
Clkasy - Drives asynchronous timer (in sleep modes)
ClkI/O - Drives SPI, USART, I2C
ClkADC - Drives ADC
ClkCPU -Drives main processor
ClkFlash - Drives FLASH memory

## Slide 10: Clock Prescalar
Slides created by:
Professor Ian G. Harris
Bit 7 – CLKPCE: Clock Prescaler Change Enable
Bits 3:0 – CLKPS3:0: Clock Prescaler Select Bits 3-0
CLKPR

## Slide 11: ATmega Clock Sources
Slides created by:
Professor Ian G. Harris
Different clock sources selected using fuses
Default clock is internal RC clock, 8MHz
  Clock div set to 8, producing 1MHz clock

## Slide 12: Crystal Oscillators
Slides created by:
Professor Ian G. Harris
Crystal of piezoelectric material which vibrates at a precise frequency
Connected externally to the ATmega

## Slide 13: RC Oscillators
Slides created by:
Professor Ian G. Harris
RC circuits designed to oscillate at a given frequency
Convenient, easy to build
Susceptible to temperature and process variation
ATmega has 128KHz and 8MHz RC oscillators

## Slide 14: Power Management
Slides created by:
Professor Ian G. Harris
Dynamic power - consumed when transistors switch state
Static (Leakage) power - consumed whenever a device receives power, independent of switching
Low power modes shut off clocks, eliminating dynamic power consumption
Components can be completely shut down to eliminate static power

## Slide 15: Low Power Modes
Slides created by:
Professor Ian G. Harris
Power-down - Only asynchronous devices operational
Standby - Clock source operational. Only 6 cycles to return to normal power state

## Slide 16: Sleep Mode Control Register
Slides created by:
Professor Ian G. Harris
Bit 0 - SE – Sleep Enable
Bits 3:1 - SM? – Sleep mode select

## Slide 17: Wakeup Sources
Slides created by:
Professor Ian G. Harris
INT 7:4 - only level interrupt
TWI Address - on receipt of message
Wakeup delays vary (i.e. standby vs. power-down)

## Slide 18: Disabling Devices
Slides created by:
Professor Ian G. Harris
Additional power can be saved by disabling peripherals
Power Reduction Register
Bit 7 - PRTWI: Power Reduction TWI
Bit 6 - PRTIM2: Power Reduction Timer/Counter2
Bit 5 - PRTIM0: Power Reduction Timer/Counter0
Bit 3 - PRTIM1: Power Reduction Timer/Counter1
Bit 2 - PRSPI: Power Reduction Serial Peripheral Interface
Bit 1 - PRUSART0: Power Reduction USART0
Bit 0 - PRADC: Power Reduction ADC

## Slide 19: Security in Embedded Systems
Cybersecurity is clearly important today
Embedded systems are a new frontier for attackers
  Many devices are networked
  ES companies do not know security
Traditional defenses may not work on embedded systems
  Ex. No ES Anti-Virus (maybe for cell phones)
Hardware is a current trend in security circles
  Arduino helps with this

## Slide 20: Common Attack Goals
Slides created by:
Professor Ian G. Harris
Confidence Scams – Traditional scams performed via computer
Information Theft – Stealing valuable information
Denial of Service (DoS) – Shutting down a network-based service
Causing Physical Events – Embedded control systems
Co-opting CPU Resources – Executing code on another machine

## Slide 21: Points of Attack
Slides created by:
Professor Ian G. Harris
Internet
User
Local
Computer
Network
Server
All four elements can be targeted by attacks

## Slide 22: Confidence Scams: Phishing
Slides created by:
Professor Ian G. Harris
Exploiting vulnerabilities in the user, not the network or device
  Traditional scams using the computer (and/or the phone) as a vehicle
  People trust official looking emails and websites
  Often used to gain information for larger attacks
Internet
User
Local
Computer
Network
Server

## Slide 23: Phishing Examples
Slides created by:
Professor Ian G. Harris
Examples:
  “Dear Honorable Sir, I need to transfer $10,000,000,000 to your account”
    Required to pay a “small” transfer fee
    This actually works “Oregon Woman Loses $400,000 to Nigerian E-Mail Scam” AP, 11/18/08
  “You need to update your Paypal account …”
    Directed to send personal information
  Call computer support and masquerade as a technician
    “Where is that TFTP server located again?”

## Slide 24: Spoofing
Slides created by:
Professor Ian G. Harris
Making a fake version of something in order to trick a user
Often used as part of a phishing scam
Example:
  You get an email saying something is wrong with your ebay account.
  It provides a link to a website www.ebayaccounts.com
  The website is fake but can look completely real
Can be done with email addresses and calling trees

## Slide 25: Preventing Phishing
Slides created by:
Professor Ian G. Harris
Don’t trust anyone or any information that you can’t verify
  Don’t give critical info to unverified websites/phone numbers
2. Don’t accept anything (i.e. programs) from unverified sources
This may be inconvenient
  1. If Citibank calls, call them back at a known number
  2. Can’t purchase online from unknown vendors
  3. Be careful about freeware/shareware

## Slide 26: Information Theft
Slides created by:
Professor Ian G. Harris
Stealing data from a computer or the network
Targets local computer, server, and network
Internet
User
Local
Computer
Network
Server

## Slide 27: Information Theft
Slides created by:
Professor Ian G. Harris
Stealing data on your computer or on the network
Identity theft - Get social security #, home address, passwords, etc.
  Credit cards, loans in your name
  This happens to individuals
Corporate theft - Get information from organizations and steal their money
  “Russian hackers stole Cape Cod Town’s money”
AP, 11/26/08
  “Hundreds of Stolen Data Dumps Found”
WashingtonPost.com, 12/22/08

## Slide 28: Other Information Theft
Slides created by:
Professor Ian G. Harris
Eavesdropping on Voice Over IP (VOIP) phone calls
  VOIP data sent over the internet
Stalking/Cyberstalking
  Find a home address, school, etc.
International Spying
  “China trying to crack U.S. computers, buy nukes”
cnn.com, 3/3/08

## Slide 29: Preventing Information Theft
Slides created by:
Professor Ian G. Harris
Use encryption as much as possible
Encrypted Communications
Website addresses starting with “https:” - automatic
Virtual Private Networks (VPN) – mostly automatic
Pretty Good Privacy (PGP) – manual interaction
Whole Disk Encryption
Protects data on your computer
Slows down your machine significantly
Servers are out of your control
You can only complain/sue

## Slide 30: Denial of Service (DoS)
Slides created by:
Professor Ian G. Harris
Attempt to shut down a network-based service
Only happens to servers (unless your machine is a server)
Internet
User
Local
Computer
Network
Server

## Slide 31: Typical DoS Attacks
Slides created by:
Professor Ian G. Harris
  May be applied to any server
    Webserver, bank, course registration, etc.
  Might be a protest of some kind
“Estonia recovers from massive denial-of-service attack”
IDG News Service , 05/17/2007
  Might be tactical warfare
“Before the Gunfire, Cyberattacks ”
8/12/08
    Site of Georgia’s president taken offline

## Slide 32: Execution of DoS Attacks
Slides created by:
Professor Ian G. Harris
Simply deluge a server with requests
- Requires many machines to do this
Exploit a bug in the server software
- Software always has many bugs
- Can be exploited if it can be triggered remotely
- Ex. VOIP phone crashes when if a call is ended at the wrong time

## Slide 33: Preventing DoS Attacks
Slides created by:
Professor Ian G. Harris
Not much a user can do
- This is a server problem
Servers use network-based intrusion detection
- Check network activity for suspicious patterns
- Block suspicious traffic

## Slide 34: Causing Physical Events
Slides created by:
Professor Ian G. Harris
Internet
User
Local
Computer
Network
Server
> Attack a computer which controls physical devices
- Building heating/cooling control, power grid control, etc.
> Server problem, but you may have a server
- Wifi printer, home automation, nannycam, etc.

## Slide 35: Cyber-Physical Attacks
Slides created by:
Professor Ian G. Harris
Vulnerabilities have been found in wireless medical devices
Daniel Halperin, Thomas S. Heydt-Benjamin, Benjamin Ransford, et al. “Pacemakers and Implantable Cardiac Defibrillators: Software Radio Attacks and Zero-Power Defenses,” May 2008, www.secure-medicine.org/icd-study/icd-study.pdf
Embedded Cyber-Physical Systems
- Special purpose computers with a simple interface
- Directly interact with the physical world
- Ex. Building control, wifi printer, cars, etc.

## Slide 36: Preventing Cyber-Physical Attacks
Slides created by:
Professor Ian G. Harris
User cannot do much, must trust the manufacturer
- Users cannot generally modify embedded devices
Large-scale cyber-physical systems need to be well protected
- Use firewalls, anti-virus, network-based intrusion detection, and physical security measures

## Slide 37: Co-opting CPU Resouces
Slides created by:
Professor Ian G. Harris
Internet
User
Local
Computer
Network
Server
Taking over a computer, forcing it to do your bidding
Can occur to any machine, but home machines are most vulnerable

## Slide 38: Malware
Slides created by:
Professor Ian G. Harris
Complete takeover of a machine requires the ability to execute arbitrary code on that machine
Malware – Generic term for malicious code that runs on a machine without permission
Typical malware functions:
- Steal critical data and send it back to a central repository
- Make a machine unbootable
- Force the machine to act as a zombie in a botnet
> botnet is used to perform larger attacks, spam, etc.

## Slide 39: Basic Malware Functions
Slides created by:
Professor Ian G. Harris
Need to know this in order to understand defenses
1. Gets into the memory of your computer
2. Tricks your computer into executing it
3. Hides itself
4. Spreads itself to other machines

## Slide 40: Getting Into Your Computer
Slides created by:
Professor Ian G. Harris
User-driven - User allows the malware in
  Read your email
  Click on an attachment
  Click on a website link
  File transfer (ftp)
Background traffic - Many programs communicate on the network in the background
  Email, skype, automatic updates, etc.

## Slide 41: Executing on Your Machine
Slides created by:
Professor Ian G. Harris
How can foreign programs run on my computer?
User Gives Permission
  “Do you want to enable this macro?”
  Bad default settings, (ex. Automatically enable all macros)
  These vulnerabilities can be fixed fairly easily
Software Vulnerability
  A networked application has a coding flaw which allows unauthorized code execution

## Slide 42: Rootkits
Slides created by:
Professor Ian G. Harris
A rootkit is a program that uses stealth
- Sneaks onto your machine without you knowing
- Hides itself on your machine so that is can’t be removed
Rootkits change components of the operating system to hide their presence
Example of stealth
- A rootkit may attach itself to a good executable
- Detected by examining properties of the executable (i.e. size)
- Checking properties is a call to an OS program
- Rootkit may change the “check properties” program to print the
original size
Most malware is fundamentally a specialized rootkit

## Slide 43: Malware Propagation/Spread
Slides created by:
Professor Ian G. Harris
Trojan Horse - Malware which is part of another program which the user believes is safe
  Spread occurs when the user installs the “safe” program
  Social engineering may be involved
Virus - Malware which is part of a larger program or file
  Ex. Macro in an .xls spreadsheet
  Self-replicates by inserting itself into new programs/files
Worm - Malware which is not attached to another program/file
  Self-replicates over the network

## Slide 44: Stopping Malware
Slides created by:
Professor Ian G. Harris
Keep you software updates current
Malware is often enabled by a bug in a networked application
  Internet Explorer, Skype phone, Adobe Acrobat, World of Warcraft, etc.
Patches often fix known vulnerabilities

## Slide 45: Stopping Malware
Slides created by:
Professor Ian G. Harris
Use a firewall to stop malware from entering your machine initially
- Firewall blocks incoming/outgoing network traffic
- Could block the traffic which delivers the malware
Problem: Firewalls only look at the message header, not the content
- Header contains message routing info
- Malware may be contained in the content
Problem: Firewalls are a blunt instrument
- Block all messages from a particular address or application
- Easy to block too much or too little

## Slide 46: Stopping Malware
Slides created by:
Professor Ian G. Harris
Use anti-virus programs to detect malware in your memory or on your disk
- Anti-virus will scan all files for known malware
- Will flag suspicious behavior to detect unknown malware
Problem: Scans may miss unknown malware
  Keep anti-virus signatures up-to-date
Problem: May produce annoying false alarms
  Behavior may look suspicious but be OK

## Slide 47: Embedded System Security
Slides created by:
Professor Ian G. Harris
May store important information
  Health information (medical devices)
  Personal information (cell phones)
  Copyrighted information (movies, music)
May control life-critical/cost-critical devices
  Human bodies (medical devices)
  ATMs
  Anti-lock braking systems

## Slide 48: Attack Goals
Slides created by:
Professor Ian G. Harris
Steal information from the device
  Personal data, passwords, copyrighted data
Denial of Service (DoS)
  Shut down your device (malicious or prank)
Eavesdrop on the device
  Stealing communications
Change the behavior
  Jailbreaking an iphone
  Include in a botnet

## Slide 49: How Are They Attacked?
Slides created by:
Professor Ian G. Harris
Many embedded systems are networked
  Wifi, ethernet, bluetooth, Irda, etc.
Direct physical access via I/O
  USB
  Memory cards (SD cards, etc.)
  App. Specific protocols (VGA, “private” protocols)
Device may be opened
  Inter-IC protocols (I2C, SPI, etc.)
  IC-specific interfaces

## Slide 50: Methods of Attack, Remote
Slides created by:
Professor Ian G. Harris
Remote attacks
Attacker does not need to be in close proximity to the device
Vast majority of attacks are remote
Remote attacks are launched via a network (internet)
Either wired (ethernet) or wireless (802.11?)
Bluetooth/IrDA possible, shorter range

## Slide 51: Methods of Attack, Remote
Slides created by:
Professor Ian G. Harris
Network
Apps.
OS
Internet Msgs.
HW
Attacker
Attacker manipulates the device using TCP/IP messages
Bugs in Networked Applications allow messages to impact device behavior

## Slide 52: Buffer Overflow Example
Slides created by:
Professor Ian G. Harris
User input copied into buff without checking length
Could come from the network as well
int foo(int argc, char *argv[]) {
int i = 0;
char buff[128];
char *arg1 = argv[1];
while (arg1[I] != ‘\0’) {
buff[I] = arg1[I];
I++;
}
buff[I] = ‘\0’;
printf(“buff = %s\n”, buff);
}

## Slide 53: Smashing the Stack
Slides created by:
Professor Ian G. Harris
Buffer overflow allows malicious code to be written onto the stack
Overflowing local var can corrupt the return address
Return address can point to malicious code
Stack frame
Stack
local
frame
return
low address
high address
main
foo
local
frame
return
local
frame
return

## Slide 54: Defenses Against Remote Attacks
Slides created by:
Professor Ian G. Harris
Update software regularly
  Updates are not common with embedded systems
Network Intrustion Detection (NIDS)
  Maybe if deep packet inspection is used
Anti-virus, Firewall, NIDS
  Embedded systems do not have sufficient computational power