## Slide 1: CAM: Constraint-aware Application Mapping for Embedded Systems
Luis A. Bathen, Nikil D. Dutt

## Slide 2: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
Customized Security Policy Generation
Related Work
Conclusion

## Slide 3: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
Customized Security Policy Generation
Related Work
Conclusion

## Slide 4: Software/Hardware Co-Design
Given an existing applications, designers can
  Design a customized platform
    Dedicated logic
    Custom memory hierarchy / communication architecture
  Take an existing platform and efficiently map the application on it
    Data allocation and Task mapping
  Start with an existing platform and customize it to satisfy the requirements
    Add custom blocks, and reuse components
Application
Mapping
Process
AMBA 2.0
Image/
Bitstream
CPU
Tier2
DC_LS, MCT, …
DWT w/iDMA
Controller/
Scheduler
Data
Dispatcher
Data
FIFO
Data
Collector
BPC/BAC
Data
FIFO
Data
FIFO
BPC/BAC
Data
FIFO
Data
FIFO
BPC/BAC
Data
FIFO
A
B
DWT w/iDMA
Controller/
Scheduler
Data
Dispatcher
Data
FIFO
Data
Collector
BPC/BAC
Data
FIFO
Data
FIFO
BPC/BAC
Data
FIFO
Data
FIFO
BPC/BAC
Data
FIFO
A
B
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
DWT w/iDMA
Data
Dispatcher
Data
FIFO
Data
Collector
BPC/BAC
Data
FIFO
Data
FIFO
BPC/BAC
Data
FIFO
Data
FIFO
BPC/BAC
Data
FIFO
A
B
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
In this presentation we will focus on the application mapping process on CMPs

## Slide 5: Target Platforms (Chip Multiprocessors)
SPM
I$
CPU
SPM
I$
CPU
SPM
I$
CPU
SPM
I$
CPU
RAM
DMA
Multiple low power RISC cores
DMA and SPM Support
Well suited for applications with high levels of parallelism
Bus based systems – still most commonly used
Notes: CMPs can have both spms and caches, with more complex memory hierarchies

## Slide 6: Motivation
Platform Definition
Define Task Mapping and Schedule
Apply loop optimizations
Define Data Placement
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
T1
T2.1
T4
T3
T2.2
C/C++
CPU1
CPU2
Simulate/Verify
T5
T1
T2
T3
T4
T5
T1
T2.1
T2.2
T3
T4
T5
Task 1 Data Sets
Task 2.1 Data Sets
Task 3 Data Sets
Time
Size
Task 2.2 Data Sets
e.g. iteration partitioning, unrolling, tiling…
Generate input task graph to scheduler
What do we care about? energy, performance?
The whole process depends on the available resources
ISS, CMP ISS?
Typical Mapping Process

## Slide 7: Motivation (Cont.)
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
T1
T3
T4f
T5
T1
T2.1
T4
T3
T2.2
CPU1
CPU2
T5
T2.3
T2.4
CPU3
CPU4
Time
Size
Platform Definition
Define Task Mapping and Schedule
Apply loop optimizations
Define Data Placement
Simulate/Verify
This dependence shows the need to evaluate different optimizations, schedules, placements for power and performance in a quick yet accurate fashion

## Slide 8: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
Customized Security Policy Generation
Related Work
Conclusion

## Slide 9: CAM: Constraint-aware Application Mapping for Embedded Systems
Power
Data partitioning and distribution
Performance
Task/kernel partitioning
Security
Policy Generation
Macro-pipelining
Data reuse
Memory-aware Scheduling
Selective Enforcement
Early Execution Edges
Application
C/C++
Data Placement/Schedule/Policies
Fully utilize compute resources
Increased Parallelism
Increased vulnerabilities
Efficiently utilize memory resources
Voltage/Frequency scaling affect performance
Limits type of security mechanisms
Very secure might mean very power hungry/slow
Limited multiprocessor support
Solutions are generic

## Slide 10: CAM Overview
Front End
Application Pre-processing
(CFG extraction, task graph generation, input model generation)
Middle End
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
Task Decomposition
Define CMP
Template
Early Execution Edge Generation
C1
K2
K3
C4
K5
C6
Task1
Task2
Task Graph Augmentation
Memory-Aware Macro-Pipelining
C1
K2
K3
C6
C4
K5
CPU1
CPU2
CPU3
SPM1
SPM2
K2D
K3D
K5D
Back End
Performance
Model
Generation
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
Meet Energy and Performance Constraints?
Data Reuse Analysis
Nope, let’s see if increasing degree of unrolling (in loops) helps, tile size?
End up with massive task graphs
Very tightly coupled process!

## Slide 11: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
  ESTImedia ‘08, ’09
Customized Security Policy Generation
Related Work
Conclusion

## Slide 12: Application Domain Example (JPEG2000)
t1
t2
tn
tm
tmn
t1
t2
t3
tmn
DWT
Quant.
EBCOT
DWT
Quant.
EBCOT
DWT
Quant.
EBCOT
DWT
Quant.
EBCOT
Task Set (T)
Supports multiple levels
of data parallelism

## Slide 13: Inter-kernel Reuse Opportunities
We target our approach to data intensive
streaming applications
  Task level parallelism, Data level parallelism
Examples
  Macroblock level (H.264)
  Component level, Tile level, Code block level (JPEG2000)
void dcls()
{
// input: B,G, R
// output: B,G, R
for ( i = 0; i < width; i++) {
for ( j = 0; j < height; j++) {
B[i][j] = B[i][j]
- pow(2, info->siz - 1);
G[i][j] = B[i][j]
- pow(2, info->siz - 1);
R[i][j] = B[i][j]
- pow(2, info->siz - 1);
}
}
}
void mct()
{
// input: B,G, R
// output: Yr, Ur, Vr
for ( i = 0; i < width; i++) {
for ( j = 0; j < height; j++) {
Yr[i][j] =
ceil((float)(R[i][j] + (2*(G[i][j])) +
B[i][j])/4);
Ur[i][j] = B[i][j] - G[i][j];
Vr[i][j] = R[i][j] - G[i][j];
}
}
}
void tiling()
{
// input: Yr, Ur, Vr
// output: n x tY, tV, tU
for( i=0; i<m; i+=tw) {
for( j=0; j<n; j+=th) {
for( k=0; k<tw; k++) {
for( l=0; l<th; l++) {
tY[k][l] = Yr[i+k][j+l];
tU[k][l] = Ur[i+k][j+l];
tV[k][l] = Vr[i+k][j+l];
}
}
yCoeff=dwt(tY);
yQ=quant(yCoeff);
ebcot(yQ);
………………
……………...
Inter-kernel data reuse opportunities are often ignored
Cache based systems are not suitable to meet these types of applications
Notes: Standard approaches look only at intra reuse, disregarding inter-kernel reuse opportunities, here data is propagated through a series of kernels.

## Slide 14: Access Patterns and Data Requirements
Task/Kernel Data Requirements:
  DCLS: Consumption=Production=3MB
  MCT: Same as DCLS, 3MB
  Tiling:
    Consumption = same as MCT, Production: 3 tiles at a time, 128x128 pixels (16KB), total of 16 x 3 tiles
The Problem:
Data is read in, and written out by each task. Cannot keep ALL data in SPM, and pass it to the next task.
Our proposal: Take kernels that produce large data streams and decompose them into smaller kernels producing smaller data streams
Address
Iteration

## Slide 15: Task Decomposition Through Transformations
Idea:
  Decompose each task into a series of kernels and compute nodes (non-kernels)
  Each kernel will ideally operate over a smaller set of data than the task itself
void dcls()
{
// input: B,G, R
// output: B,G, R
for ( i = 0; i < width; i++) {
for ( j = 0; j < height; j++) {
B[i][j] = B[i][j]
- pow(2, info->siz - 1);
G[i][j] = B[i][j]
- pow(2, info->siz - 1);
R[i][j] = B[i][j]
- pow(2, info->siz - 1);
}
}
}
void dcls()
{
for ( i = 0; i < width; i++) {
for ( j = 0; j < height; j++) {
B[i][j] = B[i][j]
- pow(2, info->siz - 1); }
}
for ( i = 0; i < width; i++) {
for ( j = 0; j < height; j++) {
G[i][j] = B[i][j]
- pow(2, info->siz - 1);
}
}
for ( i = 0; i < width; i++) {
for ( j = 0; j < height; j++) {
R[i][j] = B[i][j]
- pow(2, info->siz - 1);
}
}
}
No dependence between array accesses B and R
Can perform loop fission
void dcls()
{
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
B[i][j-i] = B[i][j-i]
- pow(2, info->siz - 1);
}
}
}
….
….
…
}
Can tile the loops and generate smaller computational kernels
Each kernel consumes and produces chunks (tiles) of the different image components.
Want to tightly couple the computation with the data
Notes: Idea is to use code transformations to reduce the amount of computation per data sets, in order to maximize parallelism and reuse opportunities

## Slide 16: Inter-task/inter-kernel Dependencies
void mct_tiled()
{
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
Yr[i][j-i] =
ceil((float)(R[i][j-i] +
(2*(G[i][j-i])) +
B[i][j-i])/4);
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
Ur[i][j-i] =
B[i][j-i] -
G[i][j-i];
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
Vr[i][j-i] =
R[i][j-i] -
G[i][j-i];
}
void dcls_tiled()
{
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
B[i][j-i] = B[i][j-i]
- pow(2, info->siz - 1);
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
R[i][j-i] = R[i][j-i]
- pow(2, info->siz - 1);
for( ii=0; ii<m; ii+=tw) {
for( jj=0; jj<n; jj+=th) {
for( i=ii; i<min(m, ii+tw); i++) {
for( j=jj+i; j<min(n+i, jj+th+i); j++) {
G[i][j-i] = G[i][j-i]
- pow(2, info->siz - 1);
}
K1
K2
K3
K4
K5
K6
Known
Task
Dep.
Inter-Task/Inter-Kernel Dependencies

## Slide 17: Early Execution Edges Generation and Exploitation
K1a
K1b
K1c
K1d
Kernel K1
Kernel K2
K2a
K2b
Kernel k2a, can start as soon as its dependencies (Kernel iterations K1a, K1b, K1c finish their execution)
K1
K2
K1
K2
Original Task Graph and Schedule
K1a
K1b
K1c
K1d
K1n
K2a
K2b
K2c
K2m
K1a
K1b
K1c
K1d
K1e
K1f
K2a
K2b
CAM’s Augmented Task Graph and Pipelined Kernels
K1g
Higher Throughput and better memory utilization!
Notes: From the dependence analysis, we can generate a new task graph with a lower level of granularity (from the original task level)

## Slide 18: Tradeoff between power and performance
Chart: Power Vs. Perf. Vs. Both (Latency)
| Tiled_16KB, SPM_16KB(L) | Tiled_8KB, SPM_8KB(L) | Tiled_4KB, SPM_4KB(L) | Tiled_16KB, SPM_16KB(M) | Tiled_8KB, SPM_8KB(M) | Tiled_4KB, SPM_4KB(M) | Tiled_16KB, SPM_16KB(B) | Tiled_8KB, SPM_8KB(B) | Tiled_4KB, SPM_4KB(B)
4CPU | 593443216 | 771288592 | 927467568 | 1367104448 | 1240373088 | 1253878144 | 777754720 | 787311184 | 971010368
8CPU | 462246368 | 453560528 | 663335056 | 823069152 | 832302320 | 932449808 | 577190288 | 517528064 | 668392512
16CPU | 244177600 | 364944928 | 529082144 | 590451984 | 334339264 | 400147136
32CPU | 219761056 | 403666176 | 225986976
Chart: Power Vs. Perf. Vs. Both (Off-chip)
| Tiled_16KB, SPM_16KB(L) | Tiled_8KB, SPM_8KB(L) | Tiled_4KB, SPM_4KB(L) | Tiled_16KB, SPM_16KB(M) | Tiled_8KB, SPM_8KB(M) | Tiled_4KB, SPM_4KB(M) | Tiled_16KB, SPM_16KB(B) | Tiled_8KB, SPM_8KB(B) | Tiled_4KB, SPM_4KB(B)
4CPU | 21 | 47 | 117 | 9 | 41 | 111 | 9 | 43 | 111
8CPU | 7 | 25 | 87 | 5 | 15 | 83 | 5 | 17 | 83
16CPU | 13 | 49 | 7 | 29 | 7 | 35
32CPU | 21 | 13 | 13
Cost function (power/performance) affect total latency
Cost function (power/performance) affect off-chip accesses
Need to efficiently walk the search space for the right power/performance combination

## Slide 19: Exploration Search Space
Chart: 
| 16K_1I | 16K_2I | 16K_4I | 8K_1I | 8K_2I | 8K_4I | 4K_1I | 4K_2I | 4K_4I
4CPU | 6382.5323 | 5353.6638 | 5525.6906 | 5866.6302 | 5991.7951 | 6127.2794 | 6591.1003 | 6723.7046 | 6799.0836
8CPU | 5025.1054 | 3321.2802 | 3066.3709 | 3849.4878 | 3139.6606 | 3207.4809 | 3456.9477 | 3456.7582 | 3683.5348
16CPU | 5025.1054 | 2942.9989 | 1999.5573 | 2942.9989 | 2029.8727 | 1950.9774 | 2620.6424 | 2018.143 | 2074.4816
32CPU | 5025.1054 | 2528.8114 | 1791.3151 | 2523.5685 | 1421.6921 | 1363.3302 | 1578.9784 | 1387.5492 | 1293.0972
64CPU | 5025.1054 | 2528.8114 | 1526.5497 | 2523.5685 | 1419.0706 | 1210.2304 | 1269.6485 | 1212.8518 | 1030.4202
Lines: # of CPUs for the given configuration
Data Point (Axis): Size of SPM and tasks considered for the given configuration
Each data point represents a configuration considered (pipelined tasks/degree of unrolling, SPM size, number of CPUs)
The closer to the center of the spectrum the better the proposed solution on the given platform
Performance in billions of cycles
In order to find the best solution possible we need a good cost function to differentiate between good and bad candidates
Notes: Shows the search space, for different data points. Each point represents a tripled <number of tasks pipelined, SPM size, and number of CPUs)

## Slide 20: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
Customized Security Policy Generation
  Embedded Systems Security ‘10
Related Work
Conclusion

## Slide 21: Secure Software Execution on Chip-Multiprocessors
CMPs allow applications to run concurrently
  Parallelism within applications
Need to run a trusted application (many tasks)
  Possible spy processes running in a separate core
  Compromised tasks from the same application
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
Many Cores
Many Memories
Many tasks/applications
Many Shared resources
t2
t1
Notes: Describe target platform… multiprocessor systems

## Slide 22: Current Approaches to Guarantee Secure Software Execution
Side-channel attacks are possible in CMP systems
  Through resource sharing
Software exploits leverage use of C legacy code
Most current secure platforms assume single processor models
  TPM based models
Example: Flicker Secure Execution Model
  eliminate resource sharing during execution of sensible code
Problems
Trusted execution environment
Context switch, halt and, build trusted environment
Not power efficient, not performance efficient, but secure
Need a means to provide a trusted environment for secure execution without sacrificing performance and power

## Slide 23: Creating a Trusted Environment Through Selective Resource Sandboxing
CPU0
100
200
300
400
500
600
700
800
900
CPU1
CPU2
CPU3
DRM (450)/CX: 100
CPU0
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
CPU1
CPU2
CPU3
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
T3
DRM (450)/CX: 100
T4
T2
T1
Untrusted Environment
Trusted Environment (LOCKDOWN)
DRM (450)/CX: 100
CPU0
T1 (250)/C: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
CPU1
CPU2
CPU3
T1
T2
HALT Approach
Load Policy P
Task | Sandboxing Delay (ms)
T1 | 150
T2 | 250
T3 | 0
T4 | 0
DRM | 50
AVG | 90 ms
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
Context switch tasks with minimum CX penalty
Task | Traditional Halt Delay (ms)
T1 | 550
T2 | 575
T3 | 550
T4 | 500
DRM | 125
AVG | 460

## Slide 24: CAM: Security as a constraint
Front End
Application Pre-processing
(CFG extraction, task graph generation, input model generation)
Middle End
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
Task Decomposition
Define CMP
Template
Early Execution Edge Generation
C1
K2
K3
C4
K5
C6
Task1
Task2
Task Graph Augmentation
Secure Policy Generation
(Schedule + Mapping)
C1
K2
K3
C6
C4
K5
CPU1
CPU2
CPU3
SPM1
SPM2
K2D
K3D
K5D
Back End
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t1
t2
sec shared
Buf2.2
sec local buf2.1
sec local var
unsec
buf1
Security Requirements
Performance
Model
Generation
Meet Energy and Power Constraints?
Nope, let’s see if increasing degree of unrolling (in loops) helps, tile size?
Nope, let us generate a policy using more/less resources – re-define CMP
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
Data Reuse
Done creating policies given power/performance requirements?
Goal: Customize security policies for different system requirements (energy savings, performance, limited CPU/Memory resources)

## Slide 25: Policy Enforcement through On-chip Sandboxing
A1
A2
A3
Initial Queue
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Initial Load
A1
Exec
Policy Selection | High Load | Low Load
On Battery | Policy 1 | Policy 1 /Policy 2
On Power Cord | Policy 2 | Policy 3
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Executing A1 : Policy 2
A2
Exec
A3
Exec
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
P1
P2
M3
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
Latency
Power
Latency
Power
Power
Latency
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Executing A2 : Policy 2
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Executing A3 : Policy 1

## Slide 26: Performance Effects of PoliMakE
Chart: Normalized Execution Time
| 1_8 | 2_8 | 3_8 | 4_8 | 5_8 | 6_8 | 8_8 | 10_8 | 16_8 | 32_8
Sharing 50 % | 1 | 0.54217 | 0.50785 | 0.5006 | 0.49943 | 0.54124 | 0.53803 | 0.54672 | 0.54754 | 0.51989
Chart: PoliMakE Vs. Halt Approach
| JPEG_1 | DRM_1 | JPEG_2 | DRM_2 | JPEG_4 | DRM_4 | JPEG_8 | DRM_8 | JPEG_16 | DRM_16
PoliMakE | 2968160 | 80 | 262760 | 160 | 262760 | 28880 | 262760 | 28880 | 262760 | 28880
Halt | 4513480 | 58240 | 963480 | 58240 | 493520 | 57760 | 493520 | 57760 | 493520 | 57760
Exploration allows us to find right level of sharing and resource partition
No further significant improvement is found after 4 core CMP
Compared to halt approach, PoliMakE can drastically improve performance
After 4 CPUs (2 and 2), performance is not improved as much

## Slide 27: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
Customized Security Policy Generation
Related Work
Conclusion

## Slide 28: Related Work
Data Allocation
  Data Reuse Analysis Technique for Software-Controlled Memory Hierarchies [Issein DATE ‘04]
  Multiprocessor System-on-Chip Data Reuse Analysis for Exploring Customized Memory Hierarchies [Issenin DAC ‘06]
  Memory Coloring: DWT Compiler Approach for Scratchpad Memory Management [Li et al. PACT ‘05]
  Efficient Utilization of Scratch-Pad Memory in Embedded Processor Applications [Panda DATE ‘97]
Loop Scheduling
  Loop Scheduling with Complete Memory Latency Hiding on Multi-core Architecture [C. Xue ICPADS ’04]
  SPM Conscious Loop Scheduling for Embedded Chip Multiprocessors [L. Xue ICPADS ‘06]
Pipelining/Scheduling Heuristics
  Integrated Scratchpad Memory Optimization and Task Scheduling for MPSoC Architectures, [V. Suhendra et al . CASES ‘06].
  Pipelined Data Parallel Task Mapping/Scheduling Technique for MPSoC [Yang, H. et al., DATE 09]
  Exploiting Coarse-grained Task, Data, and Pipeline Parallelism in Stream Programs, [Gordon et al. ASPLOS ‘06]
We exploit the application’s inter/intra kernel data reuse opportunities to minimize data transfers thereby reducing dynamic power consumption
We exploit the application’s parallelism, pipelining, and data-reuse opportunities by applying different source level transformations
Distribute computations with the ultimate goal of reducing unnecessary data transfers and increasing throughput
Notes: Suhendra et al. [7] propose an ILP formulation that combines task scheduling, SPM partitioning, and data allocation. They show that by combining task scheduling and data placement into a single problem, they can achieve high gains in performance. Szymanek et al. [36] proposed a constructive memory aware scheduling algorithm that builds a schedule around the critical path and progressively schedules tasks in order to balance the memory utilization across processors.

## Slide 29: Related Work (Cont.)
Pure software solutions (complementary)
  CCured [24], StackGuard [10], Smashguard [25, Pointguard [26]
Hardware Assisted
  Patel et al. [27], Zambreno et al. [28], Arora et al. [30]
Platforms (complementary)
  ARM TrustZone [33], SECA [8], AEGIS [31]
Halt/Execute
  Flickr
Isolation
  IBM CELL Vault, Agarwal et al. [12]
Full platform support for secure software execution might be an overkill in cases security is limited to only a few applications
Current isolation approaches do not offer efficient (power/performance) means to run applications on multiprocessors
Can be complimentary but no side channel protection
No energy/performance awareness nor a means to map an application to the platform (left to programmer)
To the best of our knowledge, we are the first to propose the idea of customized policy making to guarantee secure software execution for CMPs

## Slide 30: Outline
Introduction & Motivation
CAM Overview
Memory-aware Macro-Pipelining
Customized Security Policy Generation
Related Work
Conclusion

## Slide 31: Conclusion
Discussed CAM, a software mapping and scheduling methodology for multimedia and data intensive applications
Progressively transforms the application’s code to discover and exploit
  Inter-kernel data reuse
  Parallelism opportunities
Tightly couple transformations, with data reuse analysis, scheduling and mapping
  Tightly couple computation with its data
Explores, generates and exploits customized policy making to guarantee secure software execution
Current enhancements include
  Reliability awareness
  Move towards heterogeneous MPSoCs and CGRAs

## Slide 32: Thank you!

## Slide 33: Power and Performance Improvements over Standard CMP Application Mapping Approaches
Chart: Performance Improvement (%) over Base SPM
| 16x4 | 16x8 | 8x4 | 8x8 | 8x16 | 4x4 | 4x8 | 4x16 | 4x32
Non-Clustered | 13.2621 | 8.5485 | 15.9472 | 20.5996 | 47.2907 | 17.6472 | 40.2395 | 33.1158 | 54.2423
Clustered | 13.9993 | 9.3577 | 14.8213 | 25.3914 | 81.5604 | 17.1065 | 40.4255 | 52.4874 | 56.422
Chart: Power Savings (%) over Base SPM
| 16x4 | 16x8 | 8x4 | 8x8 | 8x16 | 4x4 | 4x8 | 4x16 | 4x32
Non-Clustered | 57.9091 | 60.711 | 18.1021 | 38.6101 | 41.9325 | 4.7228 | 17.1101 | 37.5996 | 43.0891
Clustered | 58.7511 | 60.8052 | 15.047 | 43.8427 | 54.5256 | -0.050059 | 14.1478 | 42.6541 | 31.375
Clustering helps reduce number of unnecessary memory transfers as well as improve troughput
In some cases clustering hurts performance
(i.e. 8CPU with 4KB SPMs config.)
There are cases where clustering may lead to less power reduction
(i.e. 4CPU with 32KB SPMs config)
Y-axis: Improvement Percentage
X-axis: Platform Configuration – SPM Size by # CPUs
Notes: Less power savings are often due to the fact that the clustered kernels limit the data mapping opportunities during exploration steps

## Slide 34: Memory-aware scheduling and Early Execution Edge Exploitation
Progressive comparison
  Base case
  Task partitioning
  Early Execution + Task Partitioning
  Memory Aware Scheduling
Chart: Improvement %
| Task Partitioning | Early Execution | Memory Aware
8KB8CPU16T | 13.943 | 14.4242 | 33.8452
8KB8CPU32T | 13.3099 | 13.3099 | 30.8278
8KB8CPU64T | 14.2542 | 14.6169 | 33.249
Chart: Progressive Power Savings
| Task Partitioning | Early Execution | Memory Aware
8KB8CPU16T | 12.2778 | 12.446 | 43.674
8KB8CPU32T | 19.341 | 19.341 | 44.2017
8KB8CPU64T | 17.3773 | 17.3753 | 43.7021
Progressive Performance Improvement
i
A
B1
C1
Standard with task partitioning
After analyzing when tasks can start (early execution edges)
Memory aware task scheduling
B3
B2
B4
C3
C2
C4
A
B1
C1
B2
B4
C3
C2
C4
B3
A
B1
C1
B2
C3
C2
C4
B3
B4
A
B
C
Standard with base case – initial task graph
Our approach provides:
  Higher throughput
  Load balancing
  Savings in off-chip memory transfers

## Slide 35: Early Execution Edges
HL2
HH2
LH2
LL2
HL1
DWT
Quant.
EBCOT
HH1
HL2
HH2
LH2
LL2
HH1
HL2
HH2
LH2
LL2
Data is
propagated
through
a series of
filters
Quantization operates over
Individual subbands
(HH1, HH2, etc.)
EBCOT operates over
codeblocks from
the same subband
HH1
HL1
LH1
HL2
HH2
LH2
Quant. 2
Quant. 1
<0, declevel, 3>
<0, declevel, 1>
LL2
Quantization
Standard Approach
Early Execution Edges
HH1
LH1
HH1
HL1
LH1
HL2
HH2
LH2
LL2
Quantization waits for
DWT to finish
HH1
HL1
LH1
HL2
HH2
LH2
LL2
Quantization 1
Quantization 2
LH1
Quantization can be split
Quantization2 can
start after DWT produces
subbands LH1 and HH1
HL1
LH1
HL1
HL1
HL1
LH1
LH1
Procedure to obtain early execution edges:
- Obtain list of independent data sets (HH1, etc.)
- Calculate the live range for each data set
- Find split points for tasks and split them
Question:
- What can we do to
improve throughput?
DWT
DWT
Quant.
Quant. 2
Quant. 1
<0, declevel, 3>
<0, declevel, 1>
Inter-task
reuse
Augmented
task-graph
Live ranges of HH1,LH1,
and HL1 are up after the
first decomposition level
Notes: Similar to loop based iteration space partitioning

## Slide 36: Performance Model Generation and Evaluation
instr | cycle | min_power | max_power | ave_power | switching power
XORI | 4 | 2.48E-03 | 3.66E-03 | 3.07E-03 | 7.19E-04
MULI | 7 | 4.49E-03 | 8.07E-03 | 6.28E-03 | 2.16E-03
MFSPR | 4 | 2.51E-03 | 2.56E-03 | 2.54E-03 | 1.83E-04
a=a+3;
#if PERF_MOD
wait(ADD);
#endif
cycles+=ADD;
#if POWER_MOD
uW+=P_ADD;
#endif
if(a<b) {
#if PERF_MOD
wait(SLT+BNE+J);
#endif
cycles+=SLT+BNE+J;
#if POWER_MOD
uW +=P_SLT+P_BNE+P_J;
#endif
d=A[a];
#if PERF_MOD
wait(LW);
#endif
cycles+=LW;
#if POWER_MOD
uW+=P_LW;
#endif
}
CPU LUTs
Functional Model
a=a+3;
if(a<b) {
d=A[a];
}
Annotated Model
a=a+3;
#if PERF_MOD
wait(ADD);
#endif
cycles+=ADD;
#if POWER_MOD
uW+=P_ADD;
#endif
…………….
Annotated Model
a=a+3;
#if PERF_MOD
wait(ADD);
#endif
cycles+=ADD;
#if POWER_MOD
uW+=P_ADD;
#endif
…………….
Annotated Model
a=a+3;
#if PERF_MOD
wait(ADD);
#endif
cycles+=ADD;
#if POWER_MOD
uW+=P_ADD;
#endif
…………….
CPU
I$
D$
CPU
I$
D$
SystemC
ISS – Initial Profile
GCC &
Annotation
SystemC
Model Generator
Schedule
Info
Mapping
Info
Platform DB

## Slide 37: Finding Right Degree of Unrolling
Second case provides less parallelism as well as decreased dependencies
Both cases can increase/decrease performance, so we need to explore the design space to find the right combinations (Pareto)
Fully unrolling the execution of each tile can generate maximum amount of parallelism opportunities
Notes: Increased parallelism, more inter-kernel reuse opportunities, more dependencies and possible stall cycles due to them

## Slide 38: Memory Aware Scheduling and Pipelining
P0
P1
DWT
Q1
EBCOT1
P0
P1
P0
P1
Standard task scheduling
After analyzing when tasks can start (early execution edges)
Memory aware task scheduling
Q3
Q2
Q4
EBCOT3
EBCOT2
EBCOT4
DWT
Q1
EBCOT1
Q2
Q4
EBCOT3
EBCOT2
EBCOT4
Q3
DWT
Q1
EBCOT1
Q2
EBCOT3
EBCOT2
EBCOT4
Q3
Q4
Allows for further
optimizations
Increases
throughput
Minimize Off-chip memory accesses and DMA transfers
DWT
Q1
EBCOT1
Q3
Q2
Q4
EBCOT3
EBCOT2
EBCOT4
DWT
Q1
EBCOT1
Q2
Q4
EBCOT3
EBCOT2
EBCOT4
Q3
P0
P1
Software pipelining (Pipelining with Unrolling and Memory Awareness)
DWT
Q1
EBCOT1
Q2
EBCOT3
EBCOT2
EBCOT4
Q3
Q4
Increased throughput
and reduced memory
transfers
steady state
Notes: Small boxes represent communication costs due to memory transfers between tasks, idea is that when tasks are scheduled to a given CPU the mapping is done in order to minimize unecessary data transfers (reduce the number of transfers – small rectangular boxes)

## Slide 39: Pipelining Considering Unrolling
DWT
DWT
Q1
Q1
Q2
EBCOT2
Q2
EBCOT1
EBCOT1
DWT
DWT
DWT
Q1
Q1
Q1
EBCOT2
EBCOT1
EBCOT1
EBCOT1
Q2
Q2
Q2
EBCOT1
EBCOT2
DWT
Q2
EBCOT2
EBCOT2
Q1
DWT
DWT
Q1
Q1
Q2
EBCOT2
EBCOT2
Q2
EBCOT1
EBCOT1
39
DWT
DWT
DWT
Q1
Q1
Q2
EBCOT1
EBCOT2
EBCOT2
EBCOT2
Q1
Q2
Q2
EBCOT1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
Scheduling 1 task set at a time (Unrolling degree of 1)
Scheduling 2 task sets at a time (Unrolling degree of 2)
P0
P1
P2
P0
P1
P2
P0
P1
P2
P0
P1
P2
Scheduling 3 task sets at a time (Unrolling degree of 3)
Scheduling 4 task sets at a time (Unrolling degree of 4)
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
Too many idle slots
DWT
DWT
Q1
Q1
Q2
EBCOT2
Q2
EBCOT1
EBCOT1
DWT
DWT
Q1
Q1
Q2
EBCOT2
EBCOT2
Q2
EBCOT1
EBCOT1
A more compact schedule
(P2 has longer idle slots)
DWT
DWT
DWT
Q1
Q1
Q2
EBCOT1
EBCOT2
EBCOT2
EBCOT2
Q1
Q2
Q2
EBCOT1
EBCOT1
DWT
EBCOT2
Q2
Q1
EBCOT1
Worst performance
and more idle slots
than scheduling 2 tasks
If the mapping is not schedulable within MII,
retiming is done for all possible tasks
We need to explore different schedules/mappings in
order to find out the right unrolling/scheduling
combinations (software pipelining)

## Slide 40: Policy Generation Runtime
Chart: Runtime
| 12.0 | 29.0 | 63.0 | 163.0 | 179.0
8_4 | 121.2758 | 125.6783 | 128.3265 | 136.9062 | 176.9851
16_4 | 123.4768 | 127.2777 | 128.6708 | 152.9685 | 207.586
16_8 | 124.5782 | 127.7427 | 128.7775 | 160.9113 | 222.0521
8_8 | 122.3751 | 126.7095 | 128.5559 | 145.0484 | 193.158
Even if number of task increases by 14x, policy generation runtime is less than 2x