## Slide 1: PoliMakE: A Policy Making Engine for Secure Embedded Software Execution on Chip-Multiprocessors
Luis A. Bathen, Nikil Dutt

## Slide 2: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 3: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 4: Secure Software Execution on Chip-Multiprocessors
CMPs allow applications to run concurrently
  Parallelism within applications
Need to run a trusted application (many tasks)
  Possible spy processes running in a separate core
  Compromised tasks from the same application
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
Many Cores
Many Memories
Many tasks/applications
Many Shared resources
t2
t1
Notes: Describe target platform… multiprocessor systems

## Slide 5: Attack Models
Software based
  Buffer overrun attack on legacy C
Courtesy: Coburn et al., CASES ‘05
In 2004 alone, the Department of Homeland Security reported 323 buffer overflow vulnerabilities
[Hu et al., VEE ‘06]
Side-channel attacks
  Inferring (stealing) information though leakage
  RSA, Cache-timing attacks
When it comes to cryptographic software, side channel attacks are an often overlooked thread [Lawson, ROOT Labs, 2009]
P1
P2
C1
C2
AES
Spy
Threat: Spy processes, which can be hijacked tasks through a software exploit or malicious applications installed on the system

## Slide 6: Current Approaches to Guarantee Secure Software Execution
Side-channel attacks are possible in CMP systems
  Through resource sharing
Software exploits leverage use of C legacy code
Most current secure platforms assume single processor models
  TPM based models
Example: Flicker Secure Execution Model
  eliminate resource sharing during execution of sensible code
Problems
Trusted execution environment
Context switch, halt and, build trusted environment
Not power efficient, not performance efficient, but secure
Need a means to provide a trusted environment for secure execution without sacrificing performance and power

## Slide 7: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 8: Creating a Trusted Environment Through Selective Resource Sandboxing
CPU0
100
200
300
400
500
600
700
800
900
CPU1
CPU2
CPU3
DRM (450)/CX: 100
CPU0
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
CPU1
CPU2
CPU3
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
T3
DRM (450)/CX: 100
T4
T2
T1
Untrusted Environment
Trusted Environment (LOCKDOWN)
DRM (450)/CX: 100
CPU0
T1 (250)/C: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
CPU1
CPU2
CPU3
T1
T2
HALT Approach
Load Policy P
Task | Delay=Actual-Expected (ms)
T1 | (800-250)=550
T2 | (825-250)=575
T3 | (950-400)=550
T4 | (825-325)=500
DRM | (725-650)=125
AVG | 460
Task | Delay=Actual-Expected (ms)
T1 | (400-250)=150
T2 | (500-250)=250
T3 | (400-400)=0
T4 | (325-325)=0
DRM | (700-650)=50
AVG | 90 ms
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
Context switch tasks with minimum CX penalty

## Slide 9: PoliMakE : Software Driven Policy Generation
Given an application
  What are the application’s compute and memory requirements?
  Which variables need to be protected (confidentiality)?
Given a CMP platform
  What resources should we assign to the application
  How should we partition the CMP resources
Need to optimize resource allocation and schedule for power or performance
  While providing a trusted execution environment

## Slide 10: PoliMakE Methodology Overview
Pre-process application for secure analysis
(Generate CFG and secure task graph)
Secure Data
Mapping
Secure
Scheduling
Policy Making Engine
Extraction of security requirements
Front End
Middle End
Back End
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
Policy
Policy
Policy
Policy Enforcement
Goal is to obtain number of necessary resources to securely execute application
Goal is to generate customized policies
(power/performance – aware schedule and resource allocation)
Goal is to load the right policy and enforce it through selective Sandboxing

## Slide 11: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 12: Software Driven Policy Making
t1
t2
t1
t2
sec shared
Buf2.2
sec local buf2.1
sec local var
unsec
buf1
DRM
C/C++
t1
t2
t1
t2
cpu1
cpu2
spm1
spm2
t1
t2
buf1
Buf2.2
Buf2.1
var1
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
buf1
Buf2
var3
buf2
buf1
Buf2.1
var3
buf2.2
Initial task graph
Augmented task graph (sec. info)
Need to extract application’s compute and memory requirements in order to efficiently allocate resources for secure execution
Given the underlying platform, customize a schedule (task map), memory mapping, and ACLs for efficient sandboxing
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency

## Slide 13: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 14: PoliMakE Driven On-chip Sandboxing
A1
A2
A3
Initial Queue
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Initial Load
A1
Exec
Policy Selection | High Load | Low Load
On Battery | Policy 1 | Policy 1 /Policy 2
On Power Cord | Policy 2 | Policy 3
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Executing A1 : Policy 2
A2
Exec
A3
Exec
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
P1
P2
M3
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
Latency
Power
Latency
Power
Power
Latency
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Executing A2 : Policy 2
μP
μP
μP
μP
μP
μP
μP
μP
m
m
m
m
m
m
m
m
Executing A3 : Policy 1

## Slide 15: PoliMakE Driven On-chip Sandboxing
Minimal changes, per CPU key (hardware)
SPM level ACL
Sec
Arbiter
CPU1 Core
SPM7
CPU2 Core
SPU4
CPU4 Core
SPM2
SPM3
CPU3 Core
SPM5
SPM6
CPU1 Core
CPU2 Core
SPM2
Sec
Arbiter
SPM7
SPU4
CPU4 Core
SPM3
CPU3 Core
SPM5
SPM6
Sec
Arbiter
ACL
Lockdown
Untrusted Environment

## Slide 16: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 17: Related Work (Cont.)
Pure software solutions (complementary)
  CCured [24], StackGuard [10], Smashguard [25, Pointguard [26]
Hardware Assisted
  Patel et al. [27], Zambreno et al. [28], Arora et al. [30]
Platforms (complementary)
  ARM TrustZone [33], SECA [8], AEGIS [31]
Halt/Execute
  Flickr
Isolation
  IBM CELL Vault, Agarwal et al. [12]
Full platform support for secure software execution might be an overkill in cases security is limited to only a few applications
Current isolation approaches are limited to a (single task/application) and do not go over how to guarantee that applications are executed safely
To the best of our knowledge, we are the first to propose the idea of customized policy making to guarantee secure software execution for CMPs
No power/performance awareness

## Slide 18: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 19: Experimental Results
Testing platform:
  Ubuntu Linux 8.04 running on an Intel Quad Core at 2.66 GHz and 4GB memory
Questions that need answering:
  How many resources should we allocate to an application
    CPUs, memories, etc.
  Run-time performance
  Time needed to generate policies

## Slide 20: Performance Effects of PoliMakE
Chart: Normalized Execution Time
| 1_8 | 2_8 | 3_8 | 4_8 | 5_8 | 6_8 | 8_8 | 10_8 | 16_8 | 32_8
Sharing 50 % | 1 | 0.54217 | 0.50785 | 0.5006 | 0.49943 | 0.54124 | 0.53803 | 0.54672 | 0.54754 | 0.51989
Chart: PoliMakE Vs. Halt Approach
| JPEG_1 | DRM_1 | JPEG_2 | DRM_2 | JPEG_4 | DRM_4 | JPEG_8 | DRM_8 | JPEG_16 | DRM_16
PoliMakE | 2968160 | 80 | 262760 | 160 | 262760 | 28880 | 262760 | 28880 | 262760 | 28880
Halt | 4513480 | 58240 | 963480 | 58240 | 493520 | 57760 | 493520 | 57760 | 493520 | 57760
Exploration allows us to find right level of sharing and resource partition
No further significant improvement is found after 4 core CMP
Compared to halt approach, PoliMakE can drastically improve performance
After 4 CPUs (2 and 2), performance is not improved as much

## Slide 21: Policy Generation Runtime
Chart: Runtime
| 12.0 | 29.0 | 63.0 | 163.0 | 179.0
8_4 | 121.2758 | 125.6783 | 128.3265 | 136.9062 | 176.9851
16_4 | 123.4768 | 127.2777 | 128.6708 | 152.9685 | 207.586
16_8 | 124.5782 | 127.7427 | 128.7775 | 160.9113 | 222.0521
8_8 | 122.3751 | 126.7095 | 128.5559 | 145.0484 | 193.158
Even if number of task increases by 14x, policy generation runtime is less than 2x

## Slide 22: Outline
Introduction and Attack Models
PoliMakE Overview
Software Driven Policy Making
PoliMakE Driven On-chip Sandboxing
Related Work
Experimental Results
Concluding Remarks

## Slide 23: Conclusion
Proposed PoliMakE
  explores, generates and exploits customized policy making to guarantee secure software execution
  Policy enforcement can be done by enhancing existing multiprocessors with Secure DMA/Arbiter and ACLs
    Can be supported by platforms such as SECA and potentially TrustZone
We also propose a means to enforcing these policies via on-chip sandboxing, and dynamic policy selections
Our DRM/JPEG case study we observed up to 99% execution cycle reduction over the traditional halt approach
First to propose the idea of policy making to guarantee secure software execution for CMPs
Device-aware run-time policy enforcement
  Minimize overhead of resource partition

## Slide 24: Thank you!

## Slide 25: DRM Policy under Different Utilizations (Static Evaluation)
Chart: DRM Execution Time For Different Utilizations
| 1_8 | 2_8 | 3_8 | 4_8 | 5_8 | 6_8 | 8_8 | 10_8 | 16_8 | 32_8
No Sharing 25 % | 1.0075 | 0.53139 | 0.51141 | 0.50415 | 0.50298 | 0.54512 | 0.53874 | 0.55032 | 0.54071 | 0.52401
No Sharing 50% | 1.0075 | 0.53139 | 0.51141 | 0.50415 | 0.50298 | 0.54512 | 0.53874 | 0.55032 | 0.54071 | 0.52401
Sharing 25% | 1 | 0.54217 | 0.51629 | 0.51401 | 0.51745 | 0.51832 | 0.5006 | 0.5148 | 0.54778 | 0.54754
Sharing 50 % | 1 | 0.54217 | 0.50785 | 0.5006 | 0.49943 | 0.54124 | 0.53803 | 0.54672 | 0.54754 | 0.51989
Exploration allows us to find right level of sharing and resource partition
No further improvement is found after
4 core CMP

## Slide 26: Load-aware Policy Selection
Chart: PoliMakE Vs. Halt Approach
| JPEG_1 | DRM_1 | JPEG_2 | DRM_2 | JPEG_4 | DRM_4 | JPEG_8 | DRM_8 | JPEG_16 | DRM_16
Sharing Polimake | 2968160 | 80 | 262760 | 160 | 262760 | 28880 | 262760 | 28880 | 262760 | 28880
No Sharing Polimake | 3122360 | 80 | 492860 | 28880 | 204760 | 28880 | 204760 | 28880 | 204760 | 28880
Sharing Halt | 4446480 | 58240 | 1003480 | 58240 | 550520 | 57760 | 550520 | 57760 | 550520 | 57760
No Sharing Halt | 4513480 | 58240 | 963480 | 58240 | 493520 | 57760 | 493520 | 57760 | 493520 | 57760
Compared to halt approach, PoliMakE can drastically improve performance
After 4 CPUs (2 and 2), performance is not improved as much

## Slide 27: Effect of DRM on Small/Large Synthetic Application
Chart: Effect of DRM on Synthetic Application
| Halt SYN_64T_128B_R | Halt DRM R | Polimake SYN_64T_128B R | Polimake DRM R | Halt SYN_64T_128B M | Halt DRM M | Polimake SYN_64T_128B M | Polimake DRM M
2_4 | 1678599870 | 114308273 | 1564670017 | 114296593 | 5177202581 | 1143297290 | 4170869411 | 1142966890
4_4 | 2071011204 | 105545585 | 1964666779 | 105533905 | 4795132041 | 1056335850 | 3915959951 | 1055345130
8_4 | 2136139615 | 113436161 | 2021445274 | 113424481 | 4714775173 | 1135241610 | 3760754063 | 1134742410
16_4 | 2138123767 | 115440593 | 2021136314 | 115434673 | 5200171860 | 1154302890 | 4177226730 | 1154295210
32_4 | 2130820423 | 109612289 | 2021225894 | 109606369 | 5199816762 | 1096019850 | 3876148272 | 1096012170
The bigger the execution times the higher the ability of PoliMakE to reduce execution overhead vs. halt

## Slide 28: Effects of Sharing
Chart: Execution Time Vs. Platform Configuration
| 1CPUx1KB | 1CPUx4KB | 2CPUx1KB | 2CPUx4KB | 4CPUx1KB | 4CPUx4KB | 8CPUx1KB | 8CPUx4KB | 16CPUx1KB | 16CPUx4KB
No Sharing Execution | 1859800851 | 1338050085 | 1530330085 | 1453589351 | 1700955151 | 741599951 | 397186591 | 313207891 | 337420161 | 313262261
Sharing Execution | 1201814085 | 1154783085 | 1154783085 | 1513144371 | 919820371 | 643644371 | 471978411 | 387944411 | 502119881 | 192124881
Chart: Off-chip Accesses in Millions
| 1CPUx1KB | 1CPUx4KB | 2CPUx1KB | 2CPUx4KB | 4CPUx1KB | 4CPUx4KB | 8CPUx1KB | 8CPUx4KB | 16CPUx1KB | 16CPUx4KB
No Sharing Offchip | 43920 | 43920 | 43632 | 43632 | 43600 | 43600 | 43600 | 43600 | 43600 | 42580
Sharing Offchip | 29392 | 29392 | 29136 | 29136 | 29136 | 29136 | 29136 | 29136 | 28116 | 27360
Tradeoff between sharing and not sharing

## Slide 29: Performance Improvement over Halt Approach
Chart: % Performance Improvement over Halt Approach
| JPEG_1 | DRM_1 | JPEG_2 | DRM_2 | JPEG_4 | DRM_4 | JPEG_8 | DRM_8 | JPEG_16 | DRM_16
Sharing | 33.247 | 99.8626 | 73.8151 | 99.7253 | 52.2706 | 50 | 52.2706 | 50 | 52.2706 | 50
No Sharing | 30.8215 | 99.8626 | 48.8459 | 50.4121 | 58.5103 | 50 | 58.5103 | 50 | 58.5103 | 50

## Slide 30: Introduction
Sources : www.eetimes.fr / Computer Industry Almanac www.c-i-a.com
and Guy Gogniat, Umass Amherst, May
Devices
Mobile phones
Laptops
PCs
Sales in millions in 2004
650
47
130
Evolution compared to 2003
+ 35 %
+ 30 %
- stable
PDAs
23
+ 26 %
Year
2006
2007
2008
millions in 2004
1070
1210
1350
Evolution
+ 35 %
+ 30 %
- stable
2004
934
+ 35 %

## Slide 31: Introduction (Cont.)
PC
Smart card
player
memory
car
Company
network
servers
WLAN
terminal
laptop
PC
phone
PDA
Consequences…

## Slide 32: Attack Models
Software based
  Buffer overrun attack on legacy C
Courtesy: Coburn et al., CASES ‘05
In 2004 alone, the Department of Homeland Security reported 323 buffer overflow vulnerabilities
[Hu et al., VEE ‘06]
Side-channel attacks
  Inferring (stealing) information though leakage
  RSA, Cache-timing attacks
This takes a while
to compute
This is instantaneous
Whether iteration takes a long time
depends on the kth bit of secret exponent

## Slide 33: PoliMakE Overview
Kernel
Extraction
Kernel
Decomposition
Application
Tasks
Inter-kernel
Data Reuse
Analysis
Clustering
Task Graph
Augmentation
Task Graph
Update
Task Graph
Reduction
Secure Data
Mapping
Secure
Scheduling
Policy Making Engine
Policy
Security
Analysis
Task Graph
Update
Policy
Policy
Initial
Requirements
Front End
Middle End
Back End

## Slide 34: Attack Models
Software based
  Buffer overrun attack on legacy C
Courtesy: Coburn et al., CASES ‘05
In 2004 alone, the Department of Homeland Security reported 323 buffer overflow vulnerabilities
[Hu et al., VEE ‘06]
Side-channel attacks
  Inferring (stealing) information though leakage
  RSA, Cache-timing attacks
This takes a while
to compute
This is instantaneous
Whether iteration takes a long time
depends on the kth bit of secret exponent

## Slide 35: Increase in memory resources side-effects
Shared memory model
  Even multithreading increases vulnerability
AES dependency on table lookups
  Cache address = p XOR k
    P = known, k = unknown/secret
P1
P2
C1
C2
AES
Spy
P1
P2
C1
C2
AES
Spy
P1
P2
C1
C2
AES
Spy
Which values of k give us: cache address = p XOR k?
Collect histogram of time accesses for a given plaintext
Populate lines in shared cache and compute access time
Access time to spy cache line > known access time, must be table lookup
Goal: get enough information about k so that a brute force is feasible!
When it comes to cryptographic software, side channel attacks are an often overlooked thread [Lawson, ROOT Labs, 2009]

## Slide 36: Sandboxing is a possible solution
Eliminate resource sharing during execution of sensible code
  Flush state of processors
    Context switch
  Execute sensitive piece of code
  Resume normal execution
This model suffers from performance degradation
  Constant halting, flushing, and resuming of execution
Not power efficient, not performance efficient, but secure

## Slide 37: Secure Policy Making for CMPs
Goal: Execute an application safely in a multiprocessor environment
Means:
  Statically obtain a schedule an a series of policies to follow
  Dynamically execute the schedule while enforcing policies

## Slide 38: Secure Memory/Channels
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
Task A - local
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
Task B
Task C
Shared
Buffer
Local data only
Shared data + no one else accesses secure channel
Concurrent execution limited by resources!
NoCs or Bus Matrix?

## Slide 39: Standard Halt, CXS, Execute, Resume
CPU0
100
200
300
400
500
600
700
800
900
CPU1
CPU2
CPU3
DRM (450)/CX: 100
CPU0
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
CPU1
CPU2
CPU3
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
T3
DRM (450)/CX: 100
T4
T2
T1
Task | Delay=Actual-Expected (ms)
T1 | (800-250)=550
T2 | (825-250)=575
T3 | (950-400)=550
T4 | (825-325)=500
DRM | (725-650)=125
AVG | 460

## Slide 40: Policy Enforcement + Task/Data Re-mapping
Unsecure Environment
LOCKDOWN
CPU0
100
200
300
400
500
600
700
800
900
CPU1
CPU2
CPU3
DRM (450)/CX: 100
CPU0
T1 (250)/C: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
CPU1
CPU2
CPU3
T1 (250)/CX: 25
T2 (150)/CX: 50
T3 (250)/CX: 75
T4 (175)/CX: 50
DRM (450)/CX: 100
T1
T2
Task | Delay=Actual-Expected (ms)
T1 | (400-250)=150
T2 | (500-250)=250
T3 | (400-400)=0
T4 | (325-325)=0
DRM | (700-650)=50
AVG | 90 ms
Policy P

## Slide 41: Goal: Secure Policy Making
Given an application, gather:
  Data local to task
  Data shared by task
  Secure vs. unsecure data
  Need for a secure compute and memory resources
Policies:
  Grant each CPU access to a secure channel when needed
  Grant each CPU access to a secure memory when needed
  Sandboxing of resources via run-time access control list enforcement
Goal is to obtain number of necessary resources to securely execute application
Define policies to make it possible to safely execute the application

## Slide 42: Updating Secure Buffers and Channels
t1
t2
a1∩a2:
64
a2-(a1∩ a2):
64
d:1
b:128
t1
t2
a1 ∩ a2 :
<0, 63, 64, r/w, shared, sec>
b: <128, 191, 64, w/o, local, unsec>
a2- (a1 ∩ a2)=
<64, 127, 64, r/o, local, sec>
d: <192, 193,1, r/w, local, sec>
Secure Buffers
  a2-(a1∩ a2):64 – Local (t1)
  a1∩a2:64 – Shared (t1,t2)
  d – Local (t2)
Unsecure Buffers
  b:128 – Local (t1)
Secure Channels
  a2-(a1∩ a2) to t1
  a1∩a2:64 to t1
  d to t2
Unsecure Channels
  b to t2

## Slide 43: Updating Secure Buffers and Channels
t1
t2
a1∩a2:
64
a2-(a1∩ a2):
64
d:1
b:128
t1
t2
a1 ∩ a2 :
<0, 63, 64, r/w, shared, sec>
b: <128, 191, 64, w/o, local, unsec>
a2- (a1 ∩ a2)=
<64, 127, 64, r/o, local, sec>
d: <192, 193,1, r/w, local, sec>
Define secure and unsecure buffer requirements
Define secure and unsecure channel requirements
Secure Buffers
  a2-(a1∩ a2):64 – Local (t1)
  a1∩a2:64 – Shared (t1,t2)
  d – Local (t2)
Unsecure Buffers
  b:128 – Local (t1)
Secure Channels
  a2-(a1∩ a2) to t1
  a1∩a2:64 to t1
  d to t2
Unsecure Channels
  b to t2

## Slide 44: Establishing Security
t1
t2
Mem Map:
a: 0->127
b: 128->191
d: 192
Keep global mem map
t1
t2
b: <128, 191, 64, r/o, local, unsec>
a1: <0, 63, 64, w/o, local, sec>
a2: <0, 127, 128, r/o, local, sec>
t1
t2
a1 ∩ a2 : <0, 63, 64, r/w, shared, sec>
b: <128, 191, 64, w/o, local, unsec>
Compute inter-kernel reused buffers
a2- (a1 ∩ a2)=<64, 127, 64, r/o, local, sec>
t1:
for i = 0 to 63
if(b[i]>0)
a[i] = b[i]
l_s_lst: Ø
t2:
for j = 0 to 128
d += a[j]
l_s_lst: Ø
g_s_lst: a
t1:
for i = 0 to 63
if(b[i]>0)
a[i] = b[i]
l_s_lst: Ø
t2:
for j = 0 to 128
d += a[j]
l_s_lst: d
g_s_lst: a
Compute buffer requirements for each kernel
d: <192, 193,1, r/w, local, sec>
Compute security variables
d: <192, 193,1, r/w, local, sec>
Update security if necessary

## Slide 45: Establishing Security
t1
t2
Mem Map:
a: 0->127
b: 128->191
d: 192
Keep global mem map
t1
t2
b: <128, 191, 64, r/o, local, unsec>
a1: <0, 63, 64, w/o, local, sec>
a2: <0, 127, 128, r/o, local, sec>
t1
t2
a1 ∩ a2 : <0, 63, 64, r/w, shared, sec>
b: <128, 191, 64, w/o, local, unsec>
Compute inter-kernel reused buffers
a2- (a1 ∩ a2)=<64, 127, 64, r/o, local, sec>
t1:
for i = 0 to 63
if(b[i]>0)
a[i] = b[i]
l_s_lst: Ø
t2:
for j = 0 to 128
d += a[j]
l_s_lst: Ø
g_s_lst: a
t1:
for i = 0 to 63
if(b[i]>0)
a[i] = b[i]
l_s_lst: Ø
t2:
for j = 0 to 128
d += a[j]
l_s_lst: d
g_s_lst: a
Compute buffer requirements for each kernel
d: <192, 193,1, r/w, local, sec>
Compute security variables
d: <192, 193,1, r/w, local, sec>
Update security if necessary
t1
t2
a1∩a2:
64
a2-(a1∩ a2):
64
d:1
b:128

## Slide 46: Secure Policy (Cont.)
Based on target platform
  Generate Schedule
  Generate Mapping
Need platform support
  Dynamic policy enforcement
  Secure DMA and Arbiter
cpu1
cpu2
spm1
spm2
t1
t2
b
a (0, 63)
a (64, 127)
t1
t2
sec share
buf
sec local buf
sec local buf
unsec
buf
d
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
Generate mapping and scheduling (Policy)
When application runs, enforce policy

## Slide 47: Run-time Secure Policy Selection
SPM1
Off-chip memory
DMA
CMP
CPU1 Core
SPM2
CPU2 Core
SPMn
CPUn Core
t2
Task D
t1
SPMi
CPUi
Core
Task C
cpu1
cpu2
spm1
spm2
t1
t2
b
a (0, 63)
a (64, 127)
d
Policy 1 – Low Power
cpu1
cpu2
spm1
spm2
t1
t2
b
a (0, 127)
d
Policy 2 - Performance
Provide means to customize policies to meet different power and performance requirements
At run-time, device loads policy given the current device load/state (i.e. low battery = low power policy)

## Slide 48: Policy Driven Simplified Sandboxing
Minimal changes, per CPU key (hardware)
SPM level ACL
Sec
Arbiter
CPU1 Core
SPM7
CPU2 Core
SPU4
CPU4 Core
SPM2
SPM3
CPU3 Core
SPM5
SPM6
CPU1 Core
CPU2 Core
SPM2
Sec
Arbiter
SPM7
SPU4
CPU4 Core
SPM3
CPU3 Core
SPM5
SPM6
Sec
Arbiter
ACL
Lockdown
Untrusted Environment

## Slide 49: Software Driven Policy Making
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
P1
P2
M3
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
Latency
Power
Latency
Power
Power
Latency

## Slide 50: Software Driven Policy Making
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
Latency
Power
Latency
Power
Power
Latency
Policy 3
Policy 2
Policy 1
P1
P1
P2
P1
P2
P3
M1
M1
M1
M2
M2
P4
M2
Latency
Power
Latency
Power
Power
Latency
P1
P2
M3