## Slide 1: CS 295: Modern Systems Modern Processors – SIMD Extensions
Sang-Woo Jun
Spring, 2019

## Slide 2: Modern Processor Topics
Transparent Performance Improvements
  Pipelining, Caches
  Superscalar, Out-of-Order, Branch Prediction, Speculation, …
  Covered in CS250A and others
Explicit Performance Improvements
  SIMD extensions, AES extensions, …
  …
Non-Performance Topics
  Virtualization extensions, secure enclaves, transactional memory, …

## Slide 3: Flynn Taxonomy (1966) Recap
 |  | Data Stream | 
 |  | Single | Multi
Instruction Stream | Single | SISD (Single-Core Processors) | SIMD (GPUs, Intel SSE/AVX extensions, …)
 | Multi | MISD (Systolic Arrays, …) | MIMD (VLIW, Parallel Computers)

## Slide 4: Flynn Taxonomy Recap
Single-Instruction
Single-Data
(Single-Core Processors)
Multi-Instruction
Single-Data
(Systolic Arrays,…)
Single-Instruction
Multi-Data
(GPUs, Intel SIMD Extensions)
Multi-Instruction
Multi-Data
(Parallel Computers)

## Slide 5: Intel SIMD Extensions
New instructions, new registers
Introduced in phases/groups of functionality
  SSE – SSE4 (1999 –2006)
    128 bit width operations
  AVX, FMA, AVX2, AVX-512 (2008 – 2015)
    256 – 512 bit width operations
    AVX-512 chips not available yet (as of Spring, 2019), but soon!
F16C, and more to come?

## Slide 6: Intel SIMD Registers (AVX-512)
ZMM0
YMM0
XMM0
ZMM1
YMM1
XMM1
ZMM31
YMM31
XMM31
…
XMM0 – XMM15
  128-bit registers
  SSE
YMM0 – YMM15
  256-bit registers
  AVX, AVX2
ZMM0 – ZMM31
  512-bit registers
  AVX-512

## Slide 7: SSE/AVX Data Types
YMM0
float
float
float
float
double
double
int32
int32
int32
int32
float
float
float
float
double
double
int32
int32
int32
int32
16
16
8
8
16
16
8
8
8
8
8
8
16
16
8
8
16
16
8
8
8
8
8
8
16
16
8
8
16
16
8
8
8
8
8
8
16
16
8
8
16
16
8
8
8
8
8
8
Operation on 32 8-bit values in one instruction!
255
0

## Slide 8: Sandy Bridge Microarchitecture
e.g., “Port 5 pressure” when code uses too much shuffle operations

## Slide 9: Skylake Die Layout

## Slide 10: Aside: Do I Have SIMD Capabilities?
less /proc/cpuinfo

## Slide 11: Processor Microarchitectural Effects on Power Efficiency
The majority of power consumption of a CPU is not from the ALU
  Cache management, data movement, decoding, and other infrastructure
  Adding a few more ALUs should not impact power consumption
Indeed, 4X performance via AVX does not add 4X power consumption
  FromiI7 4770K measurements:
  Idle: 40 W
  Under load : 117 W
  Under AVX load : 128 W
Aside: Not all AVX operations are active at the same time – “Specialization horseman”?

## Slide 12: Compiler Automatic Vectorization
In gcc, flags “-O3 –mavx –mavx2” attempts automatic vectorization
Works pretty well for simple loops
But not for anything complex
  E.g., naïve bubblesort code not parallelized at all
Generated using GCC explorer: https://gcc.godbolt.org/

## Slide 13: Intel SIMD Intrinsics
Use C functions instead of inline assembly to call AVX instructions
Compiler manages registers, etc
Intel Intrinsics Guide
  https://software.intel.com/sites/landingpage/IntrinsicsGuide
  One of my most-visited pages…
e.g.,
__m256 a, b, c;
__m256 d = _mm256_fmadd_ps(a, b, c); // d[i] = a[i]*b[i]+c[i] for i = 0 …7

## Slide 14: Data Types in AVX/AVX2
Type | Description
__m128 | 128-bit vector containing 4 floats
__m128d | 128-bit vector containing 2 doubles
__m128i | 128-bit vector containing integers
__m256 | 256-bit vector containing 8 floats
__m256d | 256-bit vector containing 4 doubles​
__m256i | 256-bit vector containing integers
1~16 signed/unsigned integers
1~32 signed/unsigned integers
__m512 variants in the future for AVX-512

## Slide 15: Intrinsic Naming Convention
_mm<width>_[function]_[type]
  E.g., _mm256_fmadd_ps : perform fmadd (floating point multiply-add) on 256 bits of packed single-precision floating point values (8 of them)
Width | Prefix
128 | _mm_
256 | _mm256_
512 | _mm512_
Type | Postfix
Single precision | _ps
Double precision | _pd
Packed signed integer | _epiNNN (e.g., epi256)
Packed unsigned integer | _epuNNN (e.g., epu256)
Scalar integer | _siNNN (e.g., si256)
Not all permutations exist! Check guide

## Slide 16: Load/Store/Initialization Operations
Initialization
  _mm256_setzero_ps/pd/epi32/…
  _mm256_set_...
  …
Load/Store : Address MUST be aligned by 256-bit
  _mm256_load_...
  _mm256_store_...
And many more! (Masked read/write, strided reads, etc…)
e.g.,
__mm256d t = _mm256_load_pd(double const * mem); // loads 4 double values from mem to t
__mm256i v = _mm256_set_epi32(h,g,f,e,d,c,b,a); // loads 8 integer values to v

## Slide 17: Vertical Vector Instructions
Add/Subtract/Multiply
  _mm256_add/sub/mul/div_ps/pd/epi
    Mul only supported for epi32/epu32/ps/pd
    Div only supported for ps/pd
    Consult the guide!
Max/Min/GreaterThan/Equals
Sqrt, Reciprocal, Shift, etc…
FMA (Fused Multiply-Add)
  (a*b)+c, -(a*b)-c, -(a*b)+c, and other permutations!
  Consult the guide!
…
a
b
c
d
×
×
×
×
+
+
+
+
=
__m256 a, b, c;
__m256 d = _mm256_fmadd_pd(a, b, c);
=
=
=

## Slide 18: Integer Multiplication Caveat
Integer multiplication of two N bit values require 2N bits
E.g., __mm256_mul_epi32 and __mm256_mul_epu32
  Only use the lower 4 32 bit values
  Result has 4 64 bit values
E.g., __mm256_mullo_epi32 and __mm256_mullo_epu32
  Uses all 8 32 bit values
  Result has 8 truncated 32 bit values
And more options!
  Consult the guide…

## Slide 19: Horizontal Vector Instructions
Horizontal add/subtraction
  Adds adjacent pairs of values
  E.g., __m256d _mm256_hadd_pd (__m256d a, __m256d b)
a
b
c
+
+
+
+

## Slide 20: Shuffling/Permutation
Within 128-bit lanes
  _mm256_shuffle_ps/pd/… (a,b, imm8)
  _mm256_permute_ps/pd
  _mm256_permutevar_ps/…
Across 128-bit lanes
  _mm256_permute2x128/4x64 : Uses 8 bit control
  _mm256_permutevar8x32/… : Uses 256 bit control
Not all type permutations exist, but variables can be cast back and forth
Matt Scarpino, “Crunching Numbers with AVX and AVX2,” 2016

## Slide 21: Blend
Merges two vectors using a control
  _mm256_blend_... : Uses 8 bit control
    e.g., _mm256_blend_epi32
  _mm256_blendv_... : Uses 256 bit control
    e.g., _mm256_blendv_epi8
a
b
c
?
?
?
?

## Slide 22: Alignr
Right-shifts concatenated value of two registers, by byte
  Often used to implement circular shift by using two same register inputs
  _mm256_alignr_epi8 (a, b, count)
a
b
c
Example of 64-bit values being shifted by 8

## Slide 23: Helper Instructions
Cast
  __mm256i <-> __mm256, etc…
  Syntactic sugar -- does not spend cycles
Convert
  4 floats <-> 4 doubles, etc…
Movemask
  __mm256 mask to -> int imm8
And many more…

## Slide 24: Case Study: Sorting
Important, fundamental application!
Can be parallelized via divide-and-conquer
How can SIMD help?

## Slide 25: Reminder: Sorting Network
Network structure for sorting fixed number of values
Type of a “comparator network”
  comparators perform compare-and-swap
Easily pipelined and parallelized
Example 4-element sorting network
5 comparators, 3 cycle pipelined

## Slide 26: Remind: Sorting Network
Simple to generate correct sorting networks, but optimal structures are not well-known
Source: Wikipedia (Sorting Network)
Some known optimal sorting networks

## Slide 27: SIMD And Sorting Networks
AVX compare/max/min instructions do not work internally to a register
  Typically same values copied to two different registers, permuted, compared
  Or, “two register trick”, and many more optimizations
In this case, optimal sorting networks are typically not very helpful
  Irregular computation means bubbles in the compute structure
  Simple, odd-even sorting network works well
8-element odd-even sorting network
What if I want to sort more than 8 values?

## Slide 28: SIMD And Sorting Networks
Typically, we are sorting more than one set of tuples
  If we have multiple tasks, we can have task-level parallelism – Optimized networks!
  Sort multiple tuples at the same time
Then we need to transpose the 8 8-element variables
  Each variable has a value for each sorting network instance
  Non-SIMD works, or a string of unpackhi/unpacklo/blend
…
Instruction 1, 2 (min, max)
Instruction 3, 4 (min, max)

## Slide 29: SIMD And Sorting Networks
Some SIMD instructions have high throughput, but high latency
  Data dependency between two consecutive max instructions can take 8 cycles on Skylake
  If each parallel stage has less than 4 operations, pipeline may stall
    Solution: Interleave two sets of parallel 8-tuple sorting
  In reality, min/max means even for 4-tuples, pipeline is still filled
Source: Instrinsics guide

## Slide 30: The Two Register Merge
Sort units of two pre-sorted registers, K elements
  minv = A, maxv = B
  // Repeat K times
    minv = min(minv,maxv)
    maxv = max(minv,maxv)
    // circular shift one value down
    minv = alignr(minv,minv,imm)
Inoue et.al., “SIMD- and Cache-Friendly Algorithm for Sorting an Array of Structures,” VLDB 2015

## Slide 31: SIMD And Merge Sort
Hierarchically merged sorted subsections
Using the SIMD merger for sorting
  vector_merge is the two-register sorter from before
What if we want to sort structs?
  Instead of min/max, use cmpgt, followed by permute for both key and values
  For large values, use <key, index>
Inoue et.al., “SIMD- and Cache-Friendly Algorithm for Sorting an Array of Structures,” VLDB 2015
Typically reports 2x + performance!

## Slide 32: Topic Under Active Research!
Papers being written about…
  Architecture-optimized matrix transposition
  Register-level sorting algorithm
  Merge-sort
  … and more!
Good find can accelerate your application kernel 2x

## Slide 33: Case Study: Matrix Multiply
Branch : Boser & Katz, “CS61C: Great Ideas In Computer Architecture” Lecture 18 – Parallel Processing – SIMD

## Slide 34
https://www.intel.com/content/dam/www/public/us/en/documents/manuals/64-ia-32-architectures-optimization-manual.pdf

## Slide 35: SIMD Recap
Data
Instructions
Processing
Unit
Data
Instructions
Processing
Unit
Processing
Unit
Processing
Unit

## Slide 36: SIMD Recap
Data
Instructions
Processing
Unit
Data
Instructions
Processing
Unit
Processing
Unit
Processing
Unit
Processing
Unit