250P: Computer Systems
Architecture
Lecture 3: Basic MIPS Architecture
Anton Burtsev
October, 2019

---
Basic MIPS Architecture
Now that we understand clocks and storage of states,
we’ll design a simple CPU that executes:
basic math (add, sub, and, or, slt)
memory access (lw and sw)
branch and jump instructions (beq and j)

---
Implementation Overview
We need memory
to store instructions
to store data
for now, let’s make them separate units
We need registers, ALU, and a whole lot of control logic
CPU operations common to all instructions:
use the program counter (PC) to pull instruction out
of instruction memory
read register values

---
View from 30,000 Feet
Note: we haven’t bothered
showing multiplexors
What is the role of the Add units?
Explain the inputs to the data memory unit
Explain the inputs to the ALU
Explain the inputs to the register unit
Source: H&P textbook

---
Clocking Methodology
Which of the above units need a clock?
What is being saved (latched) on the rising edge of the clock?
Keep in mind that the latched value remains there for an entire cycle

---
Implementing R-type Instructions
Instructions of the form add $r1, $r2, $r3
Explain the role of each signal

---
Implementing Loads/Stores
Instructions of the form lw $r1, 8($r2) and sw $r1, 8($r2)
Explain the role of each signal
Where does this input come from?

---
Implementing J-type Instructions
Instructions of the form beq $r1, $r2, offset

---
View from 10,000 Feet

---
View from 5,000 Feet