250P: Computer Systems
Architecture
Lecture 2: Understanding Power and Performance
Anton Burtsev
January, 2019

---
Where Are We Heading?
- Modern trends:
  - Clock speed improvements are slowing
    - power constraints
  - Difficult to further optimize a single core for performance
  - Multi-cores: each new processor generation will accommodate more cores
  - Need better programming models and efficient execution for multi-threaded applications
  - Need better memory hierarchies
  - Need greater energy efficiency

---
Power Consumption Trends
- Dyn power  activity x capacitance x voltage2 x frequency
- Capacitance per transistor and voltage are decreasing, but number of transistors is increasing at a faster rate; hence clock frequency must be kept steady
- Leakage power is also rising; is a function of transistor count, leakage current, and supply voltage
  - P = Voltage x Current = V x I
- Power consumption is already between 100-150W in high-performance processors today
- Energy = power x time = (dynpower + lkgpower) x time

---
Power Vs. Energy
- Energy is the ultimate metric: it tells us the true “cost” of performing a fixed task
- Power (energy/time) poses constraints; can only work fast
  enough to max out the power delivery or cooling solution
- If processor A consumes 1.2x the power of processor B, but finishes the task in 30% less time, its relative energy is 1.2 X 0.7 = 0.84; Proc-A is better, assuming that 1.2x power can be supported by the system

---
Reducing Power and Energy
- Can gate off transistors that are inactive (reduces leakage)
- Design for typical case and throttle down when activity exceeds a threshold
- DFS: Dynamic frequency scaling -- only reduces frequency and dynamic power, but hurts energy
- DVFS: Dynamic voltage and frequency scaling – can reduce voltage and frequency by (say) 10%; can slow a program by (say) 8%, but reduce dynamic power by 27%, reduce total power by (say) 23%, reduce total energy by 17%
  - (Note: voltage drop  slow transistor  freq drop)

---
DFS and DVFS
- DFS
- DVFS

---
Metrics to Evaluate Performance

---
Measuring Performance
- Two primary metrics:
  - wall clock time (response time for a program) and
  - throughput (jobs performed in unit time)
- To optimize throughput, must ensure that there is minimal waste of resources

---
Benchmark Suites
- Performance is measured with benchmark suites: a collection of programs that are likely relevant to the user
  - SPEC CPU 2006: cpu-oriented programs (for desktops)
  - SPECweb, TPC: throughput-oriented (for servers)
  - EEMBC: for embedded processors/workloads

---
Summarizing Performance
- Consider 25 programs from a benchmark set – how do we capture the behavior of all 25 programs with a single number?
  P1 P2 P3
  Sys-A 10 8 25
  Sys-B 12 9 20
  Sys-C 8 8 30
  - Sum of execution times (AM)
  - Sum of weighted execution times (AM)
  - Geometric mean of execution times (GM)

---
Sum of Weighted Exec Times – Example
- We fixed a reference machine X and ran 4 programs A, B, C, D on it such that each program ran for 1 second
- The exact same workload (the four programs execute the same number of instructions that they did on machine X) is run on a new machine Y and the execution times for each program are 0.8, 1.1, 0.5, 2
- With AM of normalized execution times, we can conclude that Y is 1.1 times slower than X – perhaps, not for all workloads, but definitely for one specific workload (where all programs run on the ref-machine for an equal #cycles)

---
Summarizing Performance
- Consider 25 programs from a benchmark set – how do we capture the behavior of all 25 programs with a single number?
  P1 P2 P3
  Sys-A 10 8 25
  Sys-B 12 9 20
  Sys-C 8 8 30
  - Sum of execution times (AM)
  - Sum of weighted execution times (AM)
  - Geometric mean of execution times (GM)

---
GM Example
Computer-A	Computer-B Computer-C
P1 1 sec 10 secs 20 secs
P2 1000 secs 100 secs 20 secs
Conclusion with GMs: (i) A=B
(ii) C is ~1.6 times faster
For (i) to be true, P1 must occur 100 times for every
occurrence of P2
With the above assumption, (ii) is no longer true
Hence, GM can lead to inconsistencies

---
Summarizing Performance
- GM: does not require a reference machine, but does not predict performance very well
  - So we multiplied execution times and determined that sys-A is 1.2x faster…but on what workload?
- AM: does predict performance for a specific workload, but that workload was determined by executing programs on a reference machine
  - Every year or so, the reference machine will have to be updated

---
CPU Performance Equation
- Clock cycle time = 1 / clock speed
- CPU time = clock cycle time x cycles per instruction x number of instructions
- Influencing factors for each:
  - clock cycle time: technology and pipeline
  - CPI: architecture and instruction set design
  - instruction count: instruction set design and compiler
- CPI (cycles per instruction) or IPC (instructions per cycle) can not be accurately estimated analytically

---
An Alternative Perspective - I
Each program is assumed to run for an equal number
of cycles, so we’re fair to each program
The number of instructions executed per cycle is a
measure of how well a program is doing on a system
The appropriate summary measure is sum of IPCs or
AM of IPCs = 1.2 instr + 1.8 instr + 0.5 instr
cyc cyc cyc
This measure implicitly assumes that 1 instr in prog-A
has the same importance as 1 instr in prog-B

---
An Alternative Perspective - II
Each program is assumed to run for an equal number
of instructions, so we’re fair to each program
The number of cycles required per instruction is a
measure of how well a program is doing on a system
The appropriate summary measure is sum of CPIs or
AM of CPIs = 0.8 cyc + 0.6 cyc + 2.0 cyc
instr instr instr
This measure implicitly assumes that 1 instr in prog-A
has the same importance as 1 instr in prog-B

---
AM and HM
Note that AM of IPCs = 1 / HM of CPIs and
AM of CPIs = 1 / HM of IPCs
So if the programs in a benchmark suite are weighted
such that each runs for an equal number of cycles, then
AM of IPCs or HM of CPIs are both appropriate measures
If the programs in a benchmark suite are weighted such
that each runs for an equal number of instructions, then
AM of CPIs or HM of IPCs are both appropriate measures

---
Thank you!

---
Execution times

---
Total execution time

---
Drawbacks of geometric means
- Do not predict performance
  - P1 has to run 100 times for each run of P2

---
Drawbacks of geometric means
- Do not predict performance
  - P1 has to run 100 times for each run of P2
- Encourages improving easy targets
  - Cut execution time of any benchmarks by 0.5

---
Speedup Vs. Percentage
“Speedup” is a ratio = old exec time / new exec time
“Improvement”, “Increase”, “Decrease” usually refer to
percentage relative to the baseline
= (new perf – old perf) / old perf
A program ran in 100 seconds on my old laptop and in 70
seconds on my new laptop
What is the speedup?
What is the percentage increase in performance?
What is the reduction in execution time?