250P: Computer Systems
Architecture
Lecture 4: Pipelining hazards
Anton Burtsev
January, 2019

---
A 5-Stage Pipeline
Source: H&P textbook

---
Hazards
Structural hazards: different instructions in different stages
(or the same stage) conflicting for the same resource
Data hazards: an instruction cannot continue because it
needs a value that has not yet been generated by an
earlier instruction
Control hazard: fetch cannot continue because it does
not know the outcome of an earlier branch – special case
of a data hazard – separate category because they are
treated in different ways

---
Structural hazards

---
A 5-Stage Pipeline
Source: H&P textbook

---
Structural Hazards
Example: a unified instruction and data cache 
stage 4 (MEM) and stage 1 (IF) can never coincide
The later instruction and all its successors are delayed
until a cycle is found when the resource is free  these
are pipeline bubbles
Structural hazards are easy to eliminate – increase the
number of resources (for example, implement a separate
instruction and data cache)

---
Data hazards

---
A 5-Stage Pipeline
Source: H&P textbook

---
Pipeline Implementation
Signals for the muxes have to be generated – some of this can happen during ID
Need look-up tables to identify situations that merit bypassing/stalling – the
number of inputs to the muxes goes up

---
Example
add R1, R2, R3
lw R4, 8(R1)
Source: H&P textbook

---
Example
lw R1, 8(R2)
lw R4, 8(R1)
Source: H&P textbook

---
Example
lw R1, 8(R2)
sw R1, 8(R3)
Source: H&P textbook

---
Summary
For the 5-stage pipeline, bypassing can eliminate delays
between the following example pairs of instructions:
add/sub R1, R2, R3
add/sub/lw/sw R4, R1, R5
lw R1, 8(R2)
sw R1, 4(R3)
The following pairs of instructions will have intermediate
stalls:
lw R1, 8(R2)
add/sub/lw R3, R1, R4 or sw R3, 8(R1)
fmul F1, F2, F3
fadd F5, F1, F4

---
Control hazards

---
Hazards
Structural hazards
Data hazards
Control hazards

---
Control Hazards
Simple techniques to handle control hazard stalls:
for every branch, introduce a stall cycle (note: every
6th instruction is a branch on average!)
assume the branch is not taken and start fetching the
next instruction – if the branch is taken, need hardware
to cancel the effect of the wrong-path instructions
predict the next PC and fetch that instr – if the prediction
is wrong, cancel the effect of the wrong-path instructions
fetch the next instruction (branch delay slot) and
execute it anyway – if the instruction turns out to be
on the correct path, useful work was done – if the
instruction turns out to be on the wrong path,
hopefully program state is not lost

---
Branch delay slot

---
Thank you!