250P: Computer Systems
Architecture
Lecture 5: Advanced Pipelines
Anton Burtsev
January, 2019

---
Hazards
Structural hazards
Data hazards
Control hazards

---
Control Hazards
Simple techniques to handle control hazard stalls:
for every branch, introduce a stall cycle (note: every
6th instruction is a branch on average!)
assume the branch is not taken and start fetching the
next instruction – if the branch is taken, need hardware
to cancel the effect of the wrong-path instructions
predict the next PC and fetch that instr – if the prediction
is wrong, cancel the effect of the wrong-path instructions
fetch the next instruction (branch delay slot) and
execute it anyway – if the instruction turns out to be
on the correct path, useful work was done – if the
instruction turns out to be on the wrong path,
hopefully program state is not lost

---
Branch delay slot

---
Multicycle Instructions

---
Effects of Multicycle Instructions
Potentially multiple writes to the register file in a cycle
Frequent RAW hazards
WAW hazards (WAR hazards not possible)
Imprecise exceptions because of o-o-o instr completion
Note: Can also increase the “width” of the processor: handle
multiple instructions at the same time: for example, fetch
two instructions, read registers for both, execute both, etc.

---
Precise Exceptions
On an exception:
must save PC of instruction where program must resume
all instructions after that PC that might be in the pipeline
must be converted to NOPs (other instructions continue
to execute and may raise exceptions of their own)
temporary program state not in memory (in other words,
registers) has to be stored in memory
potential problems if a later instruction has already
modified memory or registers
A processor that fulfils all the above conditions is said to
provide precise exceptions (useful for debugging and of
course, correctness)

---
Dealing with these Effects
Multiple writes to the register file: increase the number of
ports, stall one of the writers during ID, stall one of the
writers during WB (the stall will propagate)
WAW hazards: detect the hazard during ID and stall the
later instruction
Imprecise exceptions: buffer the results if they complete
early or save more pipeline state so that you can return to
exactly the same state that you left at

---
Slowdowns from Stalls
Perfect pipelining with no hazards  an instruction
completes every cycle (total cycles ~ num instructions)
 speedup = increase in clock speed = num pipeline stages
With hazards and stalls, some cycles (= stall time) go by
during which no instruction completes, and then the stalled
instruction completes
Total cycles = number of instructions + stall cycles
Slowdown because of stalls = 1/ (1 + stall cycles per instr)

---
Pipelining Limits
Gap between indep instrs: T + Tovh
Gap between dep instrs: T + Tovh
Gap between indep instrs:
T/3 + Tovh
Gap between dep instrs:
T + 3Tovh
A
B
C
A
B
C
Gap between indep instrs:
T/6 + Tovh
Gap between dep instrs:
T + 6Tovh
A
B
C
D
E
F
A
B
C
D
E
F
Assume that there is a dependence where the final result of the
first instruction is required before starting the second instruction

---
Problem 1
For the following code sequence, show how the instrs
flow through the pipeline:
ADD R3  R1, R2
LD R7  8[R6]
ST R9  4[R8]
BEZ R4, [R5]

---
Problem 1
For the following code sequence, show how the instrs
flow through the pipeline:
ADD R3  R1, R2
LD R7  8[R6]
ST R9  4[R8]
BEZ R4, [R5]
ADD
ADD
ADD
ADD
ADD
LD
LD
LD
LD
LD
ST
ST
ST
ST
BEZ
BEZ

---
Pipeline Summary
RR ALU DM RW
ADD R3  R1, R2 Rd R1,R2 R1+R2 -- Wr R3
BEZ R1, [R5] Rd R1, R5 -- -- --
Compare, Set PC
LD R6  8[R3] Rd R3 R3+8 Get data Wr R6
ST R6  8[R3] Rd R3,R6 R3+8 Wr data --

---
Problem 2
Convert this C code into equivalent RISC assembly
instructions
a[i] = b[i] + c[i];

---
Problem 2
Convert this C code into equivalent RISC assembly
instructions
a[i] = b[i] + c[i];
LD R2, [R1] # R1 has the address for variable i
MUL R3, R2, 8 # the offset from the start of the array
ADD R7, R3, R4 # R4 has the address of a[0]
ADD R8, R3, R5 # R5 has the address of b[0]
ADD R9, R3, R6 # R6 has the address of c[0]
LD R10, [R8] # Bringing b[i]
LD R11, [R9] # Bringing c[i]
ADD R12, R11, R10 # Sum is in R12
ST R12, [R7] # Putting result in a[i]

---
Problem 3
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9
CYC-1
CYC-2
CYC-3
CYC-4
CYC-5
CYC-6
CYC-7
CYC-8
IF
IF
IF
IF
IF
IF
IF
IF
D/R
D/R
D/R
D/R
D/R
D/R
D/R
D/R
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
DM
DM
DM
DM
DM
DM
DM
DM
RW
RW
RW
RW
RW
RW
RW
RW

---
Problem 3
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9
CYC-1
CYC-2
CYC-3
CYC-4
CYC-5
CYC-6
CYC-7
CYC-8
IF
I1
IF
I2
IF
I3
IF
I3
IF
I3
IF
I4
IF
I5
IF
D/R
D/R
I1
D/R
I2
D/R
I2
D/R
I2
D/R
I3
D/R
I4
D/R
ALU
ALU
ALU
I1
ALU
ALU
ALU
I2
ALU
I3
ALU
DM
DM
DM
DM
I1
DM
DM
DM
I2
DM
I3
RW
RW
RW
RW
RW
I1
RW
RW
RW
I2

---
Bypassing: 5-Stage Pipeline
Source: H&P textbook

---
Problem 4
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.
CYC-1
CYC-2
CYC-3
CYC-4
CYC-5
CYC-6
CYC-7
CYC-8
IF
IF
IF
IF
IF
IF
IF
IF
D/R
D/R
D/R
D/R
D/R
D/R
D/R
D/R
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
DM
DM
DM
DM
DM
DM
DM
DM
RW
RW
RW
RW
RW
RW
RW
RW

---
Problem 4
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.
CYC-1
CYC-2
CYC-3
CYC-4
CYC-5
CYC-6
CYC-7
CYC-8
IF
I1
IF
I2
IF
I3
IF
I4
IF
I5
IF
IF
IF
D/R
D/R
I1
D/R
I2
D/R
I3
D/R
I4
D/R
D/R
D/R
L3 L3 L4 L3 L5 L3
ALU
ALU
ALU
I1
ALU
I2
ALU
I3
ALU
ALU
ALU
DM
DM
DM
DM
I1
DM
I2
DM
I3
DM
DM
RW
RW
RW
RW
RW
I1
RW
I2
RW
I3
RW

---
Thank you!