250P: Computer Systems
Architecture
Lecture 7: Static Instruction Level Parallelism
Anton Burtsev
October, 2021

---
Static vs Dynamic Scheduling
Arguments against dynamic scheduling:
requires complex structures to identify independent
instructions (scoreboards, issue queue)
high power consumption
low clock speed
high design and verification effort
the compiler can “easily” compute instruction latencies
and dependences – complex software is always
preferred to complex hardware (?)

---
ILP
Instruction-level parallelism: overlap among instructions:
pipelining or multiple instruction execution
What determines the degree of ILP?
dependences: property of the program
hazards: property of the pipeline

---
Loop Scheduling
The compiler’s job is to minimize stalls
Focus on loops: account for most cycles, relatively easy
to analyze and optimize

---
Assumptions
Load: 2-cycles (1 cycle stall for consumer)
FP ALU: 4-cycles (3 cycle stall for consumer; 2 cycle stall
if the consumer is a store)
One branch delay slot
Int ALU: 1-cycle (no stall for consumer, 1 cycle stall if the
consumer is a branch)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

---
Loop Example
for (i=1000; i>0; i--)
x[i] = x[i] + s;
Source code
Loop: L.D F0, 0(R1) ; F0 = array element
ADD.D F4, F0, F2 ; add scalar
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
BNE R1, R2, Loop ; branch if R1 != R2
NOP
Assembly code

---
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall
Loop Example
for (i=1000; i>0; i--)
x[i] = x[i] + s;
Source code
Loop: L.D F0, 0(R1) ; F0 = array element
ADD.D F4, F0, F2 ; add scalar
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
BNE R1, R2, Loop ; branch if R1 != R2
NOP
Assembly code
Loop: L.D F0, 0(R1) ; F0 = array element
stall
ADD.D F4, F0, F2 ; add scalar
stall
stall
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
stall
BNE R1, R2, Loop ; branch if R1 != R2
stall
10-cycle
schedule

---
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall
Smart Schedule
Loop: L.D F0, 0(R1)
stall
ADD.D F4, F0, F2
stall
stall
S.D F4, 0(R1)
DADDUI R1, R1,# -8
stall
BNE R1, R2, Loop
stall
Loop: L.D F0, 0(R1)
DADDUI R1, R1,# -8
ADD.D F4, F0, F2
stall
BNE R1, R2, Loop
S.D F4, 8(R1)
By re-ordering instructions, it takes 6 cycles per iteration instead of 10
We were able to violate an anti-dependence easily because an
immediate was involved
Loop overhead (instrs that do book-keeping for the loop): 2
Actual work (the ld, add.d, and s.d): 3 instrs
Can we somehow get execution time to be 3 cycles per iteration?

---
Loop Unrolling
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
L.D F6, -8(R1)
ADD.D F8, F6, F2
S.D F8, -8(R1)
L.D F10,-16(R1)
ADD.D F12, F10, F2
S.D F12, -16(R1)
L.D F14, -24(R1)
ADD.D F16, F14, F2
S.D F16, -24(R1)
DADDUI R1, R1, #-32
BNE R1,R2, Loop
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall
Loop overhead: 2 instrs; Work: 12 instrs
How long will the above schedule take to complete?

---
Scheduled and Unrolled Loop
Loop: L.D F0, 0(R1)
L.D F6, -8(R1)
L.D F10,-16(R1)
L.D F14, -24(R1)
ADD.D F4, F0, F2
ADD.D F8, F6, F2
ADD.D F12, F10, F2
ADD.D F16, F14, F2
S.D F4, 0(R1)
S.D F8, -8(R1)
DADDUI R1, R1, # -32
S.D F12, 16(R1)
BNE R1,R2, Loop
S.D F16, 8(R1)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall
Execution time: 14 cycles or 3.5 cycles per original iteration

---
Loop Unrolling
Increases program size
Requires more registers
To unroll an n-iteration loop by degree k, we will need (n/k)
iterations of the larger loop, followed by (n mod k) iterations
of the original loop

---
Automating Loop Unrolling
Determine the dependences across iterations: in the
example, we knew that loads and stores in different iterations
did not conflict and could be re-ordered
Determine if unrolling will help – possible only if iterations
are independent
Determine address offsets for different loads/stores
Dependency analysis to schedule code without introducing
hazards; eliminate name dependences by using additional
registers

---
Superscalar Pipelines
Integer pipeline FP pipeline
Handles L.D, S.D, ADDUI, BNE Handles ADD.D
What is the schedule with an unroll degree of 4?

---
Superscalar Pipelines
Integer pipeline FP pipeline
Loop: L.D F0,0(R1)
L.D F6,-8(R1)
L.D F10,-16(R1) ADD.D F4,F0,F2
L.D F14,-24(R1) ADD.D F8,F6,F2
L.D F18,-32(R1) ADD.D F12,F10,F2
S.D F4,0(R1) ADD.D F16,F14,F2
S.D F8,-8(R1) ADD.D F20,F18,F2
S.D F12,-16(R1)
DADDUI R1,R1,# -40
S.D F16,16(R1)
BNE R1,R2,Loop
S.D F20,8(R1)
Need unroll by degree 5 to eliminate stalls
The compiler may specify instructions that can be issued as one packet
The compiler may specify a fixed number of instructions in each packet:
Very Large Instruction Word (VLIW)

---
Software Pipeline?!
L.D
ADD.D
S.D
DADDUI
BNE
L.D
ADD.D
S.D
DADDUI
BNE
L.D
ADD.D
S.D
DADDUI
BNE
L.D
ADD.D
S.D
DADDUI
BNE
…
L.D
ADD.D
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
DADDUI
BNE
…
L.D
ADD.D
DADDUI
BNE

---
Software Pipeline
Original iter 1
L.D
ADD.D
S.D
L.D
ADD.D
S.D
Original iter 2
L.D
ADD.D
S.D
Original iter 3
L.D
ADD.D
S.D
Original iter 4
L.D
ADD.D
S.D
New iter 1
L.D
ADD.D
S.D
New iter 2
L.D
ADD.D
New iter 3
L.D
New iter 4

---
Software Pipelining
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Loop: S.D F4, 16(R1)
ADD.D F4, F0, F2
L.D F0, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Advantages: achieves nearly the same effect as loop unrolling, but
without the code expansion – an unrolled loop may have inefficiencies
at the start and end of each iteration, while a sw-pipelined loop is
almost always in steady state – a sw-pipelined loop can also be unrolled
to reduce loop overhead
Disadvantages: does not reduce loop overhead, may require more
registers

---
Predication
A branch within a loop can be problematic to schedule
Control dependences are a problem because of the need
to re-fetch on a mispredict
For short loop bodies, control dependences can be
converted to data dependences by using
predicated/conditional instructions

---
Predicated or Conditional Instructions
if (R1 == 0)
R2 = R2 + R4
else
R6 = R3 + R5
R4 = R2 + R3
R7 = !R1
R2 = R2 + R4 (predicated on R7)
R6 = R3 + R5 (predicated on R1)
R4 = R8 + R3 (predicated on R1)

---
Predicated or Conditional Instructions
The instruction has an additional operand that determines
whether the instr completes or gets converted into a no-op
Example: lwc R1, 0(R2), R3 (load-word-conditional)
will load the word at address (R2) into R1 if R3 is non-zero;
if R3 is zero, the instruction becomes a no-op
Replaces a control dependence with a data dependence
(branches disappear) ; may need register copies for the
condition or for values used by both directions
if (R1 == 0)
R2 = R2 + R4
else
R6 = R3 + R5
R4 = R2 + R3
R7 = !R1 ;
R2 = R2 + R4 (predicated on R7)
R6 = R3 + R5 (predicated on R1)
R4 = R8 + R3 (predicated on R1)

---
Thank you!

---
Complications
Each instruction has one more input operand – more
register ports/bypassing
If the branch condition is not known, the instruction stalls
(remember, these are in-order processors)
Some implementations allow the instruction to continue
without the branch condition and squash/complete later in
the pipeline – wasted work
Increases register pressure, activity on functional units
Does not help if the br-condition takes a while to evaluate

---
Support for Speculation
In general, when we re-order instructions, register renaming
can ensure we do not violate register data dependences
However, we need hardware support
to ensure that an exception is raised at the correct point
to ensure that we do not violate memory dependences
st
br
ld

---
Detecting Exceptions
Some exceptions require that the program be terminated
(memory protection violation), while other exceptions
require execution to resume (page faults)
For a speculative instruction, in the latter case, servicing
the exception only implies potential performance loss
In the former case, you want to defer servicing the
exception until you are sure the instruction is not speculative
Note that a speculative instruction needs a special opcode
to indicate that it is speculative

---
Program-Terminate Exceptions
When a speculative instruction experiences an exception,
instead of servicing it, it writes a special NotAThing value
(NAT) in the destination register
If a non-speculative instruction reads a NAT, it flags the
exception and the program terminates (it may not be
desirable that the error is caused by an array access, but
the segfault happens two procedures later)
Alternatively, an instruction (the sentinel) in the speculative
instruction’s original location checks the register value and
initiates recovery

---
Memory Dependence Detection
 (Advanced Load Address Table)
 In general, when we re-order instructions, register renaming
can ensure we do not violate register data dependences
 However, we need hardware support
to ensure that an exception is raised at the correct point
to ensure that we do not violate memory dependences
st
br
ld

---
Memory Dependence Detection
If a load is moved before a preceding store, we must
ensure that the store writes to a non-conflicting address,
else, the load has to re-execute
When the speculative load issues, it stores its address in
a table (Advanced Load Address Table in the IA-64)
If a store finds its address in the ALAT, it indicates that a
violation occurred for that address
A special instruction (the sentinel) in the load’s original
location checks to see if the address had a violation and
re-executes the load if necessary