## Slide 1: Exposing Congestion Attack on Emerging Connected Vehicle based Traffic Signal Control
Qi Alfred Chen, Yucheng Yin, Yiheng Feng, Z. Morley Mao, Henry X. Liu University of Michigan

## Slide 2: Background: Connected Vehicle technology
CV = Connected Vehicle OBU = On-Board Unit RSU = Road-Side Unit
Wirelessly connect vehicles & infrastructure
Goal: Dramatically improve mobility, safety, environmental impact, & public agency operations
RSU
OBU
CV technology
Mobility
Safety
Environmental
impact
Public agency operations

## Slide 3: Background: Recent advances
CV = Connected Vehicle USDOT = United States Department of Transportation
Will soon transform transportation systems today
2016.9, USDOT launched CV Pilot Program
  National effort to deploy, test, & operationalize CV-based transportation systems
  Launched in 3 sites

## Slide 4: Cybersecurity of CV-based transportation
However, such dramatically increased connectivity also opens a new door for cyber attacks
Highly important to understand potential security vulnerabilities & new security challenges
  Need to ensure security & safety for vehicles, transportation infrastructure, drivers & pedestrians
  Need to perform study now so that they can be proactively addressed before nationwide deployment

## Slide 5: First security analysis of CV-based transp.
Target: Intelligent Traffic Signal System (I-SIG)
  Use real-time CV data for intelligent signal control
  USDOT sponsored design & impl.
  Fully implemented & tested in Anthem, AZ, & Palo Alto, CA
    26.6% reduction in total vehicle delay
  Under deployment in NYC and Tampa, FL
I-SIG
Control
Real-time CV data
RSU
CV = Connected Vehicle OBU = On-Board Unit RSU = Road-Side Unit

## Slide 6: Threat model
Malicious vehicle owners deliberately control the OBU to send spoofed data
  OBU is compromised physically1, wirelessly2, or by malware3
Can only spoof data, e.g., location & speed
  Can’t spoof identity due to USDOT’s vehicle certificate system
I-SIG
Influence signal control
Spoofed CV data
RSU
Malicious vehicle owner
Control
Real-time CV data
2 Checkoway et al.@Usenix Security'11
1 Koscher et al.@IEEE S&P’10
3 Mazloom et al.@Usenix WOOT’16

## Slide 7: Attack goal
Create traffic congestion
  Increase total delay of vehicles in the intersection
    Directly subvert the design goal of I-SIG
  Damage: City functions & individual (wasted fuel, time)
  Incentive: Politically or financially

## Slide 8: Analysis approach overview
Analysis of Attack input data flow
Data spoofing strategies
Traffic snapshots from simulator
Congestion creation vuln.
Congestion creation exploit
Real-time attack requirement (e.g., decision time ≤ 4 sec)
Exploit construction
Dynamic analysis
Spoofing option enum
Increased delay calc
Spoofing w/ top delay inc
Source code

## Slide 9: Analysis result summary
Analysis of Attack input data flow
Data spoofing strategies
Traffic snapshots from simulator
Congestion creation vuln.
Congestion creation exploit
Real-time attack requirement (e.g., decision time ≤ 4 sec)
Exploit construction
Dynamic analysis
Spoofing option enum
Increased delay calc
Spoofing w/ top delay inc
Source code
2 strategies
2 types of vuln.:
#1: Curse of transition period
#2: Last vehicle advantage

## Slide 10: Vuln #1: Curse of transition period
I-SIG has 2 operation modes based on PR:
  PR ≥ 95%, full deployment: Directly run an optimal signal planning algorithm
  PR < 95%, transition: The optimal algorithm becomes ineffective, use an unequipped vehicle estimation algorithm as pre-step
PR ≥ 95%
Unequipped vehicle estimation
Optimal signal planning algorithm
Yes (full deployment period)
No (transition period)
Vulnerable
PR = Penetration Rate

## Slide 11: Vulnerable queue estimation
Find the queue estimation part highly vulnerable
  Data from one single attack vehicle can add a queue with tens of “ghost” vehicles
  Cause delay increased by 20-50%, sometimes even > 70%
Spoof the vehicle location!
Est. queue length = 3
Est. queue length = 7

## Slide 12: An urgent & fundamental problem
An urgent problem for the current design
  Transition period is unavoidable, and long (25-30 yrs est. by USDOT)
  First thing needs to be resolved for its deployment in practice
Fundament cause: Lack a sufficiently robust signal control algorithm for the transition period
  Low PR is inherently more sensitive to data spoofing
    Fundamentally more challenging to ensure robustness
  Need joint research effort in both transportation & security communities
USDOT = United States Department of Transportation PR = Penetration Rate

## Slide 13: Full deployment period is secure?
PR ≥ 95%
Unequipped vehicle estimation
Optimal signal planning algorithm
Yes (full deployment period)
No (transition period)
Vulnerable
PR = Penetration Rate
Vulnerable

## Slide 14: Vuln #2: Last vehicle advantage
Vulnerability: Latest arriving vehicle determines signal plan
Attack: Spoof to arrive as late as possible to increase the delay of queuing vehicles in other directions
Fundamental cause: Security vs deployability trade-off
  Limited decision time forces choice of a sub-optimal config.
  Such sub-optimal config unexpectedly exposes such vuln.
Green light length
Green light length
Green light length
Spoof to arrive as late as possible!
Green light length
More optimal
Delay++

## Slide 15: Attack video demo
Demo time!

## Slide 16: Defense discussion
Robust algorithm design for the transition period
  Inherently challenging, need joint research efforts in both transportation & security communities
Speed-up control algorithm to avoid sub-optimal config.
  E.g., offload computation to a nearby workstation or cloud
Data spoofing detection using infrastructure-controlled sensors, e.g., camera
  Cross check validity of driving data from OBUs
CV = Connected Vehicle OBU = On-Board Unit RSU = Road-Side Unit

## Slide 17: Conclusion
The first security analysis of a CV based transportation system, I-SIG
  Discover new vulnerability & analyze causes
    Current control algorithm design & config. are highly vulnerable
  Construct & evaluate exploits to show the severity in practice
  Propose defense directions based on the analysis insights
Hope to inspire follow-up studies
  E.g., other attack goals, other types of CV systems (60+ open sourced), defense solutions
Reported to USDOT CV Pilot Program office & sites (NYC and Tampa)
CV = Connected Vehicle USDOT = United States Department of Transportation
  https://tinyurl.com/congestion-attack

## Slide 18
Questions?