## Slide 1: QoE Doctor: Diagnosing Mobile App QoE with Automated UI Control & Cross-layer Analysis
Qi Alfred Chen, Haokun Luo, Sanae Rosen, Z. Morley Mao,
Karthik Iyer†, Jie Hui†, Kranthi Sontineni†, Kevin Lau†
University of Michigan, †T-Mobile USA Inc.
*The views presented in this talk are as individuals and do not necessarily reflect any position of T-Mobile.

## Slide 2: Mobile app QoE
Mobile apps are increasingly important for our daily lives

## Slide 3: Mobile app QoE
Mobile apps are increasingly important for our daily lives
Expect
Faster response
Less energy
Less mobile data
Quality of
Experience (QoE)

## Slide 4: Challenges in studying QoE
Measurement methodology
  Relying on user study
    Costly, hard to control behavior variations
  Instrumenting the source code or binary
    Hard to automate testing
    Not applicable to popular apps like Facebook
Result analysis
  Complicated by multi-layer dynamics & inter-dependencies in system & network stacks

## Slide 5: Our solution: QoE Doctor
Support more accurate, systematic, and repeatable QoE measurements & analysis
Introduce UI automation into QoE measurement
  Automatically replay user behavior
  Accurately measure UI layer QoE metrics
  No need to modify app source code or the system

## Slide 6: Our solution: QoE Doctor
Result analysis
  Support multi-layer diagnosis of QoE problems
    Collect data across application, transport, network, and cellular radio link layers
    Enable cross-layer analysis

## Slide 7: Related work
QoE
Test automation
Popular apps
Cross-layer analysis
Monkey, PUMA, AMC, etc.
Joumblatt, et al. Infocom’13, etc.
AppInsight, Timecard, SIF, etc.
Prometheus
QoE Doctor
✗
✗
✓
✓
✗
✗
✗
✓
✓
✓
✓
✓
✓
✓
✗
✗
✗
✓
✓
✓

## Slide 8: QoE metrics in focus
In this work, we focus on measuring
  User-perceived latency
  Mobile data consumption
  Mobile energy consumption
    Network energy

## Slide 9: Design overview
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
Application layer
analyzer
Transport/network layer analyzer
RRC/RLC layer
analyzer
QoE-aware UI controller
Multi-layer QoE analyzer
Cross-layer
analyzer
Cross-layer
analyzer

## Slide 10: Design overview
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
Application layer
analyzer
Transport/network layer analyzer
RRC/RLC layer
analyzer
QoE-aware UI controller
Multi-layer QoE analyzer
Cross-layer
analyzer
Cross-layer
analyzer
UI
controller

## Slide 11: UI controller
Use Android built-in UI testing APIs
  Send UI events to the app
  Designed for developer self-testing
    Can be used to test any apps after re-signing the apk
  Powerful in QoE study
    Share app data, can directly access UI tree in real time
      Important for user-perceived latency measurement
  We are the first to use this UI automation technique for mobile app QoE measurement

## Slide 12: UI controller
UI control paradigm:
See
Inter-act
Wait
A unique feature due to user-perceived latency measurement:
Wait until the right UI events instead of using a heuristic timer
latency

## Slide 13: Design overview
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
Application layer
analyzer
Transport/network layer analyzer
RRC/RLC layer
analyzer
QoE-aware UI controller
Multi-layer QoE analyzer
Cross-layer
analyzer
Cross-layer
analyzer
App-specific QoE-related
behavior
control
UI
controller

## Slide 14: User behavior replay
Replay using UI control:
  Facebook:
    Post status/check-in/photos
    Pull-to-update
  YouTube:
    Watch videos
  Web browsers
  (Chrome, Firefox, …)
    Load web pages
Measure
Upload latency
Update latency
Initial loading time
Rebuffering ratio
Page loading time

## Slide 15: Design overview
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
Application layer
analyzer
Transport/network layer analyzer
RRC/RLC layer
analyzer
QoE-aware UI controller
Multi-layer QoE analyzer
Cross-layer
analyzer
Cross-layer
analyzer
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
Application layer
analyzer
Transport/network layer analyzer
RRC/RLC layer
analyzer
Wait
TCPDUMP
QxDM
User-perceived latency
Mobile data consumption
Mobile energy consumption

## Slide 16: Design overview
Network logger
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
Application layer
analyzer
Transport/network layer analyzer
RRC/RLC layer
analyzer
QoE-aware UI controller
Multi-layer QoE analyzer
Cross-layer
analyzer
Cross-layer
analyzer
Cross-layer
analyzer
Cross-layer
analyzer
Help diagnose root cause of QoE problems

## Slide 17: Cross-layer analyzer
Application
layer
Network layer
Cellular radio
link layer
Transport layer
TCP flow
IP packet
IP packet
IP packet
…
PDU
PDU
PDU
PDU
PDU
…
PDU
PDU
User-perceived latency

## Slide 18: Experiments: study app QoE
Quantify factors that may impact QoE of popular apps
Various factors we studied:
  Network type and quality
  Design & configuration in apps
  Design & implementation on carrier side

## Slide 19: YouTube: carrier throttling impact
A carrier policy: traffic throttled after exceeding the data limit
  How much does it affect QoE?
Compare throttled vs. unthrottled for YouTube videos
  Throttle to ~120 kbps in 3G & LTE by the carrier
  100 random YouTube videos (total length ~ 35 hrs)
    Diverse in both the video length (1 min to 0.5 hr) and video popularity (1000 – 10 billion views)

## Slide 20: YouTube: carrier throttling impact
Throttling causes > 30 sec (15×) more initial loading time and increases the rebuffering ratio from ~ 0% to 50% on average.

## Slide 21: YouTube: carrier throttling impact
Better initial loading time and rebuffering ratio in 3G than in LTE under throttling. Why?

## Slide 22: YouTube: carrier throttling impact
Locally control bandwidth
  repeat the bandwidth limits of 100, 200, 300, 400, and 500 kbps
From cross-layer analyzer, in LTE around 96.6% (40 MB) more data is downloaded than in 3G for ~90 s videos!
Default video resolution is HQ for 3G and HD for LTE
Should not adapt video quality simply based on network type!
Fixed!
Application layer
analyzer
Transport/network layer analyzer
Cross-layer
analyzer
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
RRC/RLC layer
analyzer
Cross-layer
analyzer
Application layer
analyzer
Transport/network layer analyzer
Cross-layer
analyzer
QoE-aware UI controller
Multi-layer QoE analyzer

## Slide 23: Facebook: post upload time breakdown
Measure device and network latency when posting a status, a check-in, and 2 photos
Sometimes no network latency, why?
[Finding]: network
delay not always
on the critical path!

## Slide 24: Facebook: post upload time breakdown
Measure device and network latency when posting a status, a check-in, and 2 photos
Big difference in network latency between 3G and LTE, why?
Let’s further
breakdown !
Application layer
analyzer
Transport/network layer analyzer
Cross-layer
analyzer
UI
controller
App-specific QoE-related
behavior
control
QoE-related UI logger
Network logger
RRC/RLC logger
RRC/RLC layer
analyzer
Cross-layer
analyzer
Transport/network layer analyzer
QoE-aware UI controller
Multi-layer QoE analyzer
RRC/RLC layer
analyzer
Cross-layer
analyzer

## Slide 25: Facebook: post upload time breakdown
Measure device and network latency when posting a status, a check-in, and 2 photos
[Finding]: Much
longer transmission
delay in 3G,
likely caused by
smaller transmitting
segments in 3G.

## Slide 26: Other results
App design & configuration impact
  Changing one Facebook default configuration can reduce ≥ 20% of data & energy consumption
  Compared to WebView, ListView version Facebook reduces ≥ 67% device latency, ≥ 30% network latency, ≥ 77% downlink data consumption
  YouTube ads reduce the initial loading time of the main video, but doubling the total loading on cellular networks.
Carrier side design
  Simplifying the 3G RRC state machine can reduce web page loading time by 22% for web browsing

## Slide 27: Summary
QoE Doctor for systematic mobile app QoE measurement
  Automated replay of QoE-related user behavior
  Accurate measurement of QoE metric at UI layer
  Multi-layer diagnosis of QoE problems
  Applicable to popular apps
Systematically quantify various factors that impact QoE of popular apps

## Slide 28
Questions?